## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
TECHNICAL STAFFS
Module 4.2:
Current and potential of EE in Cement industry in Vietnam

## Slide 2: Content
Current of industrial energy use in Vietnam
Current and potential of EE in Cement industry in Vietnam

## Slide 3
Current of industrial energy use in Vietnam

## Slide 4: Small group discuss and presentation
Devided the class into 4 group
Discuss in 15 mins
What sector do you think using the highest energy in Vietnam?
Identify the designated energy users in the cement industry?
What energy source your company mainly use?
What potential of EE in your company
Presentation in 5 mins

## Slide 5: 1. FINAL ENERGY CONSUMPTION BY INDUSTRY IN VIETNAM
Chart: 2022
| Industry | Agriculture | Transport | Service | Household | Non-energy
 | 0.519 | 0.05 | 0.208 | 0.037 | 0.139 | 0.047
Chart: 2023
| Industry | Agriculture | Transport | Service | Household | Non-energy
 | 0.523 | 0.05 | 0.206 | 0.037 | 0.135 | 0.048

## Slide 6: 2. CHARACTERISTICS OF ENERGY CONSUMPTION IN VIETNAM’S INDUSTRY
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption.
As of 2023, Vietnam has 3,491 designated energy users (DEUs) with a total energy consumption of approximately 40,586,299 TOE. Among them, the industrial sector accounts for the majority, with 2,864 establishments consuming around 39,583,611 TOE (97.5% of the total DEUs). This demonstrates a significant potential for energy efficiency improvement in Vietnam’s industrial sector.
Although the cement industry in Vietnam has only 91 DEUs, it consumes up to 8,825,788 TOE, accounting for 21.7% of total DEU energy consumption and 22.3% of industrial DEU consumption—due to the energy-intensive nature of its production equipment.
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 7: 3. NUMBER OF DESIGNATED ENERGY USERS (DEUS)
Number of DEU and corresponding energy consumption, 2017-2023 (Source: Compiled from the DEUs List)
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2023
Energy using of DEUs (kTOE) | 24126 | 26750 | 35997 | 34294 | 51394 | 40586
Number of DEUs | 2496 | 2605 | 3006 | 2961 | 3068 | 3491

## Slide 8: 4. EE TARGETS FOR VIETNAM'S INDUSTRIAL SECTORS BY 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 9: 5. AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 10: 6. ENERGY EFICIENCY POTENTIAL OF SOME TYPICAL INDUSTRIES
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report
Sector | Product | Savings potential (%)
Drinks | Beer | 9–12
 | Non-alcoholic beverages | 4–9
Plastic | Consumer plastic | 9–13
 | Construction plastic | 5–14
 | Packaging | 4–12
 | Plastic bottle | 5–14.5
 | Plastic bag | 11–17
Paper | Pulp | 6.8
 | Packaging | 3.8
 | Printing paper | 4.4
 | Toilet paper | 3.8
Chemistry | Rubber SVR 10CV, 20CV | 9.4–32.7
 | Rubber SSVR 10, 20 | 9.8–32.7
 | Fertilizer | 1.4–5.4
 | Water-based paint | 20–30
Heavy industrial products | Finished steel | 13
 | Cement | 14
 | Textile yarn | 14

## Slide 11: 7. CURRENT STATUS OF ENERGY USE IN INDUSTRY
Proportion of energy consumption: The industrial sector accounts for about 52.4% of the total energy consumption in the country (data 2023)
Industries with high energy consumption:
  The steel production, cement, textiles, wood processing, plastic, chemicals, paper production, food processing,…
  The cement sector accounted for 10 to 15 percent of total energy consumption in industries
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.
Notes: https://csis-website-prod.s3.amazonaws.com/s3fs-public/Son_Energy_Vietnam_Background_V1.pdf?

## Slide 12: 7. CURRENT STATUS OF ENERGY USE IN INDUSTRY
Specific energy consumption (SEC) is measured in kWh per ton of product or GJ per ton of product and reflects the energy efficiency in each manufacturing sector.
Cement Production Sector:
Electricity consumption: Approximately 80–100 kWh per ton of cement.
Thermal energy consumption: Approximately 3–4 Gcal per ton of clinker.
Characteristics: The cement industry is a highly energy-intensive sector, especially in the clinker burning process. The use of dry rotary kiln technology and vertical grinding mills helps reduce energy consumption.
Notes: https://csis-website-prod.s3.amazonaws.com/s3fs-public/Son_Energy_Vietnam_Background_V1.pdf?

## Slide 13: 8. CAUSES OF HIGH ENERGY CONSUMPTION
Outdated technology: Many cement enterprises still use old technologies, especially in the clinker burning process, waste heat recovery, and low levels of automation.
Lack of investment in innovation: There is a shortage of capital and motivation to invest in energy-saving equipment and technologies.
Low awareness of EE: Some enterprises have not prioritized energy-saving solutions in their production processes.
Cost challenges: The high initial investment cost of energy-efficient technologies discourages many enterprises from making changes.
Insufficient policy support: Although there are incentive policies in place, they remain ineffective in strongly encouraging widespread adoption of energy-saving solutions by enterprises.

## Slide 14: 9. TRENDS IN SUSTAINABLE DEVELOPMENT IN CEMENT INDUSTRY
1. Enhance the use of alternative fuels:
Utilize industrial solid waste, municipal waste, rice husks, sawdust, RDF (Refuse-Derived Fuel), etc.
Reduce dependence on coal – thereby lowering CO₂ emissions.
2. Use of alternative materials to clinker:
Incorporate fly ash, ground granulated blast furnace slag, finely ground limestone, and natural pozzolana.
Reduce the clinker content in cement (Clinker ratio indicator).
3. Optimize Production Technology:
Adopt advanced rotary kilns and automated analysis systems.
Optimize waste heat recovery, and reduce thermal and electrical energy consumption.
4. Digital transformation and energy monitoring:
Implement ISO 50001 energy management systems.
Apply AI and IoT to monitor equipment operations.
5. Implement carbon credits and GHG inventory:
Aim toward carbon neutrality.
Actively participate in domestic and international carbon credit markets.
6. Comply with national and international policies:
Follow Decree 06/2022/NĐ-CP, Decision 2600/QĐ-BCT, etc.
Commit to GHG emission reduction under NDC and Net Zero 2050 goals.

## Slide 15
II. Current and potential of EE in Cement industry in Vietnam

## Slide 16: 1. OVERVIEW OF CEMENT INDUSTRY
90+
Production line
Number of rotary kiln cement production lines currently available in Vietnam
120 million
Tons of products
Cement and clinker output in 2023
30-35 million
Export tons
Annual cement export volume
6-7%
Industrial energy
Share of energy consumption of cement industry in total industrial energy
Vietnam’s cement industry has grown strongly in recent years, becoming one of the world’s leading cement producers and exporters. With more than 90 production lines, the industry contributes significantly to the national economy, but also poses many challenges in terms of efficient energy use.
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 17: 2. ENERGY INTENSITY IN HIGH-ENERGY INDUSTRIES IN VIETNAM
Figure: Energy Intensity Improvement in Key Industries during VNEEP Phase 2 Changes of energy intensity in key industries
Energy Intensity of Key Industrial Sectors in Vietnam (2015–2022)
Year
Cement
Steel
Chemicals
Paper
Food
Energy Intensity (TOE/Billion VND GDP)

## Slide 18: 3. THE AVERAGE THERMAL ENERGY INTENSITY OF CLINKER
Global thermal energy intensity of clinker production by fuel in the Net Zero Scenario, 2010-2030
Fossil fuels continued to be the main source of thermal energy for the sector (90% share) in 2022, followed by bioenergy and renewable waste (4%) and non-renewable waste (4%). The adoption of low carbon fuels is key to reduce the share of fossil fuels to 79% and non-renewable waste to 3% by 2030 in line with the NZE Scenario, which sees bioenergy and renewable waste increasing to 16% and hydrogen to 2% of the total thermal energy share.

## Slide 19: 4. ENERGY USE STRUCTURE
The energy use structure in Vietnam's cement industry currently still depends mainly on coal, accounting for 80-85% of total energy consumption. Electricity comes in second with about 15-20%, mainly serving the grinding and transportation stages.
Nhiên liệu thay thế như rác thải, sinh khối và chất thải nguy hại mới chỉ chiếm dưới 5% tổng năng lượng sử dụng, nhưng đang có xu hướng tăng dần khi các nhà máy bắt đầu áp dụng các giải pháp thân thiện với môi trường hơn.
Coal (antraxit)
80-85% of total energy
Mainly used for clinker kiln
Electricity
15-20% of total energy
Used for grinding raw materials, grinding cement, packaging, transporting
Alternative fuel
Under 5% (increasing)
Including waste, biomass, hazardous waste

## Slide 20: 5. PERFORMANCE AND ENERGY INTENSITY
Index
Current level
Good level
Coal consumption for clinker production
730-850 kcal/kg clinker
<730 kcal/kg
Average electricity consumption
95-110 kWh/ton of cement
<85 kWh/ton
Furnace efficiency
Change with technology
High with precalciner
rotary kiln
Energy efficiency in Vietnam’s cement industry is still far from world standards. Coal consumption for clinker production ranges from 730-850 kcal/kg, while the optimal level should be below 730 kcal/kg. Similarly, average electricity consumption varies widely between plants..
Kiln efficiency depends largely on the technology used, with modern rotary kilns (precalciners) being more efficient, while many older lines still need to be upgraded to improve energy efficiency.

## Slide 21: 6. ENERGY CONSUMPTION IN THE CEMENT INDUSTRY (1)
The Vietnamese cement industry consumes a significant amount of energy, primarily in the form of thermal energy and electricity.
The energy consumption structure for cement production is as follows: approximately 80-85% is thermal energy, 15-20% is electricity, and a small portion (around 1%) is from DO (diesel oil) and FO (fuel oil).
It is estimated that electricity costs account for 10-15% of the cement production cost.
Electricity consumption ranges from 95 kWh to 108 kWh per ton of cement produced. This variation depends on the technology and equipment used in the plants.

## Slide 22: 6. ENERGY CONSUMPTION IN THE CEMENT INDUSTRY (2)
High energy consumption
Energy consumption is still 10-20% higher than world standards, causing waste and increasing production costs.
Outdated technology
Many kiln lines are old and have not been invested in for improvement, leading to low efficiency and high fuel consumption.
Low heat recovery
The rate of waste heat recovery for power generation is not yet thorough, only about 20 factories have WHR systems out of a total of 90 production lines.
Inefficient energy management
Many small and medium enterprises have not yet applied modern and effective energy management systems.
Vietnam’s cement industry faces many challenges in energy efficiency. Energy consumption remains higher than world standards, many kiln lines are old and have not been upgraded. The application of alternative fuels is limited due to environmental regulations and high investment costs.

## Slide 23: 7. POTENTIAL AREAS FOR ENERGY EFFICIENCY
1. Clinker Kiln Energy eficiency potential: 5–15% of thermal energy Measures:
Optimize the ratio of alternative fuels (RDF, biomass, waste tires, etc.).
Improve insulation to reduce heat loss through the kiln shell.
Optimize feed and combustion control (advanced process control – APC).
Use high-efficiency burners and new designs for the cooler zone.
2. Preheater Tower & Calciner Energy eficiency potential: 3–10% Measures:
Optimize gas-material flow in the cyclone tower to enhance heat exchange efficiency.
Reduce leakage pressure and ensure effective control of CaCO₃ decomposition (decarbonation).

## Slide 24: 7. POTENTIAL AREAS FOR ENERGY EFFICIENCY
3. Grinding system (raw materials, cement grinding) Energy eficiency potential: 5–20% of electricity consumption Measures:
Replace or upgrade ball mills with vertical roller mills (VRM).
Improve classification balls and optimize grinding media in ball mills.
Use variable frequency drives (VFDs) for main motors and fan systems.
Monitor grinding efficiency and material flow automatically.
4. Process fan system Energy eficiency potential: 10–30% of fan electricity consumption Measures:
Optimize ducting to reduce pressure loss.
Install VFDs for fans, especially primary air fans, dust collection fans, and clinker cooler fans.
Select high-efficiency fans and adjust blades appropriately.

## Slide 25: 7. POTENTIAL AREAS FOR ENERGY EFFICIENCY
5. Waste Heat Recovery (WHR) System Energy eficiency potential: 20–30 kWh electricity per ton of clinker produced Measures:
Install systems to recover waste heat from the clinker cooler and preheater to run a power generation turbine.
Suitable for plants producing ≥2,500 tons of clinker per day.

## Slide 26: 8. EEMs IN THE CEMENT INDUSTRY (1)
Waste heat recovery (WHR)
High potential with recovery of 5-7 kWh/ton of clinker, significantly reducing electricity consumption from the grid.
Optimizing grinding equipment
Upgrading the motor, vertical mill, inverter helps reduce power consumption during the grinding process.
Process Automation
Applying an automatic control system and optimizing the firing process helps reduce fuel consumption.
Use alternative fuels
Increase the use of industrial waste, biomass, RDF to partially replace coal.

## Slide 27: 8. EEMs IN THE CEMENT INDUSTRY (2)
Optimize the Clinker Production Process:
Use high-efficiency kilns (pre-calciner).
Reduce heat loss by improving insulation.
Optimize kiln operation using simulation software.
Waste Heat Recovery for Power Generation (WHR)
Recover waste heat from the kiln and clinker cooler.
Apply advanced technologies such as the ORC system (Organic Rankine Cycle).
Benefits: Save 20-30% of electricity consumption, reduce emissions

## Slide 28: 8. EEMs IN THE CEMENT INDUSTRY (3)
Use alternative fuels
Fuel type | Source | Benefit | Replacement rate
RDF | Treated municipal waste | Reduce coal consumption, reduce CO₂ emissions | 5–15%
Biomass | Agricultural by-products | Net zero emissions, renewable | 10–15%
Scrap Tires | Expired tires | High calorific value, reduced waste | 3–8%
Sludge treatment | Wastewater treatment plant | Utilize waste, reduce treatment costs | 2–5%

## Slide 29: 8. EEMs IN THE CEMENT INDUSTRY (4)
Use of Alternative Fuels
Biomass fuels: Wood pellets, straw, rice husks.
Co-processing of waste: Tires, household waste.
Benefits: Reduce costs and CO₂ emissions.
Grinding Technology Improvement
Use vertical mills instead of ball mills.
Install variable frequency drives (VFDs) to reduce electricity consumption.
Benefits: Save 20-30% of electricity consumption.
Effective Equipment Management and Maintenance
Regular maintenance to maintain equipment performance.
Install an energy consumption monitoring system.
Benefits: Reduce energy waste.

## Slide 30: 8. EEMs IN THE CEMENT INDUSTRY (5)
KILN TECHNOLOGY SOLUTIONS
Optimize the firing process
Adjust operating parameters to achieve optimum thermal efficiency, reduce energy consumption and maintain product quality.
Remodeling of the combustion chamber and burner
Upgraded combustion chamber and injector design to increase combustion efficiency, reduce fuel consumption and emissions.
Increase fuel replacement rate
Use RDF (recycled fuel from waste) and biomass to partially replace traditional coal.
Technological solutions for the clinker kiln can bring energy efficiency of 5-10%. This is the largest energy consuming area in a cement plant, so small improvements can bring significant efficiency.

## Slide 31: 8. EEMs IN THE CEMENT INDUSTRY (6)
UPGRADE AUXILIARY EQUIPMENT
Upgrading auxiliary equipment such as fans, pumps, pneumatic systems and lighting can help save 10-15% of the power consumption of these systems. In particular, installing VSD inverters for large motors brings significant efficiency in a short time.
Industrial fan
Replace with high efficiency model, install VSD inverter to adjust speed according to actual demand
Pumping system
Upgrade engines and install intelligent control systems to optimize operations
Pneumatic system
Leakage control and operating pressure optimization to reduce power consumption
Lighting system
Convert to LED lights and install sensors that automatically adjust to your needs

## Slide 32: 8. EEMs IN THE CEMENT INDUSTRY (7)
MANAGEMENT AND OPERATION SOLUTIONS
Apply ISO 50001
Implementing an energy management system according to international standard ISO 50001 helps save 5-10% energy through establishing a continuous monitoring and improvement process.
Optimize production shift
Arranging production schedules reasonably, avoiding operating low-power equipment and taking advantage of off-peak electricity hours can save 3-5% of energy.
Energy Audit
Conducting regular energy audits helps identify specific savings opportunities and evaluate the effectiveness of implemented measures.
Bim Son Cement is a typical example of successful application of ISO 50001 energy management system, combined with online energy monitoring system to monitor and optimize energy consumption in real time.

## Slide 33: 9. EXAMPLE OF EEMS IN THE WORLD (1)
Chemical absorption, partial capture rates (less than 20%)
Technology description
Chemical absorption of CO2 is a common process operation based on the reaction between CO2 and a chemical solvent (e.g. amine-based). The CO2 is released at temperatures typically in the range 120 °C to 150 °C and the solvent is regenerated for further operation. It can be applied to kilns, the main unit producing clinker for cement production.
Relevance for net zero
CO2 capture and storage is a key technology to reduce otherwise difficult to avoid process emissions from cement production. Most alternative CCS technologies are more costly and/or at earlier stages of development, while other lower emission alternatives for producing cement, such as alternative binding materials, face challenges such as low TRL or limitations in raw material availability. However, higher capture rates should be targeted.

## Slide 34: 9. EXAMPLE OF EEMS IN THE WORLD (2)
1. Norcem Brevik (Heidelberg Materials) – Norway
The world’s first cement plant implementing a commercial-scale CCS project using MEA (Monoethanolamine) to absorb CO₂.
Expected to start operation by late 2024–2025.
Capture capacity: approximately 400,000 tons of CO₂/year (about 50% of total emissions).
Solvent: amine-based, regenerable at ~120–140°C.
2. Lehigh Hanson (part of Heidelberg) – Edmonton, Canada
Developing a commercial-scale CO₂ capture project (~1 million tons/year).
Planned to use a chemical absorption system similar to Norcem.
Financially supported by the Canadian and federal governments.
3. Cemex – Germany and Mexico
Cemex is piloting amine-based CO₂ capture technology at several plants.
Some trials are part of the CLEANKER program or EU–Horizon 2020 collaboration.
Also integrating with waste heat recovery technology from kiln exhaust gases.

## Slide 35
Demonstration projects
Germany: Heidelberg Linde CCS: In April 2023, Heidelberg Materials partnered with engineering company Linde to install a 70 kt carbon capture system at its 1Mt/yr Lengfurt cement plant by 2025.
Spain: ECCO2 LafargeHolcim Carboneras cement factory: LafargeHolcim España, Carbon Clean and Sistemas de Calor have created ECCO2, a joint venture for the development of an advanced technology CO2 capture plant at the Carboneras cement factory (Almeria). The three companies have been working on the project since the end of 2020, in order to assess its technical feasibility and benefits for the local community. The plant is expected to be operational in early 2023. (Source)
United States: Capitol Aggregates: Commercial-scale post-combustion carbon capture and utilisation (CCU) facility opened in 2014 at Capitol Aggregates plant in Texas, capturing 15% of cement production emissions (75 kt CO2/yr) for use in materials such as baking soda, bleach and hydrochloric acid.
Source: https://www.osti.gov/servlets/purl/1241314
9. EXAMPLE OF EEMS IN THE WORLD (3)

## Slide 36: 10. PIONEERING ENTERPRISES IN VIETNAM
Vicem Hoang Thach
Successfully implemented waste heat recovery (WHR) system and used RDF alternative fuel, significantly reducing energy costs and CO₂ emissions.
Bim Son Cement
Apply ISO 50001 energy management system and connect online energy monitoring system, allowing real-time monitoring and optimization of energy consumption.
Fico Cement
Testing burning biomass instead of coal, aiming to reduce carbon emissions and take advantage of locally available renewable fuel sources.

## Slide 37: Question: What energy efficiency potential do you see that is most relevant to your plant? Explain?
DISCUSSION

## Slide 38
THANK YOU