## Slide 1
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 9.2:
Case studies on efficient energy measures in the cement industry
TECHNICAL STAFFS

## Slide 2
CEMENT INDUSTRY

## Slide 3: DISCUSSION
Please share the Energy efficiency measures that you impliment in your work?
Please provide more details such as: Situation, Solution, Implimentation and Results

## Slide 4: CONTENT
Waste heat recovery for power Generation (WHR – Waste Heat Recovery)
Retrofit of ID/PA/SA fan systems with Variable Speed Drives
Optimization of clinker kiln operation
Use of alternative fuels in cement production
Optimization of grinding systems in cement production
Enhancing Insulation and heat recovery in clinker coolers

## Slide 5: 1. Waste heat recovery for power generation (WHR)
Case Study: INSEE Cement Hòn Chông

## Slide 6
1. WASTE HEAT RECOVERY FOR POWER GENERATION (WHR)
1.1 Implementation context
INSEE Hòn Chông: A modern cement plant located in Kiên Giang.
High electricity consumption (~90–100 kWh/ton of cement).
Significant potential from kiln and cooler exhaust gases.
1.2 Description of the WHR system
Heat sources: Exhaust gases from the preheater and clinker cooler.
Equipment: Heat recovery boilers, steam turbines, ORC system.
Total power generation capacity: ~6.3 MW.
1.3 Achieved results
Electricity generation: ~44 million kWh/year (~20–25% of internal demand).
Electricity cost savings: ~VND 22 billion/year.
CO₂ emissions reduction: ~25,000 tons/year.
Payback period: ~4–5 years.

## Slide 7
1. WASTE HEAT RECOVERY FOR POWER GENERATION (WHR)
1.4. Challenges and considerations for implementation
High capital investment (~USD 10–12 million).
Requires thorough assessment of exhaust gas flow and temperature.
Demands synchronized equipment maintenance.
1.5. General remarks WHR at INSEE Hòn Chông is an effective model. It contributes to energy eficiencys and emissions reduction. Suitable for plants producing ≥ 5,000 tons of clinker/day.

## Slide 8: 2. Retrofit of ID/PA/SA fan systems with Variable Speed Drives
Case studies from Bỉm Sơn Cement, Vicem Hoàng Thạch, Hà Tiên 1

## Slide 9
2. RETROFIT OF ID/PA/SA FAN SYSTEMS WITH VARIABLE SPEED DRIVES
2.1. Background and rationale
ID (Induced Draft), PA (Primary Air), and SA (Secondary Air) fans operate continuously.
Account for ~30–40% of the plant’s total electricity consumption.
Previously operated with mechanical dampers/IGVs, leading to significant energy loss.
2.2. Technical solution description
Replacing old motors with high-efficiency motors (IE2/IE3).
Installing Variable Speed Drives (VSDs) for flexible speed control.
Integrating control with DCS/SCADA systems.
2.3. Achieved results – Bỉm Sơn cement
Retrofit of 6 ID/PA/SA fans.
Savings of ~1.2 million kWh/year.
CO₂ emissions reduction of ~960 tons/year.
Payback period ~2.5 years.

## Slide 10
2. RETROFIT OF ID/PA/SA FAN SYSTEMS WITH VARIABLE SPEED DRIVES
2.4. Achieved results – Hoàng Thạch & Hà Tiên 1
Vicem Hoàng Thạch: Saved 20–25%, improved reliability.
Hà Tiên 1: Power demand reduced from 150 kW to 110–120 kW per fan.
Improved excess O₂ optimization and combustion chamber stability.
2.5. Overall benefits
Electricity savings: 10–25%.
Cost reduction: VND 600 million – 1.5 billion/year.
CO₂ emissions reduction: 500–1000 tons/year.
Reduced equipment wear and increased control accuracy.
2.6. Additional notes
Applicable to: raw mill fans, clinker coolers, dust removal systems.
Considerations: control system compatibility, harmonic distortion, motor protection.

## Slide 11: 3. Optimization of clinker kiln operation
Applications: Hà Tiên 1 Cement, Nghi Sơn Cement, Fico Tây Ninh...

## Slide 12
3. OPTIMIZATION OF CLINKER KILN OPERATION
3.1. Background and rationale
The clinker kiln is the highest thermal energy consumer in a cement plant.
Fuel costs account for 40–60% of total clinker production costs.
Suboptimal operation leads to heat waste and increased CO₂ emissions.
3.2. Technical solution description
Adjust raw material mix to ensure optimal mineral composition.
Optimize combustion process: control flame shape and air supply.
Continuously monitor temperature, oxygen, and emissions using online sensors.
3.3. Achieved results
Hà Tiên 1 Cement: Reduced heat consumption by ~40 kcal/kg clinker.
Nghi Sơn Cement: Increased kiln efficiency from 88% to 91%.
Fico Tây Ninh: Reduced heat losses at the kiln inlet and outlet.
Notes
Most effective when combined with raw material control, combustion chamber upgrades, and digital technology application.
Requires operator training in data analysis and real-time process adjustment based on technical parameters.

## Slide 13: 4. Use of alternative fuels in cement production
Applications: INSEE Cement, Cẩm Phả Cement, Vicem Hoàng Mai..

## Slide 14
4.1. Background and rationale
Traditional fuel costs (coal, FO) are increasing.
Higher pressure to reduce CO₂ emissions and manage solid waste.
Cement kilns are suitable for co-processing and energy recovery.
4.2. Technical solution description
Alternative fuels include: RDF, rice husk, sawdust, biomass, treated sludge.
Specialized systems for grinding, drying, and feeding into kiln combustion chambers.
Fuel composition and blending ratio are controlled to ensure stable operation.
4.3. Achieved results
INSEE: Replaced up to 40% of total thermal energy with RDF and biomass.
Cẩm Phả Cement: Reduced coal consumption by 15–20%.
Vicem Hoàng Mai: Increased use of rice husk and sawdust to 25%.
Note: RDF (Refuse-Derived Fuel) refers to fuel derived from solid waste.
4. USE OF ALTERNATIVE FUELS IN CEMENT PRODUCTION

## Slide 15
4.4. Economic and environmental benefits
Fuel cost savings: 10–30% depending on plant and fuel source.
CO₂ emissions reduction: ~0.9–1.2 tons CO₂ per ton of coal replaced.
Reduced dependence on fossil fuels, enhanced sustainability.
Less pressure on landfilling of industrial and municipal waste.
4.5. Implementation considerations
RDF quality must be controlled (calorific value, moisture, heavy metals).
Investment in enclosed, safe feeding systems with dust/toxic gas control.
Best suited for modern rotary kilns with high temperature and continuous operation.
4. USE OF ALTERNATIVE FUELS IN CEMENT PRODUCTION

## Slide 16: 5. Optimization of grinding systems in cement production
Applications: Vicem Hoàng Thạch, Long Sơn Cement

## Slide 17
5. OPTIMIZATION OF GRINDING SYSTEMS IN CEMENT PRODUCTION
5.1. Background and rationale
Grinding systems (coal, raw materials, cement) are the highest electricity consumers in cement plants (~40–50%).
Many systems use outdated, inefficient equipment with low automation levels.
There is a need to improve efficiency, reduce electricity consumption, and optimize product quality.
5.2. Technical solution description
Replace ball mills with high-efficiency Vertical Roller Mills (VRM).
Install Variable Speed Drives (VSD) on grinding motors, exhaust fans, and material conveyors.
Optimize operation: control fineness, temperature, material recirculation, and airflow.
5.3. Achieved results
Vicem Hoàng Thạch: Saved 7–10 kWh/ton of cement after retrofitting the cement grinding system.
Long Sơn Cement: Improved clinker fineness and uniformity.
Reduced vibration incidents, decreased wear on grinding media and liners.

## Slide 18
5. OPTIMIZATION OF GRINDING SYSTEMS IN CEMENT PRODUCTION
5.4. Overall benefits
Reduced grinding system electricity consumption by 5–15%.
Increased grinding system stability and productivity.
Extended service life of mechanical equipment and motors.
Enhanced product quality (fineness, particle size distribution).
5.5. Implementation notes
Analyze recirculated materials and airflow velocity for optimal performance.
Prioritize integration of online fineness sensors and SCADA systems.
Can be combined with energy audits to identify specific savings potential.

## Slide 19: 6. Enhancing insulation and heat recovery in clinker coolers
Energy eficiency measure applicable in most cement plants

## Slide 20
6. ENHANCING INSULATION AND HEAT RECOVERY IN CLINKER COOLERS
6.1. Background and rationale
Clinker coolers release large amounts of heat, often lost to the environment.
Equipment shells, conveyors, storage silos, etc., can suffer major heat losses due to poor insulation.
Waste heat from the cooler can be recovered for raw material drying or power generation.
6.2. Technical solution description
Add or upgrade high-quality insulation materials on equipment shells.
Reinforce gaps and thermal contact points to reduce heat leakage.
Recover exhaust heat via heat collection pipes or heat exchangers to:
  Dry raw materials or coal.
  Serve as input heat for the kiln.
6.3. Achieved results
Reduced surface heat losses by 10–15%.
Utilized 300–400°C exhaust heat for drying or power generation.
Lowered kiln heat consumption by 5–20 kcal/kg clinker depending on integration setup.

## Slide 21
6. ENHANCING INSULATION AND HEAT RECOVERY IN CLINKER COOLERS
6.4. Overall benefits
Significant fuel cost savings for material drying.
CO₂ emissions reduction through decreased coal or FO consumption.
Extended equipment life and reduced thermal shock risks.
Improved operational safety and workplace environment.
6.5. Technical notes
Use insulation materials with low thermal conductivity and high abrasion resistance.
Install temperature sensors to monitor losses over time.
Most effective when combined with WHR systems or internal heat reuse.

## Slide 22: DISCUSSION
Based on the six case studies presented (WHR, fan system retrofit with VSDs, clinker kiln optimization, alternative fuels, grinding system optimization, insulation and heat recovery in clinker coolers,…), which energy efficiency measures (EEMs) do you think could be most applicable and beneficial for your company’s operations?
Consider factors such as investment cost, payback period, technical feasibility, plant capacity, and potential energy/environmental benefits.
Be ready to share examples or reasoning from your plant’s current conditions

## Slide 23
THANK YOU