## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 19:
Concepts and indicators of financial and economic analysis of EE projects
MANAGEMENT OFFICERS

## Slide 2: Content
1
Some basic issues of project finance
3
Estimation of costs and benefits of EE project
2
Financial Analysis Techniques
4
Comprehensive evaluation of energy efficiency projects

## Slide 3: 1. Some basic issues of project finance
Finance is one of the most important factors determining the success of the EE project. Expected savings costs or additional profits need to reach or exceed a certain threshold. EE projects must be competitive compared to other projects. To determine the right investment option by comparing options to achieve the organization's goals.

## Slide 4: 1.1. Types of expenses
Energy efficiency projects involve a variety of costs:
Investment costs (cost of capital)
Operating and maintenance costs
Energy and related costs Labor costs (salaries for operating and management staff, ...) Repair and maintenance costs Other expenses (auxiliary materials, administrative expenses)
Other expenses
Replacement cost: the cost to remove the equipment at the end of the project lifecycle. Loss of production due to production stoppage during project installation and commissioning of the system. ….
Expense​ install set ( build) build , install put )
Expense​ design bag
The type taxes , fees sea mandarin
The costs​ dig create core pill
The costs​ other ( Bao dangerous , technical technique and Transport load)
Notes: Qui mô của khoản đầu tư là yếu tố rất quan trọng trong đánh giá tài chính của các dự án hiệu quả năng lượng. Chi phí này thường thể hiện bằng một lượng tiền lớn chi vào năm dự án được triển khai. Chi phí đầu tư bao gồm các loại chi phí sau đây:
Các chi phí vận hành và bảo dưỡng gắn với các hoạt động đang thực hiện hoặc với các thiết bị được phân tích. Các loại chi phí khác nhau hình thành chi phí vận hành và bảo dưỡng bao gồm

## Slide 5: 1.2. Basic financial concepts
Interest
When a certain amount of money is lent over a specified period of time (typically a year), a certain percentage will be paid FV = PV(1 + i)n
Discount Rate
To convert the future cash flow to the current equivalent amount, based on the adjustment of the value of the money Referred to as the threshold rate or cost of capital
When a certain amount of money is lent over a specified period of time (typically a year), a certain percentage will be paid FV = PV(1 + i)n
To convert the future cash flow to the current equivalent amount, based on the adjustment of the value of the money Referred to as the threshold rate or cost of capital
Depreciation
Allocate investment costs over the predicted life cycle of the equipment or process Depreciation values are used to reduce the value of the investment Accounting value and expected or useful life cycle
Inflation
Measure the purchasing power of money Inflation is often described as a percentage
Residual value
The amount of money that can be obtained from the asset at the time of replacement or at the end of the research cycle

## Slide 6: 1.2. Basic financial concepts (continued)
Benefit
Benefits from an EE project may include: Energy saving; income from the sale of energy; reduce maintenance costs; Income from quality improvement income from increased productivity
Net Cash Flow
Graph depicting cash flow over a period of time
Life cycle
The cycle time between the start and end of the project in which the costs and benefits occur

## Slide 7: 1.3. Project cash flow
Cash Flow Before Tax (CFBT)
Cash flow does not include corporate income tax;
Cash Flow After Tax (CFAT)
CFBT is the basis for calculating CFAT (Cash Flow After Tax) for projects subject to corporate income tax

## Slide 8: 1.4. Value over time of cash flows - Equivalent value
Single interest matching
K0 => K0 + K0 * i * n in which: K0 : Initial capital (capital at the time of 0) i : Interest Rate (%) n : Number of interest compounding periods
Compound interest
K0 => K0 (1+i )n in which: K0 : Initial capital (capital at the time of 0) i : Interest Rate (%) n : the number of interest compounding periods

## Slide 9: 1.5. Discount Rate and Cost of Capital
The discount rate is usually denoted as "r or i". Cost of capital = source of capital x interest rate. The company's general capital cost is calculated based on the company's borrowing capital cost and the company's own capital cost (the profit rate obtained if the company invests outside). When the capital source is only derived from bank loans, the total cost of capital will be equal to the bank loan interest. Depending on the structure of the fund, the combination formula can have more than two components:

## Slide 10: 1.6. Effects of inflation
The concept of inflation: the degree of decline in the value of the currency We can prove it (1+R) = (1+r)* (1+ilf) r: nominal interest rate/discount rate; ILF: inflation rate; R: real discount rate or R = r +ilf +r*ilf approximate we have R = r + ilf
Coin
Increase Value due to investment
Decrease in value due to inflation

## Slide 11: 1.7. Current value of cash flow
Current Value = Other Reciprocal Value x (PV Coefficient)
Annual cash flow value n
Cash flow value at "Time 0," is at the start of the project
The current value factor (PV) depends on the discount rate i With different values of i (discount rate): 10%, 15%, 20% With n years (number of years) Available Tables Formula (PV = ) Excel (function PV(rate,nper,pmt,fv,type))

## Slide 12: 1.8. Some value conversion formulas

## Slide 13: 2. Financial indicators used for evaluation of EE projects
Simple Payback Period (SPP)
Return on Investment (ROI)
Net Present Value (NPV)
Internal Rate of Return (IRR)
Expense​ of operation and maintenance (O&M)
Life circle cost (LCC)

## Slide 14: 2. FINANCIAL INDICATORS USED TO EVALUATE PROJECTS
1
SPP
Time required to recover investment capital from cash flow Quantitative method is widely used to evaluate the cost effectiveness of energy-saving investments Do not consider savings after the payback year and do not take into account the time-based value of the simple payback = Annual Net Savings/ capital cost of the project
4
IRR
The discount rate at which the net present value of the cumulative benefits of an investment equals the cost of the investment. The higher the IRR, the more efficient the project.
2
ROI
Describe the “annual benefit” from the project as a percentage of the cost of capital
Does not require projects to have the same life or compare costs
ROI = cost of capital/annual cash flow
5
0&M
The operating energy cost (i.e. the electricity cost for the equipment, e.g. a pump or a 10kW fan)/year will be higher than the initial investment cost of the equipment.
3
NPV
All Net benefits are amortized at the lowest attractive rate of return to determine equivalent present values.
6
LCC
For example, consider comparing traditional fluorescent lamps, spotlights, to replace with CFL or LED.
CFLs last 5 times longer than halogen lamps and LEDs last at least 20 times longer than halogen lamps => the calculation will take into account the life cycle to compare the original equipment and the replacement

## Slide 15: Financial indicators used to evaluate renewable energy projects
Payback period – the length of time it takes for the project’s income to recover the project’s investment costs. Simple payback period (SPP): does not take into account the time value of money. Usually only applicable to projects with short payback periods (less than 3 years).
Total value delivered?
Profitability per dollar of capital?
Net Present Value (NPV)
Internal Rate of Return (IRR)
What financial performance evaluation criteria do you often use to make investment decisions?

## Slide 16: Rated by NPV and IRR
NPV
B t : Profit benefit annually​​​
C t : Cost annually​​​
i : Ratio rate extract discount
C t
B t
1
2
n
IRR
NPV= 0  IRR value
IRR (Internal Rate of Return): is the appropriate discount rate at which NPV = 0

## Slide 17: Evaluation of renewable energy projects based on NPV
NPV > 0: the larger the NPV of the project, the higher the financial efficiency of the project.
NPV ≤ 0: the project is not financially efficient
The selected option is the option with the largest NPV and NPV >0
Projects have equal lifespans
Direct comparison of NPV values ​​of projects
Projects have different lifespans.
  - Find the least common multiple of the project lives
  - Iterate through the projects to the life equal to the least common multiple
  - Compare the projects with the new lives
  - Note: can compare pairs of projects

## Slide 18: Rated by NPV and IRR
IRR : Rate collect profit internal in
With i1 we have NPV1; NPV1 >0
With i2 we have NPV; NPV2 <0
We have :
Project with IRR > i* is feasible
The project with the largest IRR is the optimal project
IRR
NPV
i
NPV1
NPV2

## Slide 19: Rated by NPV and IRR
IRR ≥ MARR - the larger the IRR of the project, the higher the financial efficiency of the project.
IRR < MARR - the project is not financially efficient.
The selected option is the option with the largest IRR ≥ MARR
MARR: Minimum Acceptable Rate of Return
Projects with equal lifespans
Directly compare the IRR values ​​of the projects
Projects with different lifespans
Compare each pair of projects
Subtract the project with small investment from the project with large investment
If the new project has an IRR larger than MARR, the project with large investment is better, otherwise the project with small investment is better

## Slide 20: Financial indicators used to evaluate EE projects
Target | Definitio | Advantages | Disvantages | Suggested Application
NPV (Net Present Value | NPV is the net present value, which measures the difference between the total present value of cash inflows and cash outflows over the life of a project, after discounting at an appropriate rate. | Full consideration of cash flows throughout the project life. - Reflects the time value of money. - Easy comparison between different projects | It is necessary to choose an appropriate discount rate, otherwise it may lead to incorrect results. - Cannot be applied to projects with too long or uncertain time and cash flows. | - Used in long-term projects, when cash flows can be forecasted and an appropriate discount rate can be determined.
IRR (Internal Rate of Return) | IRR is the internal rate of return, which is the discount rate that makes the net present value (NPV) of a project equal to 0. It reflects the profitability of the project. | Easy to understand, easy to use. - Shows the project's profit rate, helping to evaluate the project's attractiveness. - Suitable for investors requiring high profit rates. | Cannot be applied if there are many inconsistent cash inflows and outflows. - IRR can have multiple values ​​in some special situations (uneven cash flows). | Used to compare investment projects of different sizes and durations. - Suitable for investors interested in profitability.
(Payback Period) | Payback period is the amount of time required to recover the initial investment from the cash flows generated during the project. | Easy to understand and calculate. - Reflects the ability to recover capital quickly. - Simple and cost-effective analysis. | Does not take into account the time value of money. - Does not fully reflect long-term financial feasibility - Does not measure profits after the payback period. | Suitable for short-term projects or when quick decisions are needed. - Used when wanting to evaluate the liquidity of a project.
(LCC - Life Cycle Costing) | LCC is a method of calculating the total cost of a project throughout its life cycle, from design, construction, operation to maintenance and disposal. | Calculates total costs over the life of the project. Useful in making long-term cost decisions - Can identify hidden costs that are not visible at the outset. | - Complex and requires a lot of long-term forecasting data. - Can be difficult to determine exact future costs. | Used in projects requiring long-term sustainability, such as infrastructure, manufacturing plants. - Suitable for long-term maintenance and operation decisions.

## Slide 21: Financial indicators used to evaluate EE projects
NPV is the most powerful financial analysis indicator because it fully considers the project's cash flows and reflects the time value of money, helping to make a more accurate decision on the feasibility of the project. However, it requires choosing the appropriate discount rate.
IRR is useful in measuring the profitability of a project, especially when comparing projects with different rates of return. However, it can be problematic when cash flows are unstable or inconsistent.
Payback period is simple and easy to use, especially in short-term projects or when quick decisions are needed. However, it does not take into account the time value of money and does not fully reflect long-term profitability.
Life cycle analysis (LCC) is a good method to evaluate the overall cost over the life of a project, which is useful in projects that require long-term sustainability, but requires a lot of forecast data and can be complicated in determining future costs.
Depending on the goals and characteristics of each project, these indicators can be used independently or in combination to make optimal financial decisions.

## Slide 22: Advantages of NPV and IRR over other methods
Takes into account the time value of money
Takes into account all cash flows over the life of the project
IRR is more popular with development financers and those who are more familiar with the rate of return
A project is acceptable if the IRR is higher than the cost of money used to finance the project, so the investor's desired rate cannot be arbitrary

## Slide 23: Which method to use?
An investor who wants his money to pay back in a short period of time will use the discounted payback period. When there is no loan, NPV and IRR are preferred. A bank that lends and has several investment options will want to use the NPV and IRR methods to compare returns with other investment options For small projects, the calculation of the payback time may be sufficient, but for large projects that require external loans, then it is necessary to calculate NPV and IRR When you don't have enough information at hand, a simple payback period will often be used Some investors want a high intrinsic return on investment instead of immediate return on investment IRR cannot be used if the project has more than 1 year of negative net cash flow or a project with a lot of negative cash flow. In this case, use NPV

## Slide 24: Sensitivity Analysis
Project cost increase (+10%)
Base plan
Bank interest rates increased (+20%)
Exchange rate change (-20%)
Save energy reduced (-20%)
Payback period
NPV
IRR

## Slide 25: Life cycle costs
Currently, in the analysis and evaluation of energy saving projects, people use the Life Cycle Cost Analysis (LCC) method for evaluation.
Life cycle cost of a product
LCC = Purchase cost + Operation and maintenance cost + Spare parts cost + Electricity cost
In case of taking into account the time value of money flow:
LCC = Initial investment cost + Present value of future costs.
In which: C0: Initial investment cost
Ct: Cost incurred during the use of equipment in year t
n: Equipment life
i: Discount factor

## Slide 26: Wallet example LCC calculation
Calculate the life cycle cost and compare the alternative of replacing a 15W LED lamp with a 100W incandescent lamp. The parameters of the alternative are given in the table below.
LED lamps have a lifespan of 20,000 hours, each year they are lit for 4,000 hours, so the lamp can be used for 5 years. Incandescent lamps only have a lifespan of 1,000 hours, so in 1 year the bulb must be replaced 4 times. During the lifetime of the LED lamp, 20 incandescent bulbs must be used.

## Slide 27: Wallet example LCC calculation
Electricity power and cost​ money electricity belong to each type lamp row year :
Initial cost​​ and cost​ release born row year of 2 types lamp :
With system number extract discount i = 10 % then cost ring life rule about year head when comparing 2 types​ lamp To be :
 | Lamp fiber burn | Led
Electricity power pepper consumption (kWh) | 0.1*4000 = 400 | 0.015*4000 = 60
Money electricity ( copper ) | 800000 | 120000

## Slide 28: 3. Wish cost and benefit​​ benefit belong to attend EE project
Deduction loss :
  Is the systematic valuation and allocation of the value of an asset . wear and tear after a period of use. Use to calculate discount apart from tax collect enter business career in those year head belong to attend judgment​
Deduction loss all or nothing loss line calculate Okay history use universal variable best Currently​
  Money extract discount loss row year : D t = D = (G 0 -G cl )/ T kh
    In there :
    P 0 : Price initial value ( original ) price ) of talent product try determine ;
    P fa : Remaining value of fixed assets at the end of the depreciation period
    T dp : Depreciation period ​
  Single simple , but slow collect return capital head private .

## Slide 29: Example of Straight Line Depreciation
P0 = 100; Pfa = 10; Tdp : 5 years
Years
P0
Pfa
Tdp

## Slide 30: Method of repayment of principal and interest
Loan and payment method
Where to get capital to implement the project
Loan or equity?
Loan?
  How much?
  For how long?
  Guaranteed?
  Term?
  Interest rate?
  Payment method?
Payment method?
Annual payment includes: Principal and interest payment
Annual principal repayment, annual interest payment calculated on loan capital
Repay principal at the end of the loan term, pay interest annually
Repay principal and interest annually
Repay principal and interest at the end of the loan term
investment project capital
equity
loan capital
principal repayment
interest payment
interest period

## Slide 31: Principal and interest repayment methods
Annual principal repayment
Principal repayment = Loan/number of years
Interest repayment = interest rate × outstanding principal at the beginning of the year
Years
Interest
Annual
Origin
still owe
Years
Interest
Annual
Origin

## Slide 32: Principal and interest repayment methods
Annual installment
Annual payment A = Loan  ( A/P,i,n)
Interest payment = interest rate  outstanding principal at the beginning of the year
Principal payment = annual payment - interest payment
Principal and interest paid in final year
still owe
Years
Interest
Annual
Origin
still owe
Years
Interest
Annual
Origin

## Slide 33: Corporate Income Tax
Annual corporate income tax
TN = L  T n
in there:
L : Income bear tax
  T n : Tax rate
Depreciation and interest are deductible and not included in corporate income tax.

## Slide 34: Financial cash flow of EE investment project in case of non-loan
Determine project cash flow
Calculate efficiency indicators
  NPV
  IRR
Compare projects based on NPV and IRR indicators
    Cash flow before tax (CFBT): CFBTt = Bt – Ct
    Bt: project profit stream
    Ct: project cost stream
    Taxable income (TI – Taxable Income): TI = CFBT – D
    D: Depreciation
    Income tax (IT – Income Tax): IT = ts  TI
    ts: tax rate
    Cash flow after tax:
    CFAT = CFBT - IT
    CFAT = CFBT- (CFBT- Dt ) ts = CFBT (1-ts ) + Dts
    Profit after tax (NI – Net Income):
    NI = TI -IT= TI(1-ts )
    = (CFBT - D )(1-ts ) =CFBT (1-ts ) + Dts - D
    = CFAT - D

## Slide 35: Financial flow of EE investment project in case of loan
Capital head fixed assets : 500
Current money before tax
Tax rate Tr : 20 %
Deduction loss even in 5 years

## Slide 36: Financial cash flow of investment project of renewable energy in case of borrowing capital
  Borrowing affects project CFAT cash flow
  NPV CSH increases
  IRR CSH increases
  In case of borrowing, two actors have income from the project: creditors and owners
Parameters as in the example above
Borrow 200. Pay principal evenly over 5 years, interest rate 10%
Project CFBT = Shareholder CFBT = Bt - Ct
Debt CFBT in year 0: Loan Capital
Debt CFBT = - (Principal Payment + Interest Payment)
TI = CFBT - Depreciation - Interest Payment
IT = TI × Tax Rate
Shareholder CFAT = Shareholder CFBT –
Principal Payment - Interest Payment - IT

## Slide 37: Some issues when evaluating EE projects
One number problem subject about school fit get a loan capital
When​ get a loan good than Are not get a loan ?
Have right get a loan more much more good or not​
Where to be interest rate threshold to decide determine Have should borrow or not ?
Fight price risk round real presently attend sentence effect fruit power quantity
The costs​ head private increase
Expense​ power wage increase / decrease
Image enjoy belong to abuse release next attend sentence
Image enjoy belong to attend sentence next product export and next the set part link mandarin other...

## Slide 38: Quizz
The purpose of depreciation of project fixed assets (TS) is to…
A) reflects the depreciation of the asset B) knows the residual value of the asset
C) shows the useful life of the asset D) supports non-taxation of the amount invested in the asset
2. How many times can a project's cumulative cash flows change sign during the project's life?
A) no time B) one time C) many times D) No
3. If a project has an IRR less than the loan interest rate then:
A) should not borrow capital B) should not invest
C) IRR csh = IRR project D) none of the answers are correct
4. Choose the correct formula in the following sentences:
A) CFAT =CFBT*(1-Ts) + NI B) CFAT =CFBT*(1-Ts) + D*Ts
C) CFAT =CFBT+ NI D) CFAT =CFBT*(1-Ts) + D

## Slide 39: 4. Comprehensive evaluation of energy efficiency projects
Comprehensive evaluation of energy efficiency projects
Bases for Impact Assessment
Risk assessment facilities
Project Management and Risk Management for Energy Efficiency Projects

## Slide 40: Basis for impact assessment
Key elements of impact assessment and introduction of the approaches used to decide on energy savings
Establish evaluation objectives
Establish an approach, identify baseline scenarios, and prepare a plan
Compare energy use and demand before implementing the program
Report on the results of the assessment and, work with the chapter operator to implement opportunities
Program evaluation process begins

## Slide 41: Risk Management Facilities
Identify the sources of risk
Deciding the paths and the key points can cause these risks
Measuring the potential consequences of these risks under different scenarios
Provide the means to mitigate and deal with these consequences

## Slide 42: Project management and risk management for energy efficiency projects

## Slide 43: Quizz
When analyzing in a risky condition where the project efficiency is not achieved:
A)need to adjust the risk level lower B) need to change the analysis method
C) need to readjust the design project D) need to change the project evaluation criteria
2. The cost basis of a project is:
A) Variable costs according to the product B) Costs that appear in the future
C) Benefits lost due to not choosing another project D) Costs incurred in the past
3. To minimize the risk of the project, the project should be analyzed with:
A)Longer life B) Larger discount factor
C) Larger investment scale D) Higher debt ratio
4. The payback period of the project depends on:
A) CFBT Series B) CFAT Series
C) MARR D) Project Life
A) CFBT line B) CFAT line
C) MARR D) Project life

## Slide 44
THANK YOU