## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 20: Financial economic analysis & Some practical studies
MANAGEMENT OFFICERS

## Slide 2: Some financial options
Using equity (ex: using retained earnings)
Using the loan
Using the finance lease option
Using contracts effectively (Performance Contract)
Notes: Luôn có các lựa chọn khác nhau về vốn khi tiến hành triển khai dự án TKNL.
Do dự án TKNL cũng là một dự an đòi hỏi hiệu quả, do vậy việc sử dụng nguồn vốn tài trợ như thế nào để đạt được hiệu quả cao là hết sức quan trọng.
Thông thường các công ty nên xem lựa chọn vay vốn để thực hiện dự án, do lựa chọn này làm giảm áp lực về vốn cho công ty và thu được một phần lợi ích từ thuế.

## Slide 3: Using equity
Advantages
Easy to deploy
Low cost.
Good way to start commercial energy-saving activities
The sustainability of the project can be ensured through independent verification
Disadvantages
The sustainability of savings
Necessity of supervision, monitoring and independent verification
Necessity of trusted relationships and equipment suppliers
Limit scope
Equipment suppliers
Company
Purchase cost
Equipment

## Slide 4: Using the loan
Paying off the principal purchase cost
Banks
Equipment suppliers
Companies
Equipments
Bank may provide credit up to 60%-70% of the total project cost
Amount used to repay the loan is typically funded through energy savings
Repayment period corresponds to the payback period of the energy savings project

## Slide 5: Using the finance lease option
Reasons of finance lease
Financial reasons
  - Some lease agreements, the entire lease payments may be tax deductible.
  - Some lease agreements allow off-balance-sheet financing, preserving financial credibility.
Risk sharing
  - Leasing is good for using short-term assets and reduces the risk of owning outdated equipment.
  - Lease contract involves fewer risks and responsibilities.
Rent payment
Leasing organization
A renting enterprise
Rented equipment
Notes: BỔ SUNG

## Slide 6: Contracts effectively
Contract effectively is a single agreement that allows investments in necessary improvements with minimal upfront capital investment.
Contractors are responsible for purchasing, installing equipment and maintaining it throughout the contract.
Contractors are compensated based on the efficiency of the installed equipment, and only after the equipment has actually reduced costs.
Energy Service Companies (ESCOs) typically serve as contractors in this business operation.
Notes: Hợp đồng hiệu quả chưa phổ biến ở Việt Nam, cần có khung pháp lý chặt chẽ để thực hiện hợp đồng.
Các hoạt động đo lường và xác nhận tiết kiệm có vai trò cực kỳ quan trọng đối với loại hợp đồng này. Thực hiện tốt M&V sẽ tránh được các tranh cãi không đáng có sau này.

## Slide 7: Your choice?
Using equity (ex: using retained earnings)?
Using the loan?
Using the finance lease option?
Using contracts effectively (Performance Contract)?

## Slide 8: ESCOs typically offer the following options
Guaranteed fixed savings amount;
Guaranteed fixed energy savings;
A percentage of energy savings;
or
A combination of the above options.
Facility managers often lean towards the 'guaranteed savings' option

## Slide 9: Guaranteed savings
Banks
Project owners
Equipment suppliers/ Contractors
Fixed payment
Energy-saving service
Principal and interest repayment
Investment

## Slide 10: Guaranteed savings
Advantages
Disadvantages
Saving amount is guaranteed.
Scope of application is not limited.
One party handles everything.
Service provider bears most of the risks.
Easy to secure external financing.
Costs more than the direct contractor model.
Requires skilled service providers.
Repayment risk for the project owner.

## Slide 11: Shared savings
Banks
Project owners
Equipment suppliers/ Contractors
Shared savings
Capital investment
+ energy savings services
Principal and interest repayment
Investment

## Slide 12: Shared savings
Advantages
Investors do not need capital.
Scope is not limited.
One party handles everything (turnkey contract).
Service provider bears most of the risks.
Disadvantages
The costs are higher compared to both direct contract and guaranteed savings models.
Requires skilled service providers.

## Slide 13: Quizz
What financial methods can businesses use to implement projects?
A) Using equity B) Using the loan C) Using the finance lease
D) Using equity, Using the loan, Using the finance lease, Using contracts effectively
2. Advantage of using equity?
A) Necessity of supervision, monitoring and independent verification
B) Low cost.
C) Necessity of trusted relationships and equipment suppliers
D) Scope limited.
3. With ESCOs offers, which choice do facility managers usually prefer?
Guaranteed savings; B) Shared savings; C) A combination of the above options
4. Disadvantage of “guaranteed savings” option?
A) Requires skilled service providers.
B) Saving amount is guaranteed.
C) Service provider bears most of the risks.
D) Easy to secure external financing.

## Slide 14: APPLICATION EXAMPLE
Assume PizzaCo (the facility owner) needs a chilled water system for a specific production purpose. The installation cost of a new system is $2.5 million. The equipment's lifespan is 15 years, but it's only needed for 5 years, after which the cooling system is expected to be sold at an estimated market value of $1,200,000 (book value at year 5 = $669,500). The water-cooled system will save PizzaCo $1 million annually in energy costs. PizzaCo's tax rate is 34%. Annual equipment maintenance and insurance costs are $50,000. PizzaCo's MARR (Minimum Acceptable Rate of Return) is 18%. At the end of year 5, if PizzaCo plans to sell the equipment above its book value, it will realize additional income known as "capital gain" (equal to market value minus book value) and will be taxed accordingly. If PizzaCo sells the equipment below book value, it will incur a "capital loss".
PizzaCo needs to determine the most effective investment approach.

## Slide 15: Cash flow calculation formula
EOY = End of year
Saving = Pre-tax cash flow
Depr. = depreciation
Taxable income = Saving – Depr. – pay interest
Tax = (Taxable income)*(tax rate)
ATCF = After-tax cash flow = Saving – Total cost – Tax
Table of calculation formula in economic analysis
A | B | C | D | E | F | G | H | I | J
EOY | Saving | Depr. | Pay |  | Total | remaining principal | Taxable income | Tax | ATCF
 |  |  | Principal | interest |  |  |  |  | 
n n+1 n+2 |  | = straight-line depreciation |  |  | =(D)+(E) | =(G at year n) – (D at year n+1) | =(B)-(C)-(E) | =(H)*(tax rate) | =(B)-(F)-(I)
Notes: Dòng tiền dự án được đưa vào tính toán dạng bảng theo định dạng phù hợp.

## Slide 16: Equity financing
When the equipment is installed, PizzaCo will save $1 million annually for 5 years, but will incur $50,000 per year for maintenance and insurance. At the end of year 5 of the project, PizzaCo expects to sell the equipment for a market value of $1,200,000. Assuming a MARR of 18%, and the equipment is depreciated over 5 years with a residual value of 0.
Manufacturer of water-cooled cooling systems
PizzaCo
Purchase cost
Equipment

## Slide 17: Economic analysis for the case of using equity financing
Note: Loan amount: 0
Financial loan rate: 0% MARR = 18%
Tax rate = 34%
Straight-line depreciation. Book value at the end of year 5: 0
Estimation of market value at the end of year 5: 1,200,000
EOY 5* representing the market value and book value of the equipment
Taxable income: =(Market value – Book value) =(1,200,000 - 0) = $ 1,200,000
Notes: Tài trợ hoàn toàn băng vốn chủ sở hữu.
Trường hợp này sẽ không có được lợi ích thuế từ các phần trả lãi vay nợ.
Sẽ khó thực hiện với các dự án đòi hỏi vốn lớn.

## Slide 18: Bank loans
Pay principal
Purchase cost
Bank
Manufacturer of water-cooled cooling systems
PizzaCo
Equipment

## Slide 19: Economic analysis for the loan
Note: Loan amount: 2,500,000 (for equipment purchase in year 0)
Financial loan rate: 15% MARR = 18%
Tax rate = 34%
Straight-line depreciation. Book value at the end of year 5 : 0
Estimation of market value at the end of year 5: 1,200,000
EOY 5* representing the market value and book value of the equipment
Taxable income = (Market value – Book value) =(1,200,000 - 0) = $ 1,200,000
Notes: Vay ngân hàng là biện pháp đơn giản nhất có thể thực hiện tuy nhiên vẫn còn có các biện pháp khác để huy động vốn.

## Slide 20: Operating lease
Rental payment
Manufacturer of water-cooled cooling systems
(Lender)
PizzaCo
(Borrower)
Rental equipment
Notes: Các hình thức thuê chưa thực sự phổ biến ở Việt Nam hiện nay, đặc biệt là thuê vốn.
Cần có khung pháp lý và qui định chặt chẽ trong trường hợp thuê vốn.

## Slide 21: Economic analysis of leasing contracts

## Slide 22: Transactions with efficient contracts
Loan payment to ESCO
Equipment
PizzaCo
Manufacturer of water-cooled cooling systems
ESCO
Purchasing cost
Install energy-saving equipment
Financial company/ bank
Loan
Loan payment

## Slide 23: Economic analysis for efficient contracts

## Slide 24: Example of calculating an EE project
Technology diagram of cement production

## Slide 25: Example of calculating an EE project
Solution No | Name of Solution | Yearly saving |  | Estimation of savings amount (million VND) | Estimation of investment cost (million VND)
 |  | GJ/y | MWh/y |  | 
ECM 1 | Improving combustion efficiency by reducing excess air at the preheater stage and lowering the clinker burning temperature. | 75,424 |  | 2,420 | 3,890
ECM 2 | Improving cooling efficiency by evenly distributing clinker. | 95,742 |  | 3,070 | 2,380
ECM 3 | Installing an additional cyclone stage for the preheater in phase 1 and recovering additional heat from the exhaust gases. | 326,554 |  | 10,480 | 27,000
ECM 4 | Using air cooling to supply the burner of the kiln. | 21,343 |  | 685 | 740
ECM 5 | Generating electricity from waste heat from the cooling system of the kiln. | - | 29,490 | 32,180 | 187,200
ECM 6 | Installing a variable frequency drive for the raw material fan (R2S20) - production line 2. | - | 2,080 | 2,040 | 7,200
ECM 7 | Replacing inefficient equipment - preheater fan for production line 1. | - | 1,920 | 1,885 | 3,000
ECM 8 | Replacing inefficient equipment - raw material fan for production line 1. | - | 1,490 | 1,460 | 3,000
ECM 9 | Installing an input conveyor system for kiln line 1 to reduce energy consumption in the pneumatic conveying system. | - | 2,290 | 2,250 | 6,000
ECM 10 | Installing a variable frequency drive for the fan at the coal mill (P22) - production line 2. | - | 490 | 480 | 600
 | Total | 519,063 | 37,760 | 56,950 | 241,010
Example of reporting: Choose an ECM saving solution 6. Prepare investment reports to implement projects?

## Slide 26: Financial implementation contents
The initial investment of 7.2 billion can be entirely funded by the company or through borrowing.
When seeking loans, low-cost financing sources (supporting energy efficiency projects) or Ministry of Industry and Trade support should be considered.
Clear determination of interest repayment mechanism:
Equal principal repayment with interest on remaining principal
Equal annual principal and interest repayment
Determine the lifespan of project equipment (how long the investment equipment will be used) for depreciation calculation and project cash flow details.
Comprehensive calculation of construction and installation costs and initial equipment deployment (typically included in the audit report as initial investment costs).
Calculation of annual operation and maintenance costs (e.g., inverters requiring air-conditioned rooms, incurring additional costs).
If the audit report does not clearly outline annual operation and maintenance costs, these calculations need to be incorporated

## Slide 27: Financial implementation contents
Utilize all computed data to populate the project cash flow statement (refer to the spreadsheet).
When calculating the NPV of the project, ensure to apply an appropriate discount rate (depending on the company's cost of capital and the cost of different funding sources).
Conduct a risk analysis for the project:
  Increased investment (increased construction costs, increased equipment costs),
  Fluctuations in energy costs,
  Evaluate the impact of inflation if the project extends over time
  ...

## Slide 28: Some sources of funding support
Funding support from UNIDO, World Bank
Funding support from DANIDA (for both private enterprises and foreign investments)
Government support (up to 30% of total project value and maximum of 5 billion VND)
Other funding sources → Refer to detailed information from the Energy Efficiency Office, Ministry of Industry and Trade.

## Slide 29: Quizz
The project's NPV standard is the evaluation standard :
Relative value of project interest. B) Absolute value of project profit.
C) Percentage of profit compared to invested capital. D) The percentage of revenue relative to costs
2. The project's IRR standard is the evaluation standard:
Relative value of project interest. B) Absolute value of project profit.
C) Percentage of profit compared to invested capital. D) The percentage of revenue relative to costs.
3. When depreciation expense decreases by $100, the corporate income tax rate is 25%, and the project
uses 100% equity. So how has CFAT changed?
A) CFAT increases by $25 B) CFAT decreases by $25
C) CFAT does not change D) There is no correct answer
4. An investment project has an initial investment capital of 800 million VND. Annual CFAT from year 1 to year 4 is 268 million VND. Is the project feasible, knowing the MARR is 15%.
Not feasible B) Feasible
C) Not enough information to conclude D) There is no correct answer
Notes: Ý nghĩa của việc trích khấu hao tài sản cố định (TS) của dự án là để…
A) phản ánh sự giảm giá của tài sản B) biết giá trị còn lại của tài sản
C) thể hiện tuổi thọ khai thác của tài sản D) hỗ trợ không đánh thuế số tiền đã đầu tư vào tài sản
2. Dòng tiền tích lũy của một dự án có thể đổi dấu bao nhiêu lần trong suốt vòng đời dự án?
A) 0 lần B) 1 lần C) nhiều lần D) không xác định
3. Chi phí cơ hội là của một dự án là:
A) Chi phí biến đổi theo sản lượng B) Chi phí xuất hiện trong tương lai
C) Lợi ích mất đi do không lựa chọn dự án khác D) Chi phí phát sinh trong quá khứ
4. Nếu một dự án có IRR nhỏ hơn lãi suất vay thì :
A) không nên vay vốn B) không nên đầu tư
C) IRR csh = IRR dự án D) không đáp án nào đúng
5. Chọn công thức đúng trong các câu sau đây:
A) CFAT =CFBT*(1-Ts) + NI B) CFAT =CFBT*(1-Ts) + D*Ts
C) CFAT =CFBT+ NI D) CFAT =CFBT*(1-Ts) + D

## Slide 30
THANK YOU