## Slide 1: TRAINING PROGRAME for IEs
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
for: Enterprise leaders

## Slide 2: Training program for business leaders
TIME | Content
8.00 – 8.30 | Registration
8.30 – 8.40 | Opening Remarks
8.40 – 9.45 | Module 1: Project introduction Policy introduction: energy saving, greenhouse gas emission reduction, gender issues related in EE
9.45 – 10.00 | Breaks
10.00– 11.00 | Module 2. Relations between energy, environment and production and business, use of clean energy
11.00 – 11.45 | Module 3. The current situation of energy use and potential of industrial waste in Vietnam (cement, steel, seafood processing, brick and ceramic, textiles, beverages, paper and pulp, other industries (plastics...)
11.45 – 12.00 | Discuss
12.00 – 13.30 | Lunch
13.30 – 14.15 | Module 4. Energy Management, Energy Management System
14.15 – 15.00 | Module 5. EE project financing and VSUEE project financing approach
15.00 – 15.15 | Breaks
15.15 – 16.15 | Component 6. Case study in EE for Manufacturing Industry: Cement, Steel, Seafood Processing, Brick and Ceramic, Textile, Beverage, Paper & Pulp, Other Industries (Plastics...)
16.15 – 16.45 | Discuss
16.45 – 17.00 | Closing

## Slide 3
Module 3.
Current and potential of EE in steel industries in Vietnam
TRAINING PROGRAME for IEs
for: Enterprise leaders

## Slide 4: Global industrial energy usage
Total Final Energy Consumption (TFC) by Sector from 1990 to 2020-2022
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 5: Final electricity consumption by sector in Vietnam

## Slide 6: Final energy consumption by industry in Vietnam
Transportation
31,7%
Services
3,9%
Household 14,9 %
Non- energy
2%
Industry
45,7%
Argriculture
1,8 %
2012
2021
Industry
Non- energy
5,5%
Argriculture
5,2%
Transportation
16,7%
Services
3,2%
Household
15,3 %

## Slide 7: Current status of energy use in Vietnam
Agriculture, forestry and fisheries
Construction
Industry
Non- energy
Household
Services
Transportation

## Slide 8: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3,068 DEUs (up from 2,496 in 2017), consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority—2,599 facilities consuming 50,570,115 TOE. The Vietnamese industry has significant potential for energy efficiency.
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 9: Number of Designated Energy Users (DEUs)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEUs List)
Number of DEUs
Energy using of DEUs (kTOE)

## Slide 10: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 11
Primary energy
In 2020, Vietnam's TPES was estimated at 95,762 KTOE, increased by only 1.5% compared with the previous year.
1
Primary energy use
The export output in 2019 was only 8,834 KTOE, a 2.4-fold decrease compared to 2010.
In 2019, energy imports reached 44,342 KTOE, a 39.6% increase compared to 2018.
2
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 12
Energy Intensity by Country
Considering population size, Vietnam's TPES per capita in 2018 was relatively low at only 848 kgOE/person, even lower than the ASEAN average of 1,041 kgOE/person. However, the TPES intensity per GDP was quite high. This indicates that Vietnam's energy efficiency needs improvement.
3
Amount of energy needed to produce one unit of economic output. A lower number means that economies produce economic value in a less energy-intensive way.
4
Energy intensity, 2000 to 2020
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 13: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 14: Specific Energy consumption and Energy Savings Potential
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report

## Slide 15: Current status of energy use in industry
Proportion of energy consumption: The industrial sector accounts for about 47% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, and chemical industries.
  These industries consume approximately 70% of the total energy in the industrial sector.
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.

## Slide 16: Energy consumption structure in the industry
Proportion of energy consumption by sector:
  Manufacturing sector: 60%
  Construction sector: 15%
  Mining sector: 10%
  Transportation and logistics sector 5%
Main types of energy used:
  Electricity: Account for the largest proportion in the energy consumption structure of the industrial sector.
  Oil and natural gas: Used in manufacturing and chemical industries.
  Coal: Mainly used in the cement and metallurgy industries.

## Slide 17: Causes of high energy consumption
Outdated technology: Many enterprises still use old technology, which consumes high amounts of energy and causes environmental pollution.
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology.
Low awareness of energy efficiency: Some enterprises have not prioritized energy efficiency measures in their production processes.

## Slide 18: Challenges in energy management and utilization
Technological challenges: Many enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among enterprises.

## Slide 19: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating, especially in industries such as textiles and electronics.
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the industrial development of Vietnam.

## Slide 20
EE potential in steel manufacturing industry

## Slide 21: Energy Intensity in Key Industries in Vietnam
Figure: Energy Intensity Improvement in Key Industries during VNEEP Phase 2 Changes of energy intensity in key industries

## Slide 22: Benchmarking in the Steel Industry
Benchmarking | Other Relevant Requirements
According to Clause 2, Article 5 of Circular 20/2016/TT-BCT, benchmarks for the steel industry from 2021 to the end of 2025 are as follows: Iron ore sintering: 1,960 MJ/ton Cast iron production (blast furnace): 12,400 MJ/ton Steel billet production (basic oxygen furnace- BOF): 100 MJ/ton Steel billet production (electric arc furnace- EAF): 2,500 MJ/ton Steel billet production (induction furnace): 2,500 MJ/ton Hot rolling of long steel: 1,600 MJ/ton Cold rolling of steel sheets: 1,500 MJ/ton | A plan must be prepared to comply with the benchmarks stated in Article 5 of Circular 20/2016/TT-BCT. DOITs must be reported to annually by January 15 regarding the implementation status of benchmarks.

## Slide 23: Energy Consumption in the Steel Industry
Main Types of Steel Products
Construction steel: Accounts for the largest share of domestic consumption, with products such as rebar and wire rods.
Steel plates and sheets: Used in the shipbuilding industry, automobile manufacturing, and other fabrication industries.
Steel pipes: Used in construction, oil and gas pipelines, and various other industrial applications.
Coated steel and galvanized sheets: Used in construction, appliance manufacturing, and the automobile industry.

## Slide 24: Energy Consumption in the Steel Industry
Main Types of Energy Consumed in the Steel Industry
Electricity: Used in processes such as electric arc furnace steelmaking, steel rolling, and operating auxiliary equipment.
Thermal energy: Mainly from coke, natural gas, and oil, used in iron smelting, iron ore sintering, and steel billet heating. Coal and oil are used in blast furnaces and kilns to provide heat for the manufacturing process.

## Slide 25: Specific Energy Consumption in the Steel Industry
Specific energy consumption rate in steel production
Energy performance in the Vietnamese steel industry is still low compared to developed countries, due to outdated technology and ineffective energy management. According to Circular No. 20/2016/TT-BCT of the Ministry of Industry and Trade, energy consumption benchmark for some steel production stages are as follows:
Sintering of iron ore: 1.960 MJ/tonne
Iron making by blast furnace: 12.400 MJ/tonne.
Production of steel billet by (top-blown) converter: 100 MJ/tonne.
Production of steel billet by electric arc furnace: 2.500 MJ/tonne.
Production of steel billet by induction furnace: 2.500 MJ/tonne.
Hot rolling of long steel products: 1.600 MJ/tonne.
Cold rolling of steel plates: 1.500 MJ/tonne.

## Slide 26: EEMs in the Steel Industry
Application of Advanced Steel Production Technologies
Use new blast furnaces with higher energy conversion efficiency.
Apply Electric Arc Furnace (EAF) technology to replace traditional blast furnaces.
Use EAF combined with high-quality scrap steel.
Implement green hydrogen steelmaking technology.
Effectiveness:
Reduce energy consumption and greenhouse gas emissions.
Enhance market competitiveness.
Improve product quality.

## Slide 27: EEMs in the Steel Industry
Waste Heat Recovery for Power Generation
Install a waste heat recovery system from the production process.
Use Blast Furnace Energy Recovery Turbine (BPRT) technology.
Effectiveness:
Save 10% of electricity consumption.
Reduce greenhouse gas emissions.
Improve Production Processes and High-Efficiency Equipment
Install frequency converter for fan motors.
Install automatic compensation system to maintain a stable power factor.
Effectiveness:
Reduce 25% of electricity consumption for motors.
Save 2.5% of total electricity consumption for the entire factory.

## Slide 28: EEMs in the Steel Industry
Optimizing compressed air and industrial gas systems
Closely monitor and control compressed air systems.
Use measuring equipment to detect leaks and energy losses.
Efficiency:
Reduce energy consumption and operating costs.
Improve operational efficiency.
Applying an energy management system according to ISO 50001
Build an energy management system to monitor and optimize energy use throughout the factory. Set specific energy saving goals, measure efficiency, and continuously improve. Integrate energy efficiency indicators into the KPIs of each department. Train employees on energy saving awareness and techniques. Effective:
    Reduce energy consumption by 5-20%. Improve production efficiency and meet international environmental standards.

## Slide 29: EEMs in the Steel Industry
Production of iron by route and scrap share of metallic inputs in the Net Zero Scenario, 2018-2030

## Slide 30: Example of EEMs in the Steel Industry in the world
Conversion of steel off gases to fuel (blast furnace)
This technology "recycles" waste gases from steel plants (e.g. blast furnace gas and coke oven gas) into synthetic fuels, thus using the CO2 twice and delaying its release.
Relevance for net zero
This technology could help reduce emissions from a steel plant and has the benefit of using CO2 emissions twice, thus potentially providing reductions in the lifecycle assessed (LCA) CO2 footprint of fuels. Total savings depend on what fuel is displaced, since unless the CO2 is captured from the use of fuels, the CO2 is in the end emitted. Furthermore, the net impact depends on what the current use of offgases is (e.g. flaring vs power generation) compared to their uses as alternative feedstock for ethanol production.
https://onlinelibrary.wiley.com/doi/full/10.1002/anie.202100577
Source: IEA

## Slide 31
Initiatives
The process was validated in industrial environment in China by the LanzaTech BaoSteel New Energy Company, 2012 and Shougang LanzaTech New Energy Technology Company, 2013. Lanzatech also has test facilities in New Zealand and Chinese Taipei.
First commercial plant began operation in 2018 in China, by Lanza Tech, Shougang Group and TangMing; produced 30 million litres of ethanol for commercial sale in its first year of operation.
Conversion of steel offgases to fuel (blast furnace)
Belgium: Arcelor LanzaTech Carbalyst (Steelanol) Ghent: Large-scale demonstration plant has been inaugurated in Ghent, Belgium, under the Steelanol project by ArcelorMittal and Lanzatech with a capacity of 80 million litres of ethanol upon completion. The process has been previously successfully tested at the site in 2016.
Example of EEMs in the Steel Industry in the world

## Slide 32
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU