## Slide 1: TRAINING PROGRAME for IEs
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
for: Enterprise leaders

## Slide 2: Training program for business leaders
TIME | Content
8.00 – 8.30 | Registration
8.30 – 8.40 | Opening Remarks
8.40 – 9.45 | Module 1: Project introduction Policy introduction: energy saving, greenhouse gas emission reduction, gender issues related in EE
9.45 – 10.00 | Breaks
10.00– 11.00 | Module 2. Relations between energy, environment and production and business, use of clean energy
11.00 – 11.45 | Module 3. The current situation of energy use and potential of industrial waste in Vietnam (cement, steel, seafood processing, brick and ceramic, textiles, beverages, paper and pulp, other industries (plastics...)
11.45 – 12.00 | Discuss
12.00 – 13.30 | Lunch
13.30 – 14.15 | Module 4. Energy Management, Energy Management System
14.15 – 15.00 | Module 5. EE project financing and VSUEE project financing approach
15.00 – 15.15 | Breaks
15.15 – 16.15 | Component 6. Case study in EE for Manufacturing Industry: Cement, Steel, Seafood Processing, Brick and Ceramic, Textile, Beverage, Paper & Pulp, Other Industries (Plastics...)
16.15 – 16.45 | Discuss
16.45 – 17.00 | Closing

## Slide 3
Module 3.
Current and potential of EE in Cement industries in Vietnam
TRAINING PROGRAME for IEs
for: Enterprise leaders

## Slide 4: Global industrial energy usage
Total Final Energy Consumption (TFC) by Sector from 1990 to 2020-2022
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 5: Final electricity consumption by sector in Vietnam

## Slide 6: Final energy consumption by industry in Vietnam
Transportation
31,7%
Services
3,9%
Household 14,9 %
Non- energy
2%
Industry
45,7%
Argriculture
1,8 %
2012
2021
Industry
Non- energy
5,5%
Argriculture
5,2%
Transportation
16,7%
Services
3,2%
Household
15,3 %

## Slide 7: Current status of energy use in Vietnam
Agriculture, forestry and fisheries
Construction
Industry
Non- energy
Household
Services
Transportation

## Slide 8: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3,068 DEUs (up from 2,496 in 2017), consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority—2,599 facilities consuming 50,570,115 TOE. The Vietnamese industry has significant potential for energy efficiency.
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 9: Number of Designated Energy Users (DEUs)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEUs List)
Number of DEUs
Energy using of DEUs (kTOE)

## Slide 10: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 11
Primary energy
In 2020, Vietnam's TPES was estimated at 95,762 KTOE, increased by only 1.5% compared with the previous year.
1
Primary energy use
The export output in 2019 was only 8,834 KTOE, a 2.4-fold decrease compared to 2010.
In 2019, energy imports reached 44,342 KTOE, a 39.6% increase compared to 2018.
2
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 12
Energy Intensity by Country
Considering population size, Vietnam's TPES per capita in 2018 was relatively low at only 848 kgOE/person, even lower than the ASEAN average of 1,041 kgOE/person. However, the TPES intensity per GDP was quite high. This indicates that Vietnam's energy efficiency needs improvement.
3
Amount of energy needed to produce one unit of economic output. A lower number means that economies produce economic value in a less energy-intensive way.
4
Energy intensity, 2000 to 2020
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 13: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 14: Specific Energy consumption and Energy Savings Potential
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report

## Slide 15: Current status of energy use in industry
Proportion of energy consumption: The industrial sector accounts for about 47% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, and chemical industries.
  These industries consume approximately 70% of the total energy in the industrial sector.
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.

## Slide 16: Energy consumption structure in the industry
Proportion of energy consumption by sector:
  Manufacturing sector: 60%
  Construction sector: 15%
  Mining sector: 10%
  Transportation and logistics sector 5%
Main types of energy used:
  Electricity: Account for the largest proportion in the energy consumption structure of the industrial sector.
  Oil and natural gas: Used in manufacturing and chemical industries.
  Coal: Mainly used in the cement and metallurgy industries.

## Slide 17: Causes of high energy consumption
Outdated technology: Many enterprises still use old technology, which consumes high amounts of energy and causes environmental pollution.
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology.
Low awareness of energy efficiency: Some enterprises have not prioritized energy efficiency measures in their production processes.

## Slide 18: Challenges in energy management and utilization
Technological challenges: Many enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among enterprises.

## Slide 19: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating, especially in industries such as textiles and electronics.
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the industrial development of Vietnam.

## Slide 20
EE potential in cement industry

## Slide 21: Energy Intensity in Key Industries in Vietnam
Figure: Energy Intensity Improvement in Key Industries during VNEEP Phase 2 Changes of energy intensity in key industries

## Slide 22: The average thermal energy intensity of clinker
Global thermal energy intensity of clinker production by fuel in the Net Zero Scenario, 2010-2030
Fossil fuels continued to be the main source of thermal energy for the sector (90% share) in 2022, followed by bioenergy and renewable waste (4%) and non-renewable waste (4%). The adoption of low carbon fuels is key to reduce the share of fossil fuels to 79% and non-renewable waste to 3% by 2030 in line with the NZE Scenario, which sees bioenergy and renewable waste increasing to 16% and hydrogen to 2% of the total thermal energy share.

## Slide 23: Energy Consumption in the Cement Industry
The Vietnamese cement industry consumes a significant amount of energy, primarily in the form of thermal energy and electricity.
The energy consumption structure for cement production is as follows: approximately 80-85% is thermal energy, 15-20% is electricity, and a small portion (around 1%) is from DO (diesel oil) and FO (fuel oil).
It is estimated that electricity costs account for 10-15% of the cement production cost.
Electricity consumption ranges from 77.3 kWh to 108 kWh per ton of cement produced. This variation depends on the technology and equipment used in the plants.

## Slide 24: Energy Efficiency Solutions in the Cement Industry
Optimize the Clinker Production Process:
Use high-efficiency kilns (pre-calciner).
Reduce heat loss by improving insulation.
Optimize kiln operation using simulation software.
Waste Heat Recovery for Power Generation (WHR)
Recover waste heat from the kiln and clinker cooler.
Apply advanced technologies such as the ORC system (Organic Rankine Cycle).
Benefits: Save 20-30% of electricity consumption, reduce emissions

## Slide 25: Energy Efficiency Solutions in the Cement Industry
Use of Alternative Fuels
Biomass fuels: Wood pellets, straw, rice husks.
Co-processing of waste: Tires, household waste.
Benefits: Reduce costs and CO₂ emissions.
Grinding Technology Improvement
Use vertical mills instead of ball mills.
Install variable frequency drives (VFDs) to reduce electricity consumption.
Benefits: Save 20-30% of electricity consumption.
Effective Equipment Management and Maintenance
Regular maintenance to maintain equipment performance.
Install an energy consumption monitoring system.
Benefits: Reduce energy waste.

## Slide 26: Energy Efficiency Solutions in the Cement Industry
Establish an Energy Management System (ISO 50001)
Set up energy policies and goals.
Evaluate and continuously improve.
Benefits: Reduce energy consumption by 5-10%.
Improving the Cement Production Process
Reduce clinker ratio by using additives (fly ash, blast furnace slag).
Produce non-fired cement.
Benefits: Reduce energy consumption and emissions.
Application of Smart Technologies
Automation and intelligent control.
Use Big Data analytics to optimize processes.
Benefits: Optimize the process, reducing waste.

## Slide 27: Energy Efficiency measures in the Cement Industry
CO2 emitted and captured in the cement sector and clinker-to-cement ratio in the Net Zero Scenario, 2015-2030

## Slide 28: Example of EEMs in the world
Chemical absorption, partial capture rates (less than 20%)
Technology description
Chemical absorption of CO2 is a common process operation based on the reaction between CO2 and a chemical solvent (e.g. amine-based). The CO2 is released at temperatures typically in the range 120 °C to 150 °C and the solvent is regenerated for further operation. It can be applied to kilns, the main unit producing clinker for cement production.
Relevance for net zero
CO2 capture and storage is a key technology to reduce otherwise difficult to avoid process emissions from cement production. Most alternative CCS technologies are more costly and/or at earlier stages of development, while other lower emission alternatives for producing cement, such as alternative binding materials, face challenges such as low TRL or limitations in raw material availability. However, higher capture rates should be targeted.

## Slide 29
Demonstration projects
Germany: Heidelberg Linde CCS: In April 2023, Heidelberg Materials partnered with engineering company Linde to install a 70 kt carbon capture system at its 1Mt/yr Lengfurt cement plant by 2025.
Spain: ECCO2 LafargeHolcim Carboneras cement factory: LafargeHolcim España, Carbon Clean and Sistemas de Calor have created ECCO2, a joint venture for the development of an advanced technology CO2 capture plant at the Carboneras cement factory (Almeria). The three companies have been working on the project since the end of 2020, in order to assess its technical feasibility and benefits for the local community. The plant is expected to be operational in early 2023. (Source)
United States: Capitol Aggregates: Commercial-scale post-combustion carbon capture and utilisation (CCU) facility opened in 2014 at Capitol Aggregates plant in Texas, capturing 15% of cement production emissions (75 kt CO2/yr) for use in materials such as baking soda, bleach and hydrochloric acid.
Source: https://www.osti.gov/servlets/purl/1241314
Example of EEMs in the world

## Slide 30
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU