## Slide 1: TRAINING PROGRAME for IEs
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
for: Enterprise leaders

## Slide 2: Training program for business leaders
TIME | Content
8.00 – 8.30 | Registration
8.30 – 8.40 | Opening Remarks
8.40 – 9.45 | Module 1: Project introduction Policy introduction: energy saving, greenhouse gas emission reduction, gender issues related in EE
9.45 – 10.00 | Breaks
10.00– 11.00 | Module 2. Relations between energy, environment and production and business, use of clean energy
11.00 – 11.45 | Module 3. The current situation of energy use and potential of industrial waste in Vietnam (cement, steel, seafood processing, brick and ceramic, textiles, beverages, paper and pulp, other industries (plastics...)
11.45 – 12.00 | Discuss
12.00 – 13.30 | Lunch
13.30 – 14.15 | Module 4. Energy Management, Energy Management System
14.15 – 15.00 | Module 5. EE project financing and VSUEE project financing approach
15.00 – 15.15 | Breaks
15.15 – 16.15 | Component 6. Case study in EE for Manufacturing Industry: Cement, Steel, Seafood Processing, Brick and Ceramic, Textile, Beverage, Paper & Pulp, Other Industries (Plastics...)
16.15 – 16.45 | Discuss
16.45 – 17.00 | Closing

## Slide 3
Module 3.
Current and potential of EE in brick and ceramic industries in Vietnam
TRAINING PROGRAME for IEs
for: Enterprise leaders

## Slide 4: Global industrial energy usage
Total Final Energy Consumption (TFC) by Sector from 1990 to 2020-2022
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 5: Final electricity consumption by sector in Vietnam

## Slide 6: Final energy consumption by industry in Vietnam
Transportation
31,7%
Services
3,9%
Household 14,9 %
Non- energy
2%
Industry
45,7%
Argriculture
1,8 %
2012
2021
Industry
Non- energy
5,5%
Argriculture
5,2%
Transportation
16,7%
Services
3,2%
Household
15,3 %

## Slide 7: Current status of energy use in Vietnam
Agriculture, forestry and fisheries
Construction
Industry
Non- energy
Household
Services
Transportation

## Slide 8: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3,068 DEUs (up from 2,496 in 2017), consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority—2,599 facilities consuming 50,570,115 TOE. The Vietnamese industry has significant potential for energy efficiency.
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 9: Number of Designated Energy Users (DEUs)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEUs List)
Number of DEUs
Energy using of DEUs (kTOE)

## Slide 10: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 11
Primary energy
In 2020, Vietnam's TPES was estimated at 95,762 KTOE, increased by only 1.5% compared with the previous year.
1
Primary energy use
The export output in 2019 was only 8,834 KTOE, a 2.4-fold decrease compared to 2010.
In 2019, energy imports reached 44,342 KTOE, a 39.6% increase compared to 2018.
2
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 12
Energy Intensity by Country
Considering population size, Vietnam's TPES per capita in 2018 was relatively low at only 848 kgOE/person, even lower than the ASEAN average of 1,041 kgOE/person. However, the TPES intensity per GDP was quite high. This indicates that Vietnam's energy efficiency needs improvement.
3
Amount of energy needed to produce one unit of economic output. A lower number means that economies produce economic value in a less energy-intensive way.
4
Energy intensity, 2000 to 2020
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 13: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 14: Specific Energy consumption and Energy Savings Potential
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report

## Slide 15: Current status of energy use in industry
Proportion of energy consumption: The industrial sector accounts for about 47% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, and chemical industries.
  These industries consume approximately 70% of the total energy in the industrial sector.
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.

## Slide 16: Energy consumption structure in the industry
Proportion of energy consumption by sector:
  Manufacturing sector: 60%
  Construction sector: 15%
  Mining sector: 10%
  Transportation and logistics sector 5%
Main types of energy used:
  Electricity: Account for the largest proportion in the energy consumption structure of the industrial sector.
  Oil and natural gas: Used in manufacturing and chemical industries.
  Coal: Mainly used in the cement and metallurgy industries.

## Slide 17: Causes of high energy consumption
Outdated technology: Many enterprises still use old technology, which consumes high amounts of energy and causes environmental pollution.
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology.
Low awareness of energy efficiency: Some enterprises have not prioritized energy efficiency measures in their production processes.

## Slide 18: Challenges in energy management and utilization
Technological challenges: Many enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among enterprises.

## Slide 19: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating, especially in industries such as textiles and electronics.
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the industrial development of Vietnam.

## Slide 20
Brick & Ceramic Industry in Vietnam

## Slide 21: The current situation of fired brick production
Current State of Fired Brick Production
Number of production facilities: Approximately 4,000 clay brick manufacturing facilities with a total designed capacity of about 25 billion bricks per year.
Annual production: Estimated to reach 60-70% of the total designed capacity.
Geographical distribution: Mainly concentrated in the Red River Delta, Central Vietnam, and Southeastern regions.
Shift Towards Non-Fired Brick Production
Number of non-fired brick production facilities: Approximately 2,500 facilities with a total designed capacity of about 15 billion standard bricks per year.
Annual production: Estimated to reach 50-60% of the total designed capacity.
Benefits:
Reduces clay consumption.
Saves energy.
Lowers CO₂ emissions.
Contributes to environmental protection.

## Slide 22: Comparison of fired bricks and non-fired bricks
Criteria | Fired bricks | Non-fired bricks
Material | Clay | Industrial waste, cement, sand
Production technology | Đốt ở nhiệt độ cao | Pressing, vibrating, not overheated
Environmental Impact | High (CO₂ emissions, air pollution) | Low (emission reduction, environmental protection)
Production costs | Lower | Higher
Product Quality | High strength, good bearing | Variety, sound insulation, good heat insulation

## Slide 23: State Policies and Regulations
Decision 2171/QĐ-TTg (2021):
The program for the development of non-fired construction materials in Vietnam until 2030 aims to reduce the use of fired clay bricks and lower CO₂ emissions.
Circular 13/2017/TT-BXD:
Regulation on the use of non-fired construction materials in building projects.

## Slide 24: Overview of the Ceramic Industry in Vietnam
Vietnam’s ceramic industry has a long history, playing a significant role in the country’s culture and economy.
The diversity of ceramic types reflects the richness of art and practical applications.
Vietnam has approximately 2,000 traditional craft villages, including renowned ceramic-producing villages like Bát Tràng, Chu Đậu, and Phù Lãng.
Vietnamese ceramic products are exported to major markets such as the United States, Japan, and the EU, with export turnover reaching $711 million in 2022.

## Slide 25: Types of Ceramics in Vietnam
Types of Ceramics in Vietnam
Household Ceramics: Bowls, plates, cups, teapots, and vases.
Decorative Ceramics: Statues, bas-reliefs, ceramic lamps, and screens.
Construction Ceramics: Roof tiles, floor tiles, and wall tiles.
Artisan Ceramics: Artistic creations and souvenirs.
Technical Ceramics: Insulating porcelain products, sanitary ware, and other technical ceramic items.
Development Solutions for the Ceramic Industry
Artisan Training: Preserve and promote traditional techniques.
Technological Innovation: Adopt advanced production technologies.
Market Expansion: Strengthen trade promotion and participate in international fairs.
Craft Village Tourism Development: Combine ceramic production with experiential tourism.

## Slide 26: Fired Brick Production Technology
Handmade Kilns: Completely phased out due to outdated technology and environmental pollution.
Improved Ring Kiln: Uses plastic clay, but its longevity is limited due to the depletion of raw materials.
Modern Tunnel Kiln: Uses riverbank soil and hillside clay; high productivity, good quality, highly automated, and energy-efficient. The modern tunnel kiln is characterized by the modernization of the shaping process, with robots handling the bricks when entering and exiting the kiln. The modern tunnel kiln is divided into three types:
1. Traditional Tunnel Kiln Technology: Built with an improved flat roof and wide kiln chamber.
2. Moving Tunnel Kiln: Designed to move along tracks, allowing bricks to be arranged in a circular fixed pattern and moved sequentially through the kiln.
3. Moving Roof Tunnel Kiln: The kiln is designed as a rectangular structure buried underground. The roof panels are movable to cover the fixed rows of bricks.

## Slide 27: Fired Brick Production Technology
Old-style Tunnel Kiln with an arched roof made of refractory bricks and a narrow kiln chamber.

## Slide 28: Fired Brick Production Technology
New type Tuynel brick kiln with flat ceiling made of ceramic cotton pressed wide furnace

## Slide 29: Fired Brick Production Technology
Movable Tuynel Oven

## Slide 30: Fired Brick Production Technology
Portable Flat Ceiling Tube Oven

## Slide 31: Energy used in fired brick production:
Coal: Accounts for over 80% of the energy source, used for firing bricks.
Wood and agricultural by-products: Used to start the kiln and supplement heat at some facilities with available resources.
Electricity: Used to operate production equipment.
Energy consumption by kiln types:
• Hand kilns: 1,200-1,500 kcal/kg of brick.
• Ring kilns and old tunnel kilns: 700-900 kcal/kg of brick.
• New tunnel kilns and moving tunnel kilns, flat roof moving tunnel kilns: 400-600 kcal/kg of brick.
The significant differences between technologies show the potential for energy savings.

## Slide 32: EEMs in fired brick production
Technology improvements:
Transition to advanced kiln technologies such as flat roof tunnel kilns, moving tunnel kilns, and moving flat roof tunnel kilns.
Use of advanced product shaping processes with semi-dry extrusion lines, reducing energy needs for water evaporation.
Optimization of the drying process to minimize the impact of weather factors and better utilize solar energy for drying.
Implement energy balancing for kilns to identify opportunities to reduce heat losses during firing and better utilize heat between drying, heating, firing, and cooling stages.

## Slide 33: EEMs in fired brick production
Use of Renewable Energy: Traditional kilns previously used a lot of biomass energy. In modern technologies, coal is the primary fuel. Efforts should be made to use biomass fuels (rice husks, sawdust, and other agricultural residues) in modern kilns to supplement heat in the firing process.
Automatic Control System: Monitor and adjust the temperature in the kiln. This reduces energy waste caused by operational errors.
Enhanced Insulation: Use high-quality insulation materials in the firing and drying systems to minimize energy loss.
Energy Management System (EMS): Track energy consumption in real-time. Identify and address points of inefficiency in energy use.

## Slide 34: EEMs in fired brick production
Replace Traditional Kilns with Gas or Gas-Electric Hybrid Kilns:
• Reduce energy consumption by 30-50%.
• Better temperature control reduces the occurrence of defective products.
• Decrease environmental pollution.
Heat Recovery from Firing Kilns:
• Use excess heat to dry products before firing.
• Reduces energy consumption during the drying process.
Biomass Gasification:Rice husks, sawdust, cashew shells, and agricultural waste are renewable, inexpensive, and environmentally friendly energy sources. However, the use of raw biomass can impact product quality. The gasification process helps convert solid fuels into higher-quality gaseous fuels.

## Slide 35: EEMs in fired brick production
Automatic Control System:
Monitor and adjust the temperature and air flow in the kiln.
Reduce energy waste caused by operational errors.
Modern Machinery: Automatic clay pressing and mixing machines help reduce electricity and fuel consumption.
Energy Management System (EMS):
Track real-time energy consumption.
Analyze and eliminate unnecessary energy consumption points.

## Slide 36: EEMs in brick industry in the world
Induction (high temperature heating)
Technology description
During induction, an electromagnetic field is generated when AC current flows through an inductor: this induces a current flow in a conductive material appositely placed nearby. The higher the current flow, the more the heat generated inside the object itself. If the field is raised enough to overcome the melting point, the material changes phase: this technology is used commonly for the melting of metals. While already commercial for some applications, research and development could expand the range of applications, further improve efficiency and reduce costs.
Relevance for net zero
High- to medium-temperature heat (greater than 100 °C) in industry is currently supplied mostly by fossil fuels. This technology can replace fuel-fired ovens in several processes, reducing on-site emissions. The use of renewable electricity can enable a CO2-free heating process. Since induction furnaces are already commercial in some applications, they could provide good potential for further development for other applications.

## Slide 37: EEMs in brick industry in the world
Induction (high temperature heating)
Initiatives
Austria: NEFI - Greenbricks: Implementing an industrial-scale concept of a carbon-neutral brick factory based on an innovative, high temperature tunnel kiln for brick firing driven by green electricity to be integrated with a set of energy efficiency measures. One of the main aims of this project is reduce emissions by 88% (7.3kt) CO2-eq/year and reduce the primary energy demand for brick production up to 25%.
Source: https://www.nefi.at/en/project/GreenBricks
@ wienerberger/Manfred Fesl

## Slide 38: Benefits of Energy Saving in Ceramic Production
Economic: Reduces production costs, increases profits.
Environmental: Decreases greenhouse gas emissions, protects the living environment.
Social: Creates a safer working environment, raises community awareness.
Market: Enhances competitiveness in the international market.

## Slide 39: Conclusion and Recommendations
Conclusion:
EE in fired brick production is a key factor for sustainable development.
The adoption of modern technologies and efficient energy management will yield significant benefits.
Recommendations:
Encourage businesses to switch to tunnel kilns and EE technologies.
Enhance financial support policies and EE training.
Research and apply renewable fuel sources in production.

## Slide 40: Conclusion and Recommendations
Conclusion:
EE is a core element for the sustainable development of the ceramic production industry.
Technology conversion and efficient energy management will bring economic, environmental, and social benefits.
Recommendations:
Strengthen policies to support businesses investing in new technologies.
Increase research and development of alternative fuel sources.
Organize EE training programs for ceramic production businesses.

## Slide 41
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU