## Slide 1: TRAINING PROGRAME for IEs
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
for: Enterprise leaders

## Slide 2: Training program for business leaders
TIME | Content
8.00 – 8.30 | Registration
8.30 – 8.40 | Opening Remarks
8.40 – 9.45 | Module 1: Project introduction Policy introduction: energy saving, greenhouse gas emission reduction, gender issues related in EE
9.45 – 10.00 | Breaks
10.00– 11.00 | Module 2. Relations between energy, environment and production and business, use of clean energy
11.00 – 11.45 | Module 3. The current situation of energy use and potential of industrial waste in Vietnam (cement, steel, seafood processing, brick and ceramic, textiles, beverages, paper and pulp, other industries (plastics...)
11.45 – 12.00 | Discuss
12.00 – 13.30 | Lunch
13.30 – 14.15 | Module 4. Energy Management, Energy Management System
14.15 – 15.00 | Module 5. EE project financing and VSUEE project financing approach
15.00 – 15.15 | Breaks
15.15 – 16.15 | Component 6. Case study in EE for Manufacturing Industry: Cement, Steel, Seafood Processing, Brick and Ceramic, Textile, Beverage, Paper & Pulp, Other Industries (Plastics...)
16.15 – 16.45 | Discuss
16.45 – 17.00 | Closing

## Slide 3
Module 3.
Current and potential of EE in the seafood industry in Vietnam
TRAINING PROGRAME for IEs
for: Enterprise leaders

## Slide 4: Global industrial energy usage
Total Final Energy Consumption (TFC) by Sector from 1990 to 2020-2022
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 5: Final electricity consumption by sector in Vietnam

## Slide 6: Final energy consumption by industry in Vietnam
Transportation
31,7%
Services
3,9%
Household 14,9 %
Non- energy
2%
Industry
45,7%
Argriculture
1,8 %
2012
2021
Industry
Non- energy
5,5%
Argriculture
5,2%
Transportation
16,7%
Services
3,2%
Household
15,3 %

## Slide 7: Current status of energy use in Vietnam
Agriculture, forestry and fisheries
Construction
Industry
Non- energy
Household
Services
Transportation

## Slide 8: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3,068 DEUs (up from 2,496 in 2017), consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority—2,599 facilities consuming 50,570,115 TOE. The Vietnamese industry has significant potential for energy efficiency.
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 9: Number of Designated Energy Users (DEUs)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEUs List)
Number of DEUs
Energy using of DEUs (kTOE)

## Slide 10: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 11
Primary energy
In 2020, Vietnam's TPES was estimated at 95,762 KTOE, increased by only 1.5% compared with the previous year.
1
Primary energy use
The export output in 2019 was only 8,834 KTOE, a 2.4-fold decrease compared to 2010.
In 2019, energy imports reached 44,342 KTOE, a 39.6% increase compared to 2018.
2
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 12
Energy Intensity by Country
Considering population size, Vietnam's TPES per capita in 2018 was relatively low at only 848 kgOE/person, even lower than the ASEAN average of 1,041 kgOE/person. However, the TPES intensity per GDP was quite high. This indicates that Vietnam's energy efficiency needs improvement.
3
Amount of energy needed to produce one unit of economic output. A lower number means that economies produce economic value in a less energy-intensive way.
4
Energy intensity, 2000 to 2020
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 13: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 14: Specific Energy consumption and Energy Savings Potential
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report

## Slide 15: Current status of energy use in industry
Proportion of energy consumption: The industrial sector accounts for about 47% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, and chemical industries.
  These industries consume approximately 70% of the total energy in the industrial sector.
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.

## Slide 16: Energy consumption structure in the industry
Proportion of energy consumption by sector:
  Manufacturing sector: 60%
  Construction sector: 15%
  Mining sector: 10%
  Transportation and logistics sector 5%
Main types of energy used:
  Electricity: Account for the largest proportion in the energy consumption structure of the industrial sector.
  Oil and natural gas: Used in manufacturing and chemical industries.
  Coal: Mainly used in the cement and metallurgy industries.

## Slide 17: Causes of high energy consumption
Outdated technology: Many enterprises still use old technology, which consumes high amounts of energy and causes environmental pollution.
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology.
Low awareness of energy efficiency: Some enterprises have not prioritized energy efficiency measures in their production processes.

## Slide 18: Challenges in energy management and utilization
Technological challenges: Many enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among enterprises.

## Slide 19: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating, especially in industries such as textiles and electronics.
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the industrial development of Vietnam.

## Slide 20
Seafood industry

## Slide 21: Energy Intensity in Key Industries in Vietnam
Figure: Energy Intensity Improvement in Key Industries during VNEEP Phase 2 Changes of energy intensity in key industries

## Slide 22: Benchmarking in the Seafood Industry
Benchmarking | Other Relevant Requirements
According to Article 6 of Circular 52/2018/TT-BCT, benchmarks for the seafood processing sector up to the end of 2025 are as follows: | 
- Industrial processing of catfish products: 1,050 kWh/ton of equivalent product - Industrial processing of shrimp products: 2,050 kWh/ton of equivalent product | Facilities exceeding the SEC benchmark must develop and implement an EE improvement plan to meet the benchmarks stated in Article 5 of Circular 52/2018/TT-BCT. DOITs must be reported to annually by January 15 regarding the status of benchmark implementation. Facilities with SEC higher than the benchmarks must also report their EE improvement plans, including proposed EEMs and implementation plans, in accordance with Clause 1, Article 6 of Circular 52/2018/TT-BCT.

## Slide 23: EEMs in the seafood processing industry
Heat Recovery from Cooling Systems for Hot Water Production
Process:
Install heat exchangers in the cooling system to recover waste heat from the refrigeration compressors.
This recovered heat is used to heat water for sanitation and processing activities.
Integrate the heat exchanger with the existing system, minimizing installation time and costs.
Manage heat recovery through an automated system to ensure efficient utilization of thermal energy.
Benefits:
Saves energy used for heating water, reducing fuel or electricity consumption.
Shortens the payback period for the investment to 1.4–2.2 years.

## Slide 24: EEMs in the seafood processing industry
Direct Use of Chilled Water Instead of Flake Ice
Process:
Replace the use of flake ice with a direct cooling system that supplies chilled water at 2–5°C.
The chilled water can be reused in cooling processes for raw materials or finished products.
Implement a recirculation system to minimize water and energy waste.
Optimize the flow of chilled water to each production stage to prevent excess cooling energy usage.
Benefits:
Saves electricity consumption ranging from 220,000 to 660,000 kWh/year, depending on the plant’s scale.
Reduces operational costs and CO₂ emissions.

## Slide 25: EEMs in the seafood processing industry
Optimizing Refrigeration Systems
Optimization Steps:
Regularly inspect and maintain refrigeration equipment, such as compressors, evaporators, and condensers.
Install temperature and pressure sensors to monitor cooling performance and promptly detect issues.
Adjust and maintain storage, freezing, and refrigeration temperatures to match specific product requirements.
Use high-efficiency evaporator fans and regulate fan flow according to actual thermal loads.
Benefits:
Enhances cooling efficiency and reduces energy consumption by 20–30%.
Lowers operational and maintenance costs.

## Slide 26: EEMs in the seafood processing industry
Using High-Efficiency LED Lighting
Implementation:
Replace fluorescent or halogen bulbs with high-efficiency LED lighting throughout the factory.
Install automatic light sensors to adjust brightness based on production activity and ambient light levels.
Benefits:
Reduces electricity costs for lighting.
Saves 15–20% energy and extends the lifespan of lighting equipment.

## Slide 27: EEMs in the seafood processing industry
Optimizing the Steam System
Implementation:
Regularly maintain the boiler system to remove deposits and improve heat exchange efficiency.
Install economizers to recover heat from exhaust gases to preheat boiler feedwater.
Use effective insulation materials for steam pipelines, valves, and storage tanks.
Recover condensate from the steam system for reuse, reducing the need for new water and heating energy.
Benefits:
Reduces fuel consumption by 15–20%.
Increases boiler efficiency by 3–10%, extending equipment lifespan.

## Slide 28: EEMs in the seafood processing industry
Optimizing the Compressed Air System
Implementation:
Inspect and repair air leaks to prevent wastage, as leaks can account for 20–30% of total energy consumption.
Install variable frequency drives (VFDs) to adjust compressor speed based on actual demand, reducing energy use during low loads.
Optimize system operating pressure to match equipment requirements without exceeding necessary levels.
Recover waste heat from air compressors for use in activities like water heating or space heating.
Benefits:
Saves 15–35% of electricity consumption.
Recovers 50–90% of waste heat, reducing additional energy costs.

## Slide 29: EEMs in the seafood processing industry
Implementing an Energy Management System According to ISO 50001
Implementation Steps:
Establish an energy management system (EnMS) to monitor and optimize energy usage across the facility.
Set specific energy-saving targets, measure performance, and implement continuous improvements.
Integrate energy-saving criteria into the Key Performance Indicators (KPIs) of each department.
Conduct employee training on energy-saving awareness and techniques.
Benefits:
Reduces energy consumption by 5–20%.
Enhances production efficiency while meeting international environmental standards.

## Slide 30: EEMs in the seafood industry in the world
Whitby Seafoods' Energy Efficiency Initiatives
Company: Whitby SeafoodsLocation: United Kingdom (https://www.whitby-seafoods.com/)
Industry: Seafood Processing
Background: Whitby Seafoods, a leading UK scampi producer, faced challenges in monitoring and managing energy consumption across its manufacturing operations. With rising energy costs and a commitment to sustainability, the company sought to gain detailed insights into its energy usage to identify inefficiencies and implement corrective measures.

## Slide 31: EEMs in the seafood industry in the world
Implemented Measures: Deployment of RS Industria Monitoring System.
Whitby Seafoods collaborated with RS Industria to install a continuous energy monitoring system across 49 energy-intensive assets, including equipment in the cold storage, ammonia plant room, and packing and coating lines. This system enabled real-time data collection on energy consumption.
Results
Enhanced Visibility: The monitoring system provided detailed insights into energy consumption at the site, line, and asset levels, enabling more informed decision-making.
Rapid Identification of Inefficiencies: The real-time data allowed for the swift detection of inefficiencies, such as equipment running unnecessarily during non-production periods, leading to prompt corrective actions.
Promotion of Energy-Saving Culture: The initiative fostered greater awareness among employees regarding energy usage, encouraging behaviors aligned with the company's sustainability goals.
Source: rs-industria.com

## Slide 32
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU