## Slide 1: TRAINING PROGRAME for IEs
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
for: Enterprise leaders

## Slide 2: Training program for business leaders
TIME | Content
8.00 – 8.30 | Registration
8.30 – 8.40 | Opening Remarks
8.40 – 9.45 | Module 1: Project introduction Policy introduction: energy saving, greenhouse gas emission reduction, gender issues related in EE
9.45 – 10.00 | Breaks
10.00– 11.00 | Module 2. Relations between energy, environment and production and business, use of clean energy
11.00 – 11.45 | Module 3. The current situation of energy use and potential of industrial waste in Vietnam (cement, steel, seafood processing, brick and ceramic, textiles, beverages, paper and pulp, other industries (plastics...)
11.45 – 12.00 | Discuss
12.00 – 13.30 | Lunch
13.30 – 14.15 | Module 4. Energy Management, Energy Management System
14.15 – 15.00 | Module 5. EE project financing and VSUEE project financing approach
15.00 – 15.15 | Breaks
15.15 – 16.15 | Component 6. Case study in EE for Manufacturing Industry: Cement, Steel, Seafood Processing, Brick and Ceramic, Textile, Beverage, Paper & Pulp, Other Industries (Plastics...)
16.15 – 16.45 | Discuss
16.45 – 17.00 | Closing

## Slide 3
Module 6:
Typical report on energy efficiency in steel industry in Vietnam
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
TRAINING PROGRAME for IEs
for: Enterprise leaders

## Slide 4
Steel manufacturing industry

## Slide 5: Content
The facility’s information on the case study
Energy efficiency measures
Notes: Hợp đồng hiệu quả năng lượng (EPC): là hợp đồng ký kết giữa ESCO và Khách hàng để thực hiện dịch vụ sử dụng năng lượng tiết kiệm và hiệu quả.
– Hợp đồng chia sẻ mức tiết kiệm năng lượng: ESCO chịu mọi rủi ro tài chính và kỹ thuật của dự án bằng cách thu xếp tài chính để thực hiện dự án đầu tư lắp đặt các trang thiết bị hiệu quả năng lượng tại cơ sở sử dụng năng lượng của khách hàng
– Hợp đồng đảm bảo mức tiết kiệm năng lượng: ESCO chịu trách nhiệm cung cấp, thiết kế, lắp đặt, đo lường và đảm bảo hiệu quả giải pháp sử dụng năng lượng tiết kiệm và hiệu quả cho khách hàng.

## Slide 6
Main production sector: Production of galvanized steel pipes, steel tubes
Main products: Galvanized steel pipes, galvanized sheets
Main energy equipment: Transformer station, compressed air station, coal used for boilers
1. General information

## Slide 7
Hot Rolling Process
1. Material Loading
2. Flattening
3. Roughing Mill
4. Slitting
5. Roughing Mill
6. Tensioning
7. Coiling
8. Material Unloading
1. Production line
Descaling Process
1. Material Loading
2. Pickling Tank 1
3. Pickling Trough
4. Rinsing Trough
5. Drying
6. Tensioning 1
7. Pickling Tank 2
8. Tensioning 2
9. Coiling
10. Material Unloading

## Slide 8
Cold Rolling Process
1. Material Loading
2. Pickling Tank
3. Stand 1
4. Stand 2
5. Stand 3
6. Stand 4
7. Coiling
8. Material Unloading
Annealing Process
1. Material Loading
2. Roughing Mill 1
3. Annealing Furnace
4. Rapid Cooling
5. Annealing Tank
6. Rapid Cooling Tower
7. Roughing Mill 2
8. Coiling
9. Material Unloading
Pipe Making Process
1. Uncoiling
2. Pickling Tank
3. Forming Roll Stand
4. High-Frequency Welding
5. Shaping Roll Stand
6. Cutting Table
7. Pipe Collection
8. Bundling
1. Production line

## Slide 9
Types of energy used in the production line
Electricity is used for almost all equipment in the production line and
auxiliary systems such as lighting systems, air conditioning systems, compressors, etc…
Diesel oil (DO) is used to operate backup generators, forklifts, fire pumps, and internal vehicles..
1. Production line

## Slide 10: 1. Energy supply system
Types of energy used in the production line
The company's electricity supply is sourced from a 22/0.4 kV grid via three transformers.
Install automatic reactive power compensation cabinets to improve the power factor
Electrical system
Picture of the transformer station.
The factory has two compressed air systems serving the valve control mechanisms of the production line.
Fusheng air compressor
Compressed Air System

## Slide 11
The heating system consists of one boiler that supplies heat for certain production stages.
The control method is based on the negative pressure inside the boiler and does not rely on O2 concentration. The control mode is managed by adjusting the pressure and temperature at different time points. Fuel is supplied to the boiler separately, following a load-balancing mode.
1. Energy supply system
Heating system.

## Slide 12
2. Energy efficiency measure 1
Enhance internal management and equipment maintenance
For the electrical equipment system.
Regularly propagandize and train staff on energy efficiency. Enhance the participation of operational staff (energy efficiency should be based on a broad foundation and supported by the operational staff).
Monitor energy consumption according to production and non-production days to identify and fix energy losses. Develop procedures and checklists to ensure that equipment shutdowns are properly carried out.
Install automatic control devices to turn off equipment when not in use.
Turn off all unnecessary electrical devices (e.g., during breaks, lunch hours, and shift changes).

## Slide 13
2. Energy efficiency measure 1
For the refrigeration system and office air conditioning
Minimize heat load
Regularly inspect and assess the air conditioning system to ensure it is not overloaded.
Set the air conditioning system temperature to an appropriate level (26°C to 27°C in summer; avoid setting it too low or too high).
Review the operating mode regularly according to recommendations and changes in weather conditions.
For the compressed air system.
Train and raise employees' awareness to operate and maintain the compressed air system effectively.
Ensure that condensate is removed from the distribution system immediately or that there is no condensate.
Regularly maintain and clean air filtration equipment
Carry out regular maintenance and inspections.
Strengthen internal management and equipment maintenance
For the office area.
Check and seal any gaps that cause heat loss to the outside of the room.
Turn off all lighting equipment when not in use or after working hours
Use curtains on both the inside and outside of windows to retain heat in the winter and cool the space in the summer.

## Slide 14
Monitor and address air leakage points
Current situation: Through the survey and inspection of air leakages in the company's compressor stations, the auditing unit detected leaks at control valves, fittings, and pneumatic cylinder valve mechanisms.
Proposed solution
Develop operational rules and requirements for compressed air machine operators.
Regularly inspect the compressed air systems.
2. Energy efficiency measure 2

## Slide 15
Inspection, monitoring and handling of compressed air leak points
Leak Testing Equipment
STT | Parameter | Unit | Value
 | Electricity price information |  | 
1 | Average electricity prices in 2022 | VNĐ/kWh | 1.599
 | Operating Information |  | 
2 | Average Operating Hours in a Year | h/năm | 8520
 | Device Status Information |  | 
3 | Power consumption before implementing the solution | kWh/year | 2.300.400
4 | Solution investment costs | million VNĐ | 62,0
 | Calculation energy saving |  | 
5 | Savings rate after implementing the solution | % | 2,5
6 | Electricity consumption after implementing the solution | kWh/year | 2.242.890
7 | Electricity saved after implementing the solution | kWh/year | 57.510
8 | Income brought by EEMs in 1 year | million VNĐ | 91,958
9 | Simple payback period | month | 8,1
10 | Reduce CO2 emissions | ton/year | 42
Brand: Allsun Model: EM282 40kHz ± 2kHz frequency response Operating Temperature 0 – 40°
Compressed air leak deployment cost estimate table
2. Energy efficiency measure 2

## Slide 16
Install a flow control system to save electricity.
Current status: The factory's compressed air system includes 10 air compressors that control the opening and closing of valves in the production line and supply air for certain production processes.
Proposed solutions: The Intelligent Flow Control (IFC) system helps reduce energy losses during idle mode, ensures continuous and stable compressed air pressure at the end-use points, and saves compressed air energy by reducing artificial demand. It also allows easy monitoring of compressed air signals, enabling the implementation of optimal operating methods.
2. Energy efficiency measure 3
Installation diagram of the IFC equipment system at the outlet of the air compressor station
Installation diagram of the IFC equipment system at the outlet of the air compressor station
air compressors
Air treatment
Actual installation image of IFC equipment system

## Slide 17
2. Energy efficiency measure 3
TT | PARAMETER | UNIT | VALUE
 | Electricity price information |  | 
1 | Average electricity prices in 2022 | VNĐ/kWh | 1.599
 | Operating Information |  | 
2 | Average Operating Hours in a Year | h/year | 8.520
 | Device Status Information |  | 
3 | Total actual operating capacity of the compressed air system | kW | 91
4 | Power consumption before implementing the solution | kWh/year | 775.320
5 | Total investment cost to implement the solution | Million VNĐ | 364
 | Calculation energy saving |  | 
6 | Percentage of system savings when implementing the solution | % | 10.0
7 | Electricity consumption after implementing the solution | kWh/year | 697.788
8 | Electricity saved after implementing the solution | kWh/year | 77.532
9 | Income brought by EEMs in 1 year | Million VNĐ/year | 124,0
10 | Simple payback period | month | 35,2
11 | Project lifespan | year | 10
12 | Reduce CO2 emissions | tons/year | 56,0
Benefits of the Solution:
Reduces leakage losses in the plant when the peak pressure is low.
Easily establishes the plant's optimal pressure.
Prevents voltage drops in the electrical system, reducing startup currents and mechanical shocks, which increases motor lifespan.
The calculation table for the solution “Installing a flow control system to save electricity for the compressed air system” is presented below.

## Slide 18
Install the CESS energy-saving device for transformer 1.1 with a capacity of 1,500 kVA.
Current status: Transformer 1.1 has a capacity of 1,500 kVA, with an actual load of 276 kW, which is approximately 20% of its capacity. The transformer is currently operating under low-load conditions.
Proposed solutions: The CESS device is an energy efficiency device from South Korea. This device improves the transmission efficiency of electricity from the power supply to the end-use equipment, enhances the power factor, and adjusts the phase shift, among other functions…
2. Energy efficiency measure 4
Sơ đồ lắp đặt thiết bị CESS
Hình ảnh lắp đặt thực tế CESS

## Slide 19
TT | Factory | Province/City | Electricity Saving Rate (%)
1 | Thach Ban Tiles | Bắc Giang | 20,4
2 | S.K Tech Vina | Bắc Ninh | 12,9
3 | KPF Vina | Hưng Yên | 9,2
4 | Posco VNPC | Hưng Yên | 10,9
5 | Thai Trung Steel Rolling | Thái Nguyên | 7,8
6 | Jangwon Tech Vina | Bắc Ninh | 9,0
7 | Intops VN | Bắc Ninh | 9,5
Experimental results in Vietnam
Benefits of the solution brings:
Reduce machine maintenance costs Average energy saving: 6 – 15%, depending on load consumption Reducing CO2 emissions causing the greenhouse effect
2. Energy efficiency measure 4

## Slide 20
No | PARAMETER | UNIT | VALUE
 | Electricity price information |  | 
1 | Average electricity prices in 2022 | VNĐ/kWh | 1.599
 | Operating Information |  | 
2 | Average Hours of Operation in a Day | hour | 24
3 | Average number of active days in a year | ngày | 355
 | Current equipment information |  | 
4 | Transformer Rated Power | kVA | 1.500
5 | Actual average operating capacity | kW | 276
6 | Power consumption of devices before implementing the solution | kWh/year | 2.351.520
7 | Investment Rate | USD/kW | 85
8 | CESS Equipment Installed Capacity | kW | 350
9 | Total investment cost to implement the solution | Million VNĐ | 701,39
No | PARAMETER | UNIT | VALUE
10 | Calculation energy saving |  | 
11 | Percentage savings after implementation of the solution | % | 6.0%
12 | Electricity consumption after implementing the solution | kWh/year | 2.210.429
13 | Electricity saved after implementing the solution | kWh/year | 141.091
14 | Income brought by EEMs in 1 year | Million VNĐ/year | 225,60
15 | Simple payback period | month | 37,3
16 | Reduce CO2 emissions | tons/year | 101,9
Energy saving calculation for the solution:
2. Energy efficiency measure 4

## Slide 21
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU