## Slide 1: TRAINING PROGRAME for IEs
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
for: Enterprise leaders

## Slide 2: Training program for business leaders
TIME | Content
8.00 – 8.30 | Registration
8.30 – 8.40 | Opening Remarks
8.40 – 9.45 | Module 1: Project introduction Policy introduction: energy saving, greenhouse gas emission reduction, gender issues related in EE
9.45 – 10.00 | Breaks
10.00– 11.00 | Module 2. Relations between energy, environment and production and business, use of clean energy
11.00 – 11.45 | Module 3. The current situation of energy use and potential of industrial waste in Vietnam (cement, steel, seafood processing, brick and ceramic, textiles, beverages, paper and pulp, other industries (plastics...)
11.45 – 12.00 | Discuss
12.00 – 13.30 | Lunch
13.30 – 14.15 | Module 4. Energy Management, Energy Management System
14.15 – 15.00 | Module 5. EE project financing and VSUEE project financing approach
15.00 – 15.15 | Breaks
15.15 – 16.15 | Component 6. Case study in EE for Manufacturing Industry: Cement, Steel, Seafood Processing, Brick and Ceramic, Textile, Beverage, Paper & Pulp, Other Industries (Plastics...)
16.15 – 16.45 | Discuss
16.45 – 17.00 | Closing

## Slide 3
Module 6:
Typical report on energy efficiency in beverage industry in Vietnam
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
TRAINING PROGRAME for IEs
for: Enterprise leaders

## Slide 4
Beverage manufacturing industry

## Slide 5: Content
The facility’s information on the case study
Energy efficiency measures
Notes: Energy Performance Contract (EPC): An agreement signed between the ESCO and the customer to implement energy efficiency and conservation services.
EE sharing contract: The ESCO assumes all financial and technical risks of the project by arranging financing to implement the investment project for installing energy-efficient equipment at the customer's energy-using facility.
Guaranteed EE contract: The ESCO is responsible for supplying, designing, installing, measuring, and ensuring the effectiveness of EEMs for the customer.

## Slide 6
1. The facility’s information on the case study

## Slide 7
Main manufacturing sector: Beverage production
Main products: Purified water, canned soft drinks, PET bottled soft drinks (CF), RGB soft drinks, PET bottled soft drinks (HF)
Consisting of two production lines: Purified water production line and basic beverage production line
Main energy equipment: Transformer station, high-pressure air compressor station, cooling tower, chiller...
General information

## Slide 8: Production line
Purified water production process
Electricity
Electricity
ozone generator
Ingot
bottle blowing machine
Cover
Water treatment
Water purification
ultrafiltration disinfection
bottling and capping
labeling
packaging
Elictricity
Elictricity
Elictricity
Elictricity
Electricity/Steam
Finished product

## Slide 9: Production line
Basic beverage production process
Electricity
Water Treatment
raw materials
Electricity/ Steam
Syrup Preparation
Water Filtration
Mixing Ingredients
Electricity/ Steam
CO₂ Saturation
Bottle Blowing Machine
Bottling/Canning
capping
Electricity
Electricity
Electricity
Electricity
Electricity
Electricity
Electricity
Electricity
Electricity/ Steam
Capping
ingot
Electricity
heat oven
packaging
Finished product
Electricity

## Slide 10: Production line
Types of energy used in the production line
Electricity is used for almost all the equipment in the production line and auxiliary systems such as lighting systems, air conditioning systems, air compressors, etc.
Steam is used for heating in production.
DO oil is used to run the backup generator, forklifts, fire pumps, are internal vehicles.

## Slide 11: Energy supply system
Types of energy used in the production line
The company's power supply is sourced from a 22 kV grid through 10 transformer stations, delivering electricity to usage points
The backup generator system serves the electrical system in case of a power outage
Picture of the transformer station
1. Electrical system

## Slide 12: Energy supply system
The plant has two air compressor systems, divided into a high-pressure air system and a low-pressure air system.
The low-pressure air compressor station operates at an average actual capacity of about 52% load
The high-pressure air compressor station is equipped with separate controls and operates based on the activity status of the production line.
Low-pressure air compressor station
High-pressure air compressor station
2. Air compressor system

## Slide 13: Energy supply system
The company's steam supply system is currently operating in standby mode because the company uses steam purchased from external sources. The steam production systems only run on a monthly standby schedule to prevent malfunctions and are activated when there are issues with the external steam supply.
3. Heat supply system

## Slide 14
2. Energy efficiency measures

## Slide 15
EEMs 1: Enhance internal management and equipment maintenance
1. For the electrical equipment system.
Regularly propagate and train employees on energy efficiency. Increase the involvement of operational staff (Electricity saving should be based on a broad foundation and supported by the operational staff).
Monitor energy consumption based on production and non-production days to identify and address energy loss points. Develop procedures and checklists to ensure that equipment shutdowns have been carried out.
Install automatic control devices to shut down equipment when not in use.
Turn off all unnecessary lighting (such as during breaks, lunch hours, shift changes, and on holidays)
Install power factor correction capacitors to improve the “leading” power factor and address the “lagging” power factor of equipment. These can be installed on individual devices or groups of devices to control part or the entire distribution system.
Control the ambient temperature to extend the insulation life and reliability of motors, avoid exposing motors to direct sunlight, place motors in well-ventilated areas, and keep motors clean.

## Slide 16
2. For office buildings:
Check the thickness of the insulation on walls and roofs.
Inspect and seal any gaps that cause heat loss to the outside.
Use curtains both inside and outside windows to retain heat in winter and cool the room in summer.
Install sunshades for windows to reduce heat during summer.
Install automatic door and gate closing systems.
Set air conditioning temperature to above 26°C in summer and 23°C in winter.
Turn off all lighting when not in use or after working hours.
EEMs 1: Enhance internal management and equipment maintenance

## Slide 17
EEMs 2: Improve the operational efficiency of the refrigeration compressor
Current status
The factory currently uses a central refrigeration system with ammonia (NH3) as the refrigerant. The system uses glycol and water as the cooling medium. The main equipment in the system includes compressors, evaporators for cooling glycol, condensers, heat exchanger systems, and refrigeration pump systems.
The refrigeration compressor system provides chilled water through a network of AHUs (Air Handling Units) that distribute the cooling to the various areas of use. The air conditioning system is responsible for ensuring a comfortable working environment in both the production areas and the office spaces.
The localized air conditioning system in the factory has a relatively small total capacity.
Proposed solution
The operating method for compressors
Reducing the Condenser Refrigerant Temperature
Cleaning the Gas from the Refrigerant
Effective Maintenance Methods

## Slide 18
EEMs 3: Inspect, monitor, and address compressed air leakage points
Current situation
Through the survey and inspection of compressed air leaks at the company’s compressor stations, the auditing unit discovered leaks at control valves, couplings, and pneumatic cylinder valve mechanisms.
Proposed solution
Building operating rules and requirements for compressed air operators
Regular inspection of compressed air systems

## Slide 19
EEMs 3: Inspect, monitor, and address compressed air leakage points
Compressed air leak detection equipment
NO | SPECIFICATION | UNIT | VALUE
 | Information about electricity prices |  | 
1 | Average electricity price in 2023 | VNĐ/kWh | 1.721
 | Operational information |  | 
2 | Average number of operating hours in a year | h/year | 8400
 | Current equipment information |  | 
3 | Electricity consumption of the equipment before implementing the measure | kWh/year | 2.116.800
4 | Total investment cost for implementing the solution | million VNĐ | 94
 | EE calculation |  | 
5 | Percentage of savings achieved after implementing the measure | % | 2,0
6 | Electricity consumption after implementing the measure | kWh/year | 2.074.464
7 | Electricity saved after implementing the measure | kWh/year | 42.336
8 | Income generated from EE in one year | million VNĐ | 92
9 | Simple payback period | year | 1
10 | Project lifespan | year | 5
Brand: Allsun Model: EM282 Frequency response: 40 kHz ± 2 kHz Operating temperature: 0 - 40 °C
Estimated cost table for implementing compressed air leak detection

## Slide 20
EEMs 4: Install a flow control system to save electricity for the low-pressure air compressor station
Current situation
The company's low-pressure air compressor station consists of 4 screw compressors. The operating mode of the air compressor station depends on the production demand. The compressed air system operates at an average capacity of 252 kW, equivalent to 52% of the rated capacity of the entire compressed air system.
Proposed solution
The IFC (Intelligent Flow Control) system helps reduce energy losses in no-load mode, ensures continuous and stable compressed air pressure at the point of end use, saves compressed air energy by reducing artificial demand, and allows easy monitoring of compressed air signals to optimize the operating method.

## Slide 21
Installation diagram of the IFC device system at the output of the air compressor station
air compressor
Gas treatment equipment
EEMs 4: Install a flow control system to save electricity for the low-pressure air compressor station

## Slide 22
Actual installation image of the IFC device system
EEMs 4: Install a flow control system to save electricity for the low-pressure air compressor station

## Slide 23
NO | SPECIFICATION | UNIT | VALUE
 | Information about electricity prices |  | 
1 | Average electricity price in 2023 | VNĐ/kWh | 1.721
 | Operational information |  | 
2 | Average number of operating hours in a year | h/year | 8400
 | Current equipment information |  | 
3 | Total actual operating capacity of the compressed air system | kW | 250
4 | Electricity consumption of the equipment before implementing the measure | kWh/year | 2.116.800
5 | Total investment cost for implementing the solution | Million VNĐ | 865
 | EE calculation |  | 
6 | Percentage of savings achieved after implementing the measure | % | 7
7 | Electricity consumption after implementing the measure | kWh/year | 1.968.624
8 | Electricity saved after implementing the measure | kWh/year | 148.176
9 | Income generated from EE in one year | Triệu VNĐ/năm | 255
10 | Simple payback period | năm | 2,8
11 | Project lifespan | năm | 10
Benefits brought by the measures :
Reduce leakage losses in the factory when peak pressure is low
Easily establish the factory's optimal pressure
Prevent voltage drop in the electrical system, reduce inrush current, and minimize mechanical shock to components, thereby extending the motor's lifespan.
The calculation table for the solution 'Install a flow control system to save electricity for the compressed air system' is shown here:
EEMs 4: Install a flow control system to save electricity for the low-pressure air compressor station

## Slide 24
EEMS 5: Install a CESS energy efficiency device for Transformer Station No. 5 – 1,000 kVA
Status situation
Transformer station No. 5 has a rated capacity of 1,000 kVA, with an average operating load of 595 kW (equivalent to 59.5% of the rated capacity). This is the transformer station with the highest and most stable capacity in the factory's system of 10 transformer stations
Proposed measure
CESS device is an EE device from South Korea. This device improves the efficiency of electrical transmission from the power supply station to the equipment, enhances the power factor, and more.

## Slide 25
Physical function for energy savings: activates the compensating wavelength to offset distorted waves, improving the waveform and adjusting the phase shift to enhance power efficiency
CESS divice
EEMS 5: Install a CESS energy efficiency device for Transformer Station No. 5 – 1,000 kVA

## Slide 26
Secondary function: The function of maintaining a fixed wavelength helps change the electron displacement structure in a stable direction. It maintains effectiveness through a semi-permanent effect by restoring the half-life cycle

EEMS 5: Install a CESS energy efficiency device for Transformer Station No. 5 – 1,000 kVA

## Slide 27
Installation diagram of the CESS device
Actual installation image of the CESS
Phase
grounding wire
EEMS 5: Install a CESS energy efficiency device for Transformer Station No. 5 – 1,000 kVA

## Slide 28
NO | Plant | Province/City | Electricity savings rate(%)
1 | Thạch Bàn tiles | Bắc Giang | 20,4
2 | S.K Tech Vina | Bắc Ninh | 12,9
3 | KPF Vina | Hưng Yên | 9,2
4 | Posco VNPC | Hưng Yên | 10,9
5 | Thai Trung Steel Rolling | Thái Nguyên | 7,8
6 | Jangwon Tech Vina | Bắc Ninh | 9,0
7 | Intops Việt Nam | Bắc Ninh | 9,5
Experimental results in Vietnam
Benefits brought by the measure
Reduce machinery maintenance costs
Average electricity savings: 6 – 15%, depending on consumption load
Reduce CO2 emissions that contribute to the greenhouse effect.
EEMS 5: Install a CESS energy efficiency device for Transformer Station No. 5 – 1,000 kVA

## Slide 29
NO | SPECIFICATION | UNIT | VALUE
 | Information on electricity prices |  | 
1 | Average electricity price in 2023 | VNĐ/kWh | 1.721
 | Operational information |  | 
2 | Average number of operating days in a year | hour | 8.400
 | Current equipment information |  | 
3 | Average operating capacity of transformer station no. 3 | kW | 595
4 | Electricity consumption of the equipment before implementing the measure | kWh/year | 4.998.000
5 | Investment rate | USD/kW | 85
6 | Installed capacity of the CESS device | kW | 900
7 | Total investment cost for implementing the solution | Million VNĐ | 1.855
NO | SPECIFICATION | UNIT | VALUE
8 | EE calculation |  | 
9 | Percentage of savings achieved after implementing the measure | % | 6.5%
10 | Electricity consumption after implementing the measure | kWh/year | 4.673.130
11 | Electricity saved after implementing the measure | kWh/year | 324.870
12 | Income generated from EE in one year | Million VNĐ/year | 559
13 | Simple payback period | year | 2,8
14 | Project lifespan | year | 7
Calculate EE for the measure :
EEMS 5: Install a CESS energy efficiency device for Transformer Station No. 5 – 1,000 kVA

## Slide 30
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU