## Slide 1: TRAINING PROGRAME for IEs
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
for: Enterprise leaders

## Slide 2: Training program for business leaders
TIME | Content
8.00 – 8.30 | Registration
8.30 – 8.40 | Opening Remarks
8.40 – 9.45 | Module 1: Project introduction Policy introduction: energy saving, greenhouse gas emission reduction, gender issues related in EE
9.45 – 10.00 | Breaks
10.00– 11.00 | Module 2. Relations between energy, environment and production and business, use of clean energy
11.00 – 11.45 | Module 3. The current situation of energy use and potential of industrial waste in Vietnam (cement, steel, seafood processing, brick and ceramic, textiles, beverages, paper and pulp, other industries (plastics...)
11.45 – 12.00 | Discuss
12.00 – 13.30 | Lunch
13.30 – 14.15 | Module 4. Energy Management, Energy Management System
14.15 – 15.00 | Module 5. EE project financing and VSUEE project financing approach
15.00 – 15.15 | Breaks
15.15 – 16.15 | Component 6. Case study in EE for Manufacturing Industry: Cement, Steel, Seafood Processing, Brick and Ceramic, Textile, Beverage, Paper & Pulp, Other Industries (Plastics...)
16.15 – 16.45 | Discuss
16.45 – 17.00 | Closing

## Slide 3
Module 6.5:
Typical report on energy efficiency in Ceramic and Brick industries in Vietnam
The Vietnam Scaling up Energy Efficiency Project (VSUEE)
TRAINING PROGRAME for IEs
for: Enterprise leaders

## Slide 4
Brick & Ceramic Industry in Vietnam

## Slide 5: Contents of the Ceramics industry
The facility’s information on the case study
Energy Efficiency Measures (EEMs)

## Slide 6
1
The facility’s information on the case study

## Slide 7: General Information
Main Production Field: Manufacturing building materials from clay.
Main Products: Clay tiles, ceramic tiles, porcelain tiles.
Production Scale: One comprehensive production line.
Main Energy Equipment: Crushers, tile grabbers, transformer stations, compressed air stations, kilns, pumps, fans, cooling systems, etc.

## Slide 8: Production Line
Production Process

## Slide 9: Production Line
Types of Energy Used in the Production Line:
Electricity: Utilized in systems and equipment such as crushers, grinders, machinery in the production line, fan systems, air conditioning, lighting, air compressors, etc.
Compressed Air System: Supplies compressed air for controlling pistons in production machinery.
Natural Gas: Used as fuel for the kilns.
Wood/Husk and Coal: Used as fuel for combustion.
Diesel Oil (DO): Used as fuel for various production processes.

## Slide 10: Energy Consumption System
The Company's power system uses a 22 kV grid power source through 4 substations.
At the transformer stations, the monitoring and measurement systems are relatively well-equipped. The company has installed automatic reactive power compensation capacitors for the electrical system to improve the power factor, ensuring that the power factor of the power supply system exceeds 0.9.
Pictures of distribution cabinets
1. Electrical system

## Slide 11: Energy Consumption System
The factory is using 5 air compressors all of LINGHEIN with a capacity of 75 kW, operating pressure of 6 bar, all of which are screw air compressors. An all-in-one air compressor system runs throughout the plant.
Air Compressor Images
2. Air compressor system

## Slide 12: Energy Consumption System
The lighting system is quite extensive, accounting for a significant portion of electricity consumption.
Natural lighting is effectively utilized in workshop areas, with good use of natural light helping to reduce electricity consumption for lighting on days with sufficient sunlight.
Regular cleaning of lighting equipment should be enhanced to ensure adequate illumination for production areas.
3. Lighting system

## Slide 13: Energy Consumption System
The company's kiln system includes a system of billet kilns, enamel kilns and continuously operating drying furnace systems.
Furnace system
No | Furnace | Fuel Type | Design capacity (tons/hour) | Operating Hours (hours/day)
1 | 2-tier drying oven | Take advantage of the heat of the furnace | 35.000 | 24
2 | Billet kiln | Natural Gas | 35.000 | 24
3 | Enamel kilns | Natural Gas | 35.000 | 24
4. Furnace system

## Slide 14
2
Energy Efficiency Measures (EEMs)

## Slide 15: EEMs 1: Enhancing Internal Management and Equipment Maintenance
1. For Electrical Equipment Systems:
Regularly promote and train employees on energy-saving practices. Encourage active participation from operational staff (energy-saving efforts require broad-based implementation and operator support).
Monitor energy consumption levels based on production and non-production days to identify and address energy loss points. Develop procedures and checklists to ensure equipment shutdowns are properly carried out.
Install automated control devices to switch off equipment when not in use.
Turn off all unnecessary lighting (e.g., during breaks, lunch hours, shift changes, and non-working days).
Install capacitor banks to create a “leading” power factor, correcting the “lagging” power factor of equipment. Capacitors can be installed for individual devices or groups of equipment to manage parts or the entire distribution system.
Regulate the surrounding temperature to extend motor insulation lifespan and reliability. Avoid exposing motors to direct sunlight, place them in well-ventilated areas, and maintain cleanliness for optimal performance.

## Slide 16: EEMs 1: Enhancing Internal Management and Equipment Maintenance
2. For Cooling and Air Conditioning Systems:
Perform regular cleaning and replacement of filters, and clean evaporators and condenser coil tubing to improve the cooling efficiency of air conditioning units.
Set the air conditioning temperature appropriately. During summer, the temperature should be set between 26°C and 27°C. Avoid setting it too low or too high. Setting the temperature too low will cause the air conditioner to operate for longer periods. Every 1°C decrease in temperature increases energy consumption by 3–4% of the air conditioning system’s total power usage.
3. For Compressed Air Systems:
Train and raise awareness among employees to ensure efficient operation and maintenance of the compressed air system.
Ensure the system remains dry by maintaining proper drainage slopes, drainage points, and outlet points to limit pipe corrosion.
Invest in leakage detection equipment or air leak testers to measure overall losses in the compressed air system and compressor capacity. Identify and repair leaks promptly and take preventive measures to avoid recurrence.

## Slide 17: EEMs 1: Enhancing Internal Management and Equipment Maintenance
4. For Office Buildings:
Check the thickness of wall and roof insulation.
Inspect and seal any gaps to prevent heat loss from the room.
Use curtains or blinds inside and outside windows to retain heat during winter and cool the interior during summer.
Install sunshades over windows to reduce heat during the summer.
Install automatic door and gate closing systems.
Install double-layer doors or air curtains on the west–north facing directions.
Set air conditioners to a temperature above 26°C in summer and 23°C in winter.
Turn off all lighting when not in use or after working hours.

## Slide 18: EEMs 2: Inspecting, Monitoring, and Addressing Compressed Air Leaks
Current Situation:
During a survey and inspection for compressed air leaks at the company, auditors identified leaks at control valves, couplings, and pneumatic cylinder valve mechanisms. Air leaks are inevitable during the operation of compressed air systems. The main locations where air leaks were detected include:
• Pneumatic valves of machinery.
• Couplings.

## Slide 19: EEMs 2: Inspecting, Monitoring, and Addressing Compressed Air Leaks
Compressed Air Leak Detection Device
Solution:
“Inspect, Monitor, and Address Compressed Air Leak Points”
Technical Specifications:
Brand: Allsun
Model: EM282
Color: White & Black
Frequency Response: 40kHz ± 2kHz
Battery Type: 9V Battery (not included)
Operating Temperature: 0–40°C
Product Weight: 80g
Product Dimensions: 191 x 50 x 29mm

## Slide 20: EEMs 2: Inspecting, Monitoring, and Addressing Compressed Air Leaks
No. | Parameter | Unit | Value
1 | Average electricity price | VND | 1,738
2 | Actual operating capacity of the compressed air system | kW | 231
3 | Electricity consumption before implementing the solution | kWh/year | 1,524,600
4 | Total investment cost for implementing the solution | Million VND | 64
5 | Percentage of savings achieved by the system after implementation | % | 2.0
6 | Electricity consumption after implementing the solution | kWh/year | 1,494,108
7 | Electricity saved after implementing the solution | kWh/year | 30,492
8 | CO2 emission reduction | Tons/year | 20.6
9 | Revenue from CO2 emission reduction (20 USD/ton CO2) | Million VND/year | 10
10 | Total revenue generated by the solution | Million VND/year | 67
11 | Payback period | Years | 1.0

## Slide 21: EEMs 3: Implementation of Energy Management System According to ISO 50001
Current Status:
The energy management system is at a fairly good level. The company has planned to establish an energy management committee in compliance with ISO 50001:2018 and has assigned staff to attend energy manager training courses.
Solution:
To facilitate the establishment of an energy management committee under ISO 50001:2018 and the training of energy managers, the audit unit proposes the solution: “Implementing an energy management system according to ISO 50001 standards.”
Energy management model according to ISO 50001 standard

## Slide 22: EEMs 3: Implementation of Energy Management System According to ISO 50001
Improvement of Energy Policy:
Continuously seek effective energy usage solutions and reduce energy consumption intensity.
Raise awareness about energy-saving and efficient usage in a sustainable manner for all employees in the factory.
The energy policy is regularly reviewed to ensure it remains aligned with the operational conditions of the factory.
Commitment to reducing energy consumption (e.g., 5% reduction in the next 5 years).
Commit to allocating a budget equivalent to (e.g., 15% of the previous year’s energy consumption costs) for energy management and energy-saving initiatives in the factory.
Closely monitor energy consumption in key energy-consuming departments within the factory.

## Slide 23: EEMs 3: Implementation of Energy Management System According to ISO 50001
Developing an Energy Planning Process:
Establish an energy baseline and energy performance indicators.
Identify energy improvement opportunities (The Energy Management Committee is responsible for proposing energy improvement opportunities that will enhance energy usage in the factory; The energy manager is responsible for evaluating and reporting suitable energy improvement opportunities to senior management).
Set energy goals and targets.
Develop an action plan (Clearly define responsibilities of the involved parties; Methods and timelines to achieve individual targets; Declare the method for checking and confirming energy efficiency improvements; Declare the method for checking and confirming results).

## Slide 24: EEMs 4: Installation of IFC Flow Control System for Energy Savings in the Compressed Air System
IFC Equipment System
Current Situation:
The factory’s air compressor system consists of two screw-type air compressors used to control the opening and closing of valves in the production line and for certain production stages. At the time of the survey, the company was operating two air compressors: one in Workshop 1 and one in Workshop 2.
Solution: Install an IFC flow control system to optimize flow and save energy for the compressed air system.

## Slide 25: EEMs 4: Installation of IFC Flow Control System for Energy Savings in the Compressed Air System
Actual installation image of IFC equipment system
Installation diagram of the IFC equipment system at the outlet of the air compressor station
Compressed Air System
Gas Treatment Equipment

## Slide 26: EEMs 4: Installation of IFC Flow Control System for Energy Savings in the Compressed Air System
No. | Parameter | Unit | Value
1 | Average electricity price | VND/kWh | 1,732
2 | Electricity consumption before implementing the solution | kWh/year | 1,524,600
3 | Total investment cost for IFC GE-30 system (excluding installation and accessory costs) | Million VND | 741
4 | Percentage of system savings after implementing the solution | % | 7.5
5 | Electricity consumption after implementing the solution | kWh/year | 1,410,255
6 | Electricity saved after implementing the solution | kWh/year | 114,345
7 | CO2 emission reduction | Tons/year | 77.4
8 | Revenue from CO2 emission reduction (20 USD/ton CO2) | Million VND/year | 37
9 | Total revenue generated by the solution | Million VND/year | 236
10 | Payback period | Years | 3.1

## Slide 27: EEMs 5: Installation of CESS Energy Saving System for 2,000 kVA Transformer Substation
Current Situation: The substation has a rated capacity of 2,000 kVA, with the actual transformer load reaching approximately 1,060 kW, which is equivalent to 53% of the load. The transformer is currently operating in medium-load mode.
Solution: Install the CESS energy-saving system for the 2,000 kVA transformer substation.
CESS Set Pictures

## Slide 28: EEMs 5: Installation of CESS Energy Saving System for 2,000 kVA Transformer Substation
Sơ đồ lắp đặt thiết bị CESS

## Slide 29: EEMs 5: Installation of CESS Energy Saving System for 2,000 kVA Transformer Substation
CESS Pictures in site

## Slide 30: EEMs 5: Installation of CESS Energy Saving System for 2,000 kVA Transformer Substation
No. | Parameter | Unit | Value
1 | Average annual electricity price | VND/kWh | 1,732
2 | Calculated consumption capacity | kW | 1,060
3 | Installed capacity of the CESS system | kW | 1,600
4 | Electricity consumption before implementing the solution | kWh/year | 9,285,600
5 | Electricity savings after implementing the solution | kWh/year | 577,136
6 | CO2 emission reduction | Tons/year | 377
7 | Income from energy savings in one year | Million VND/year | 968
8 | Income from CO2 emission reduction (20$/1 ton CO2) | Million VND/year | 182
9 | Total income from the solution | Million VND/year | 1,150
10 | Simple payback period | Years | 2.9

## Slide 31: Content for the Brick Industry
The facility’s information on the case study
Energy Efficiency Measures (EEMs)
Notes: Hợp đồng hiệu quả năng lượng (EPC): là hợp đồng ký kết giữa ESCO và Khách hàng để thực hiện dịch vụ sử dụng năng lượng tiết kiệm và hiệu quả.
– Hợp đồng chia sẻ mức tiết kiệm năng lượng: ESCO chịu mọi rủi ro tài chính và kỹ thuật của dự án bằng cách thu xếp tài chính để thực hiện dự án đầu tư lắp đặt các trang thiết bị hiệu quả năng lượng tại cơ sở sử dụng năng lượng của khách hàng
– Hợp đồng đảm bảo mức tiết kiệm năng lượng: ESCO chịu trách nhiệm cung cấp, thiết kế, lắp đặt, đo lường và đảm bảo hiệu quả giải pháp sử dụng năng lượng tiết kiệm và hiệu quả cho khách hàng.

## Slide 32
1
The facility’s information on the case study.

## Slide 33: General Information
Main production field: Manufacturing bricks and building materials
Main products: Ceramic bricks, tiles
Production scale: 1 production line with a capacity of 350,000 m²/month
Key energy equipment: Transformer station, compressed air station, circulation pump station, etc.

## Slide 34: Production Line
Production Process
Prepare Bone Powder
Pressing and Drying
Glazing
Firing (Kiln)
Inspection & Classification
Packaging Products
Finished Products
Water, Heat
Wastewater, Waste Heat
Glaze, Water
Excess Glaze, Wastewater
Heat
Waste Heat
Defective Bricks
Boxes, Labels
Excess Boxes and Labels

## Slide 35: Production Line
Types of Energy Used in the Production Line:
Electricity: Used in systems and equipment such as presses, dryers, kilns, fan systems, dust collectors, packaging machines, air conditioning, lighting, and air compressors.
Compressed Air: Supplied by the compressed air distribution system for controlling pistons in production machines and for processes like dust collection, packaging, and kiln operation.
Coal: Used for firing bricks in the kilns.
Fuel Oil (FO): Used for starting up the kilns and as supplemental fuel when needed.

## Slide 36: Energy Supply System
The company’s electrical system utilizes a 22/0.4 kV power grid through three transformers.
Image of measuring equipment at the power station
At the transformer stations, the monitoring and measurement systems are relatively well-equipped. The company has installed high-voltage and low-voltage power factor correction systems, ensuring the power factor of the electrical supply system consistently exceeds 0.9.
Substation pictures
1. Electrical System

## Slide 37: Energy Supply System
The company’s drying and kiln system represents a significant portion of energy usage due to its scale and intensity.
Currently, many sections of the kiln system pipelines have inadequate insulation, resulting in very high surface temperatures, leading to heat loss to the external environment and increased fuel consumption.
Some areas of the surface remain uninsulated.
2. Drying and Kiln System

## Slide 38: Energy Supply System
The company has a centralized, independent compressed air station interconnected with a shared network where the valves are kept open continuously.
It consists of three screw air compressors with a power capacity of 37 kW each and a working output of 6.28–7.42 m³/min.
Compressed air station image
3. Air Compressor System

## Slide 39
2
Energy Efficiency Measures (EEMs)

## Slide 40: EEMs 1: Install Smoke Ducts from Kilns to Spray Dryers for Heat Recovery Instead of Using Outside Air
Current Status:
The air supplied to the combustion chamber of the spray dryer is drawn directly from the external environment, with an ambient temperature of about 30°C.
The residual oxygen concentration in the exhaust fumes from the spray dryer is very high, approximately 18–19%. This indicates that the supplied air volume is significantly excessive compared to the actual fuel combustion requirements (with an excess air ratio of approximately 600%).

## Slide 41: EEMs 1: Install Smoke Ducts from Kilns to Spray Dryers for Heat Recovery Instead of Using Outside Air
Solution:
“Install additional heat recovery ducts to redirect exhaust fumes from the glaze kiln or biscuit firing kiln to the spray dryers.”
Energy Savings Calculation for the Solution:
“Install smoke ducts from kilns to spray dryers for heat recovery instead of using outside air.”

## Slide 42: EEMs 2: Enhancing Moisture Removal Efficiency for Coal Gasification Products
Current Status
The company does not have efficient moisture separation and cooling equipment for the finished gas, resulting in a relatively high moisture content in the coal gas.
Measurements indicate that the relative humidity of coal gas at the supply station is approximately 97-98%; at the kiln area in Workshop 2, it ranges from 83-90%; and in the biscuit kiln at Workshop 1, the humidity is 97.5% at the kiln entrance and 94.5% at the exit.
Solution: “Reduce the moisture content in the finished coal gas.”
Implementation Plan
Enhance the cooling efficiency at the heat exchange tower by adding cooling fans or installing additional indirect water-based heat exchangers.
Install an indirect heat exchanger using water to cool the coal gas after the cooling tower, reducing its temperature to approximately 120-150°C, and replace the water-based washing tower with a fabric bag dust filter.
Use water to cool the coal gas indirectly through heat exchange, directing the gas through zigzag walls or cyclones to separate moisture.

## Slide 43: EEMs 2: Enhancing Moisture Removal Efficiency for Coal Gasification Products
Energy-Saving Principle
Moisture in the fuel consumes a significant amount of heat to evaporate and reach the exhaust gas temperature. As moisture neither burns nor generates heat, it leads to energy losses. Reducing the moisture content in the fuel helps save energy.
Energy-Saving Potential
Improved moisture removal efficiency in coal gas can increase kiln thermal efficiency by approximately 1-3%.
Solution Implementation Costs
The method chosen for moisture reduction will determine the implementation cost. The estimated cost for this solution is approximately 1.2 billion VND.

## Slide 44: EEMs 3: Enhancing Thermal Insulation for Heat-Generating Surfaces on Hot Coal Gas Pipelines
Current Status:
At the coal gasification station, in the hot coal gas furnace area, the surface temperature of components such as the pipelines exiting the furnace, cyclones, and hot coal gas conduits to the gas collector is very high. This leads to significant heat loss to the environment and increased fuel consumption.
Some photos of surface heat at locations that are not insulated or poorly insulated at the location of the hot coal gas channel

## Slide 45: EEMs 3: Enhancing Thermal Insulation for Heat-Generating Surfaces on Hot Coal Gas Pipelines
Observation:
Evaluations indicate considerable heat loss to the environment. At locations without thermal insulation, the average surface temperature ranges from 90°C to 220°C.
Heat loss for 1 m² of uninsulated surface at 120°C: 1,191 W/m²
Calculation of uninsulated surface heat loss

## Slide 46: EEMs 3: Enhancing Thermal Insulation for Heat-Generating Surfaces on Hot Coal Gas Pipelines
Solution:
To enhance insulation for the kiln walls, various widely available thermal insulation materials can be used, such as fiberglass and rockwool.
Consider using Thermoluxx Premium thermal insulation material, a product of Thermoluxx Swiss AG from Switzerland, known for its nano-technology-based thermal insulation, fire resistance, UV resistance, and anti-corrosion properties.
Specifications of Thermoluxx Premium insulation
Specifications of some insulation materials
Fiberglass Insulation
Rockwool Insulation
Ceramic Wool Insulation

## Slide 47: EEMs 3: Enhancing Thermal Insulation for Heat-Generating Surfaces on Hot Coal Gas Pipelines
Tính toán tổn thất nhiệt bề mặt được bảo ôn
Benefits:
Enhancing thermal insulation significantly reduces heat loss to the environment.
Heat loss saved after implementing the solution: 626 W/m²
Energy-Saving Calculations for the Solution:
Total area requiring insulation: ~70 m²
Average reduction in surface temperature after insulation: 60°C
Total coal saved annually after implementing the solution: 388 tons
Estimated paint consumption after implementation: 70 m² (with a 3mm insulation layer thickness)
Estimated material cost: 108.1 million VND
Total implementation cost (including materials and labor): 124.3 million VND
Payback period: 5.4 months

## Slide 48: EEMs 4: Optimize the Excess Air Ratio Control for the Glaze Firing Kiln
Results of analysis of furnace exhaust fumes
Current Status:
The company operates 3 production lines:
Line 1: Includes 1 biscuit firing kiln (using coal gasification) and 1 glaze firing kiln (using LPG).
Line 2: Includes a dual-layer kiln (Layer 1 for biscuit firing using coal gasification, and Layer 2 for glaze firing using LPG).
Line 3: Includes 1 dryer and 1 kiln (using LPG).
Currently, glaze firing kilns use LPG as fuel, while biscuit firing kilns use coal gasification.
Excess oxygen concentration in exhaust gases is high.
The control loops for exhaust gas temperature and supplied airflow are manually adjusted, relying heavily on operator expertise and experience.
The fan motors for airflow and exhaust have inverters installed, but the load is still controlled manually based on operator judgment and real-time load demand.

## Slide 49: EEMs 4: Optimize the Excess Air Ratio Control for the Glaze Firing Kiln
Excess air factor control system
Proposed Solution:
“Optimize the excess air ratio control for the glaze firing kiln.”
Implementation Plan:
Install devices to measure oxygen and carbon monoxide concentrations in exhaust gases. These gas analyzers are widely available in the market.
Identify parameters for the FIC controller, configured as a PI or PID controller. Integrate the control system into the plant’s PLC. This includes a control loop for fan speed based on exhaust pressure, which is already part of the controller.
Equip the kilns with oxygen and CO analyzers to enable operators to monitor and adjust parameters effectively.

## Slide 50: EEMs 4: Optimize the Excess Air Ratio Control for the Glaze Firing Kiln
Energy-Saving Potential:
Post-implementation, the oxygen percentage in exhaust gases is expected to decrease from 12% to 6%.
Reduction in fuel consumption: 2.8% (for every 1% reduction in exhaust oxygen, fuel consumption decreases by 0.6%).
Estimated Investment Costs:
Components for excess air ratio control, including airflow fan controller, fuel-air ratio controller, airflow controller, oxygen sensors, pressure sensors, humidity sensors, display screens, and accessories: 1,000 million VND.
Labor and installation costs: 15% of the investment cost.
Total estimated project investment: 1,150 million VND.
Calculate the energy savings of the solution

## Slide 51: EEMs 5: Installation of a CESS Energy-Saving System for a 2,500 kVA Transformer
Current Status:
The transformer supplies power to production line equipment, mainly powering motors for manufacturing technology systems (presses, grinders, fans), lighting systems, and auxiliary equipment.
The transformer’s total capacity is 2,500 kVA, and during daytime measurements, the actual load was approximately 787 kW, equivalent to 45% of capacity.
Harmonic voltage distortion was measured at 2.47% to 2.67%, within acceptable limits, while harmonic current distortion ranged from 12.58% to 16.28%, exceeding acceptable thresholds.
Voltage phase deviation was 0.2%, and current phase deviation was 7.8%.
Kết quả đo công suất và phân tích chất lượng điện năng của máy biến áp 2.500 kVA (PX1)

## Slide 52: EEMs 5: Installation of a CESS Energy-Saving System for a 2,500 kVA Transformer
CESS Equipment Installation Diagram
Pictures of the actual installation of CESS in the field
Proposed Solution: “Install a CESS Energy-Saving System.”
Improve the efficiency of converting electrical energy into light, heat, or kinetic energy in machinery and equipment.
Enhance power transmission efficiency from the transformer station to electrical devices and machinery.
Increase the power factor of the system to boost the useful power of equipment.
Implementation Plan:
The CESS system is installed in parallel with the electrical load and is suitable for all power scales, ranging from a few kW to several thousand kW.
Installation locations: electrical cabinets or transformer stations.

## Slide 53: EEMs 5: Installation of a CESS Energy-Saving System for a 2,500 kVA Transformer
Some test results in Vietnam
Benefits of the CESS System:
Average energy savings: 6–15%, depending on the type of electrical load.
System safety: Ensures compatibility with the electrical system and equipment.
Extended equipment lifespan: Reduces wear and increases productivity.
Lower maintenance costs: Decreases the frequency of machinery servicing.
Environmental impact: Reduces CO2 emissions, contributing to the mitigation of greenhouse gases.
Energy-Saving Potential:
Based on calculations, energy savings are estimated at ~7.5% of total electricity consumption, with a guaranteed saving commitment of 6% upon installation.
Cost of Implementation:
The cost for the solution is $55 per kW.
Installed capacity: 1,500 kW.

## Slide 54: EEMs 6: Installation of a Power Management and Monitoring System
Cấu trúc hệ thống PMS
Current Status:
The factory’s measurement system is equipped with mechanical electricity meters. However, operational status evaluation and monitoring have not been implemented due to the limitations of the current measurement system.
Energy consumption is recorded and consolidated mid-month and at the end of the month, without timely evaluation or review of statistical data.
Proposed Solution:
Implement an automated Power Management System (PMS) for managing and monitoring energy consumption.

## Slide 55: EEMs 6: Installation of a Power Management and Monitoring System
Collect data before and after installing the PMS system
Chart of continuous data tracking 24 hours/day using PMS system
Benefits of the PMS System:
Reduced time and labor costs: Automates data recording processes.
Minimized errors: Accurate measurement reduces mistakes caused by manual data collection.
Continuous energy monitoring: Monitors energy usage 24 hours a day.
Utility bill verification: Provides energy usage reports to verify electricity invoices.
Identify disturbances and harmonics: Determines if issues are caused by external power sources or company equipment.
Optimized load management: Ensures equipment operates at appropriate loads, avoiding underloading or overloading.
Informed investment decisions: Facilitates accurate decisions when investing in additional power equipment during company expansion.

## Slide 56: EEMs 6: Installation of a Power Management and Monitoring System
Advantages of Using the PMS System
Comparison of Benefits After Installing the PMS Monitoring System
PMS System Assists in Monitoring the Entire Load of the Factory
PMS Software Supports Identifying and Locating Wasteful Areas
Save 2-4% on electricity costs by knowing where and when electricity is being consumed.
Save 2-5% on operational costs by optimizing equipment operation, reducing repair and replacement costs.
Save 10% or more by improving production efficiency, reducing abnormal downtime, and minimizing damage from malfunctions.

## Slide 57
Energy saving potential: Energy saving is in the range of ~0.5 - 5% of total electrical energy consumption (from the fact that companies and factories have installed the system).
Cost of implementing the solution
EEMs 6: Installation of a Power Management and Monitoring System
No. | Parameter | Unit | Value
Electricity Cost Information |  |  | 
1 | Average electricity price in 2022 | VND | 1,590
2 | Electricity consumption in 2022 | kWh/year | 20,698,788
3 | Total investment cost for implementing the solution | Million VND | 1,200
Energy Saving Calculation |  |  | 
4 | Percentage of savings compared to the baseline solution | % | 3.0
5 | Electricity consumption after implementing the solution | kWh/year | 20,077,824
6 | Electricity saved after implementing the solution | kWh/year | 620,964
7 | Income from energy savings in 1 year | Million VND/year | 987.3
8 | Simple payback period | months | 14.6
9 | Project lifetime | years | 10.0
10 | Net Present Value (NPV) of the project | Million VND | 5,341
11 | Internal Rate of Return (IRR) | % | 84%
12 | CO₂ emissions reduction | tons/year | 525.2

## Slide 58
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU