## Slide 1
VIETNAM SCALING UP ENERGY EFFICIENCY PROJECT
(VSUEE)

## Slide 2
BUSINESS MODELS FOR IMPLEMENTING EE PROJECTS, INCLUDING PERFORMANCE CONTRACTS AND ESCO

## Slide 3
DEFINITION OF ESCO
  Energy Service Company (ESCO)
An ESCO is a type of company whose business model is to use Energy Performance Contracts (EPCs) as the basis for its compensation when implementing energy saving projects.
Energy Efficiency Project + EPC = ESCO
ESCO

## Slide 4
KEY CHARACTERISTICS OF AN ESCO
Contractor
Energy Supplier
Professional Technical Consulting Engineer
Equipment Manufacturer
Financial institution
Government
ESCO
Contractor
Governments
Equipment Manufacturer
Financial Institution
Professional Technical Consulting Engineer
Energy Supplier
Business Owner

## Slide 5
ESCO BUSINESS MODEL – INTEGRATED SERVICES
Contractor
Energy Supplier
Professional Technical Consulting Engineer
Equipment Manufacturer
Financial institution
Government
ESCO
Business owner
Integrated Energy Services
  Identification of Energy Conservation Measures (ECMs)
  Technical Design
  Financing*
  Procurement
  Construction and On-site Supervision
  Commissioning
  Capacity Building
  Performance Guarantee
  Operation and Maintenance*
  Savings Tracking & Evaluation
Some ESCOs offer..

## Slide 6
TYPES OF ENERGY PERFORMANCE CONTRACTS (EPCs)
Guaranteed Savings Contract
Shared Savings Contract
Chauffage Contract
Page 5

## Slide 7
Guaranteed Savings Contract
Guaranteed Savings – How Financing Works
Chart: €
| Hiện tại | Trong chương trình EPC | Sau chương trình EPC
Série 1 | 1 | 0.6 | 0.6
Série 2 | 0 | 0.3 | 0.4
Série 3 | 0 | 0.15 | 0
The business owner's current annual costs
Energy costs and O&M costs
Business owners repay bank loans
Financial fees
Business owners receive (optional) profits/benefits.
Energy costs and O&M costs.
Business owners
benefit.
Annual business costs slightly decrease or remain equal
During EPC contract term
After EPC contract term

## Slide 8
GUARANTEED SAVINGS CONTRACT
Payment during the construction period (similar to a turnkey model)
Provide a loan to the customer
Customer commitment
Financial Institution
Customer
ESCO
ESCO implements the solution
Solution implementation period
Page 7

## Slide 9
GUARANTEED SAVINGS CONTRACT
Achieved energy savings
Customer directly repays the financial institution
Financial
Customer
ESCO
Repayment period
ESCO guarantees the savings level
The cost savings are used to repay the debt and pay the ESCO.
M&V
Notes: Emphasis:
The payment schedule for the ESCO is determined by the contract. The two most commonly considered payment options are:
Payment during the construction phase (similar to a turnkey model),
Payment upon completion of Measurement and Verification (M&V) and achievement of the guaranteed savings.

## Slide 10
GUARANTEED SAVINGS CONTRACT
ESCO guarantees:
Energy savings ≥ the loan amount.
ESCO covers all deficit.
BANKS
Lenders
Customer repays the loan
Energy savings:
As compared to the baseline
COSTUMERS
ESCO
Loans
Energy savings
Notes: Emphasis: This example illustrates the case where payment is made to the ESCO during the contract's implementation period. During this repayment period, if the M&V (Measurement & Verification) shows that the achieved savings fall short of the guaranteed amount, the ESCO must pay for the shortfall.
Cost Structure: Fixed price or cost-plus. It's possible for the actual savings to exceed the guaranteed level.
Guarantee: If the achieved savings are below the guaranteed level, the ESCO compensates the client for the shortfall amount.
Term: The contract has a fixed term.
Cash Flow: The client's cash flow improves immediately.
Equipment Ownership: The client typically owns the equipment.

## Slide 11
GUARANTEED SAVINGS CONTRACT
Capital
The business owner uses their own capital or borrows funds for implementation, or a combination of both.
The ESCO does not face credit risk.
The ESCO can assist in sourcing funding.
Contract term
Typically fixed and aligned with the debt service (in case of borrowing).

## Slide 12
SHARED SAVINGS CONTRACT
Shared Savings – How Financing Works
Chart: €
| Hiện tại | Trong chương trình EPC | Sau chương trình EPC
Série 1 | 1 | 0.6 | 0.6
Série 2 | 0 | 0.3 | 0.4
Série 3 | 0 | 0.15 | 0
Business owner's current annual costs
Energy costs and O&M costs
Business pays ESCO, ESCO pays the bank
Financial fees
Business owner receives (optional)
Energy costs and O&M costs
Business
owners
benefit
Business's annual costs slightly decrease or remain equal
Current
During EPC contract term
After EPC contract term
Investment capital

## Slide 13
SHARED SAVINGS CONTRACT
Borrow capital
Technical design, construction, commissioning, monitoring & verification (M&V)
Financial Institution
Business
ESCO
Implementation Period

## Slide 14
SHARED SAVINGS CONTRACT
Repayment
Monitoring & Verification (M&V), Remedial Actions
Shared savings payment based on performance
Financial institution
Business
ESCO
Repayment Period

## Slide 15
SHARED SAVINGS CONTRACT
ESCO repayments using saving costs from the energy savings portion
May be full or a percentage
Typically reconciled annually
Option: cumulative savings ("savings bank")
Notes: Saving accumulation: Some ESCO stipulate in their contract that any excess saving in one year goes into a virtual “bank of savings”. The extra saving can be used in future years to offset a lack of savings.
Savings Accumulation: Some ESCOs stipulate in the contract that any excess savings in a given year will be placed into a virtual "savings bank." These additional savings can then be used in subsequent years to offset any performance shortfalls.

## Slide 16
Chauffage (a French term) is a type of Energy Performance Contract (EPC) where a business owner pays the Energy Service Company (ESCO) or contractor a fixed fee per unit of useful energy (heating, cooling, electricity) supplied to the building.
The ESCO charges for the energy provided in different units:
GJ/BTU for heat
GJ/ton for cooling (chilled water)
kWh for electricity
The ESCO controls the operation and maintenance process of the plant and drafts the service level agreements.
CHAUFFAGE CONTRACT

## Slide 17
CHAUFFAGE CONTRACT
The ESCO is responsible for:
Providing energy services (e.g., heating, cooling, hot water),
Operating and maintaining equipment, and
Ensuring efficiency and cost savings (often sharing the savings with the customer).
In simple terms: Instead of paying separately for fuel or electricity, the customer pays for the "comfort provided" (e.g., cooling or heating), while the ESCO bears the risk related to efficiency and performance.
The contract can last from 10 to 15 years, or align with the lifespan of the energy-efficient equipment.
Notes: Key differences: Chauffage Contracts: Payment is made for the output energy service (guaranteed supply level and reliability). Guaranteed Savings Contracts: Payment is based on guaranteed savings (guaranteed reduction in energy consumption). Shared Savings Contracts: Payment is based on actual energy savings shared between the business owner and the ESCO

## Slide 18
CHAUFFAGE CONTRACT
Chauffage contract- How Financing Works
Chart: €
| Hiện tại
Série 1 | 1 | 0.6 | 0.6 | 60
Série 2 | 0 | 0.3 | 0.3 | 40
Série 3 | 0 | 0.1 | 0.1
Transferred via ESCO
Capital
Customer receives benefits
ESCO's profit
Interest
Customer receives benefits
Business benefits
EPC contract term
During the investment payback period
After the investment payback period
Current
Notes: Column 1: The Baseline This column represents the current energy and O&M (Operation & Maintenance) costs before implementing the energy-saving solution.
Column 2: The First Contract Phase (Investment Recovery) This column illustrates the initial phase of the chauffage contract: The ESCO implements the solution, and the customer makes periodic payments to the ESCO based on the amount of energy supplied (guaranteed to be lower than the current cost). The ESCO uses these payments to repay the principal and interest on the investment.
Column 3: The ESCO's Profit Phase This column represents the phase where the ESCO generates profit. The customer continues to pay the ESCO after the ESCO has fully recouped its investment. The duration of this phase can be long or short, or it may even be integrated into the phase described in Column 2, depending on the agreement between the two parties.
Column 4: Post-Contract Transfer (Optional) The final column represents the period after the EPC (Energy Performance Contract) ends. The equipment or system is transferred to the customer for operation and management, and the customer enjoys the full amount of energy savings. This phase may or may not exist, depending on the agreement (e.g., if the chauffage contract lasts for the entire lifespan of the solution, this phase will not occur).

## Slide 19
CHAUFFAGE CONTRACT
The ESCO implements energy-saving/alternative energy solutions
The ESCO has the right to operate the energy-saving system/equipment
Financial Institution
Business
ESCO
During the implementation period
Cooling/heating center (eg.)

## Slide 20
CHAUFFAGE CONTRACT
Customer pays for energy services supplied
ESCO provides energy services
ESCO operates the power plant
Financial institution
Business
ESCO
ESCO repays the loan
After the implementation period
Cooling/heating center (eg.)

## Slide 21
CHOOSING A CONTRACT TYPE - SHARED SAVINGS CONTRACT
Advantages
No/Low initial CAPEX; payment is made from actual savings based on a pre-agreed percentage.
Disadvantages
Requires sharing a portion of savings → lower net benefit compared to self-investment.
Transfers most performance risks to the ESCO; often includes O&M/operational support.
Minimal increase in debt on financial statements; enables rapid technology upgrades.
Ensures transparency if the contract clearly defines the sharing ratio, baseline, and M&V plan.
Requires close M&V coordination: providing data, allowing metering, accepting baseline adjustments.
Changes in facility usage, production output, or processes must comply with adjustment clauses to avoid disputes (reduces flexibility).
Long-term commitment; risk of technology/vendor lock-in if flexibility clauses are not well-defined.
For
industrial enterprises:
Notes: Technology lock-in" is the risk where a business becomes "stuck" with a specific technology/solution/vendor for multiple years, making it difficult or costly to upgrade or switch to a better alternative later.

## Slide 22
CHOOSING A CONTRACT TYPE - SHARED SAVINGS CONTRACT
Advantage
Disadvantage
Requires significant upfront capital/working capital investment; cash flow is delayed as it is contingent upon the realization of actual savings.
Revenue is directly tied to the level of savings achieved; revenue may increase if savings exceed the target.
Bears performance risk and M&V/baseline adjustment risk; incurs higher M&V and transaction costs.
Client credit risk (late/non-payment); operational change risk leading to savings shortfalls.
More complex legal-financial structure compared to guaranteed savings contracts; may require insurance/guarantees/risk-sharing mechanisms.
Proactive control over design–procurement–operation (per agreement), with technical optimization to maximize savings.
Long-term partnership relationship; potential to standardize the model for scaling the project portfolio.
For ESCO:
Notes: This contract type typically requires more complex legal and financial structuring than a guaranteed savings agreement. To mitigate risks for both parties, additional safety layers—such as insurance, third-party guarantees, or risk-sharing funds/mechanisms—are often necessary.

## Slide 23
CHOOSING A CONTRACT TYPE – GUARANTEED SAVINGS
Advantages
IE owns the assets and controls operations.
Disadvantages
IE must arrange financing and record debt; a full tender/procurement process is required. Requires contract management & M&V capabilities to monitor, verify savings, and enforce compensation mechanisms. Early alignment is critical: baseline, guaranteed savings level, adjustment rules for production/usage changes; timelines may extend if historical data is limited. Commitment to operate under predefined conditions (e.g., operating hours, load) is essential to uphold the guarantee.
Capital costs are typically lower (the IE secures its own financing); savings are guaranteed – shortfalls are compensated by the ESCO per contract terms.
The IE retains all upside benefits if actual savings exceed the guaranteed level.
For
industrial enterprises (IE):

## Slide 24
CHOOSING A CONTRACT TYPE – GUARANTEED SAVINGS
Advantages
Minimal to no capital expenditure required (IE is responsible); the ESCO's cash flow is typically received based on contractual milestones, with limited dependence on measured savings (only relevant for compensation adjustments).
Disadvantages
Guarantee Responsibility: Bears the responsibility to cover any shortfall in savings through compensation/payment of liquidated damages.
Lower credit risk compared to the shared savings model, as the primary payer is the IE based on a fixed contract value.
A clearly defined guarantee scope → enables technical proactivity to meet or exceed guaranteed performance levels.
Requires: Clear M&V (Measurement and Verification) and baseline adjustment protocols; requires performance insurance/guarantees, and sometimes demands lender "step-in" rights.
Profit: Is capped (the upside primarily belongs to the IE), and the profit margin per project may be lower than in the shared savings model.
Requires: High-quality input data to establish a safe and secure guarantee level.
For ESCO:
Notes: For guaranteed savings contracts, if the actual savings exceed the target, the client (Industrial Enterprise - IE) is the primary beneficiary of the excess amount. The ESCO typically only receives the pre-agreed fee. Consequently, the profit per contract under this model is usually lower compared to the shared savings model.
A step-in right (or substitution right) is a clause that allows a third party – typically the lender to the ESCO or the client (IE) – to temporarily "step in" and assume the ESCO's role to operate/remedy the situation if the ESCO fails to meet its critical obligations.

## Slide 25
CHOOSING A CONTRACT TYPE – CHAUFFAGE CONTRACT
Advantage
Little to No Capital Investment: Shifts from capital equipment investment to purchasing a "utility" (e.g., steam, hot/cold water, compressed air, electricity...).
Predictable Cash Flow: Payment consists of a fixed availability fee + a variable fee based on metered utility consumption; this facilitates operational budgeting.
Fewer Disputes Over Savings: Payment is based on useful output, eliminating the need for complex Measurement and Verification (M&V) of savings.
Service Quality Defined by SLA (Service Level Agreement): Performance guarantees for temperature/pressure/flow rate; the ESCO faces penalties for non-compliance.
Focus on Core Business: The client can focus on core operations as the ESCO assumes full responsibility for the design, operation, maintenance, and safety of the energy solution.
Flexible Scalability: The model allows for expanding services to include Operation & Maintenance (O&M) for existing systems, integrating metering, and implementing energy management.
For
industrial enterprises:

## Slide 26
CHOOSING A CONTRACT TYPE – CHAUFFAGE CONTRACT
Disadvantage
Long-term commitment: Multi-year contracts require careful review of price adjustment clauses and early termination conditions.
Minimum output commitment (take-or-pay): Risk exposure if demand decreases or facility functions change.
Supplier dependency: Risk of service disruption impacting production; necessitates contingency plans/step-in rights.
Fuel cost risk: Without transparent pass-through/hedging mechanisms, the Industrial Enterprise (IE) may bear cost volatility.
Lifecycle cost: Total service fees may exceed self-investment costs if demand is stable and the IE has access to low-cost capital.
On-site safety & regulatory compliance: Permits, fire safety, environmental standards, site access rights; requires clear responsibility allocation.
Technology/vendor lock-in: Mitigate through open standards, data rights clauses, and mid-term upgrade/innovation provisions.
Metering & verification: Requires standardized measurement systems, periodic calibration, and protocols for handling data errors/loss.
For IE:
Notes: Price Adjustment Clause: The price adjustment clause incorporates specific indices as benchmarks for price revisions, such as:
CPI (Consumer Price Index): To offset inflation in labor and O&M (Operation & Maintenance) costs.
Fuel Price Index (published by a relevant authority/supplier): To pass through fluctuations in fuel costs.
Exchange Rate (if there are import/calculation components in foreign currency).
Reference Interest Rate (e.g., SOFR/VNIBOR): For the financial cost component, if agreed upon.
Typical Wording:
Take-or-pay is a clause in a service/goods contract stipulating that the customer must pay for a pre-committed minimum quantity/ output level, whether they fully take that amount or not.
  Purpose: To ensure the supplier recovers its fixed costs (investment, readiness to operate).
  In Chauffage/ESCO contracts: The Industrial Enterprise (IE) typically commits to a minimum monthly/quarterly consumption level of a utility (e.g., steam, chilled water, compressed air...). If consumption is below this commitment, the IE still pays for the shortfall.
Pass-through: The practice of directly passing cost fluctuations (typically for fuel) to the selling price/service charge according to a pre-agreed formula. The supplier does not bear the price risk.
  Example: Steam Price (month t) = Base Price + 0.8 × (Coal Price_t – Base Coal Price).
  Advantage: Simple and transparent. Disadvantage: The customer (IE) bears the cost volatility.
Hedging: "Hedging against price risk" using financial instruments/commercial terms to fix or cap input costs (e.g., oil/gas/electricity prices, exchange rates...). The risk is partially locked in, in exchange for an insurance cost (the cost of the hedge).

## Slide 27
CHOOSING A CONTRACT TYPE – CHAUFFAGE CONTRACT
Advantage
Stable cash flow from long-term contracts, structured with a capacity charge (or availability fee) and a consumption-based energy charge.
Payment is based on metered useful energy output, eliminating disputes over baselines or savings levels ⇒ reduces Measurement and Verification (M&V) costs.
Operational autonomy to implement technical optimizations for fuel and maintenance cost savings ⇒ increases profit margins.
ESCOs often partner with equipment manufacturers/technology providers.
Easier capital raising and project financing as the project asset can be recognized and used as collateral; suitable when investment capital is scarce.
Scalability to multiple utilities (steam, hot/cold water, compressed air, electricity…) and the ability to bundle Operation & Maintenance (O&M) services.
Potential for additional benefit from asset residual value or contract-end transfer arrangements.
For ESCO:
Notes: Advantages for the ESCO
Stable cash flow from long-term contracts, structured with a capacity charge (or availability fee) and a consumption-based energy charge.
Payment is based on metered useful energy output, eliminating disputes over baselines or savings levels ⇒ reduces Measurement and Verification (M&V) costs.
Operational autonomy to implement technical optimizations for fuel and maintenance cost savings ⇒ increases profit margins.
Easier capital raising and project financing as the project asset can be recognized and used as collateral; suitable when the client lacks investment capital.
Scalability to multiple utilities (steam, hot/cold water, compressed air, electricity…) and the ability to bundle Operation & Maintenance (O&M) services.
Potential for additional benefit from asset residual value or contract-end transfer arrangements.
Risks and Challenges for the ESCO
High capital requirements and long payback periods ⇒ creates cash flow pressure and financial leverage risk.
Risk of fuel and material price volatility if the contract lacks effective pass-through mechanisms or price indexation.
Volume risk due to changes in client demand ⇒ necessitates take-or-pay clauses or minimum purchase commitments.
Risk of failing to meet service quality commitments (e.g., availability rate, temperature/pressure/flow); resulting in penalties (liquidated damages) for non-compliance.
Legal, environmental, and safety risks during operation; compliance costs can be significant.
Counterparty risk (creditworthiness, early termination); asset recovery or relocation at contract end is often difficult and costly.
Contract Design Recommendations (Summary)
Clearly separate the capacity charge and energy charge; implement fuel price indexation.
Stipulate minimum purchase commitments (take-or-pay), metering boundaries, and quality of service standards.
Include clauses for changes in law, early termination and compensation, along with payment security mechanisms (e.g., performance bonds, guarantees).

## Slide 28
CHOOSING A CONTRACT TYPE – CHAUFFAGE CONTRACT
Disadvantage
High capital requirements and long payback periods ⇒ creating cash flow pressure and financial leverage risk.
Risk of fuel and material price volatility if the contract lacks a pass-through mechanism or price indexation.
Volume/Output risk due to changes in customer demand ⇒ necessitating a minimum purchase commitment (take-or-pay) clause.
Risk of failing to meet service quality commitments (e.g., availability rate, temperature/pressure/flow rate); resulting in penalties (liquidated damages) for non-compliance.
Legal, environmental, and safety risks during operation; compliance costs can be significant.
Counterparty risk (credit risk, early termination); asset recovery/relocation at contract end is often difficult and costly.
For ESCO:
Notes: Advantages for the ESCO
Stable cash flow from long-term contracts, structured with a capacity charge (or availability fee) and a consumption-based energy charge.
Payment is based on metered useful energy output, eliminating disputes over baselines or savings levels ⇒ reduces Measurement and Verification (M&V) costs.
Operational autonomy to implement technical optimizations for fuel and maintenance cost savings ⇒ increases profit margins.
Easier capital raising and project financing as the project asset can be recognized and used as collateral; suitable when the client lacks investment capital.
Scalability to multiple utilities (steam, hot/cold water, compressed air, electricity…) and the ability to bundle Operation & Maintenance (O&M) services.
Potential for additional benefit from asset residual value or contract-end transfer arrangements.
Risks and Challenges for the ESCO
High capital requirements and long payback periods ⇒ creates cash flow pressure and financial leverage risk.
Risk of fuel and material price volatility if the contract lacks effective pass-through mechanisms or price indexation.
Volume risk due to changes in client demand ⇒ necessitates take-or-pay clauses or minimum purchase commitments.
Risk of failing to meet service quality commitments (e.g., availability rate, temperature/pressure/flow); resulting in penalties (liquidated damages) for non-compliance.
Legal, environmental, and safety risks during operation; compliance costs can be significant.
Counterparty risk (creditworthiness, early termination); asset recovery or relocation at contract end is often difficult and costly.
Contract Design Recommendations (Summary)
Clearly separate the capacity charge and energy charge; implement fuel price indexation.
Stipulate minimum purchase commitments (take-or-pay), metering boundaries, and quality of service standards.
Include clauses for changes in law, early termination and compensation, along with payment security mechanisms (e.g., performance bonds, guarantees).

## Slide 29
WHICH TYPE OF CONTRACT SHOULD YOU CHOOSE?
A GUARANTEED SAVINGS CONTRACT OR A SHARED SAVINGS CONTRACT?
DISCUSSION

## Slide 30
COMPARISON OF COMMON CONTRACT TYPES
Criterion | Guaranteed Savings | Shared Savings
Source of Funds | The customer self-arranges funds/ or obtains a bank loan. | The ESCO arranges financing (often through bank loans/project finance).
Cash Flow / Repayment | The customer pays the ESCO a service/performance fee; the customer repays the bank debt independently (if any). | The ESCO recovers its investment through a share of the actual savings until the payback period/profit is reached.
Core Commitment | The ESCO guarantees a minimum level of savings; any shortfall is compensated by the ESCO. | There is no guaranteed minimum; savings are shared based on the measured results.
Performance Risk | Primarily on the ESCO. | Primarily on the ESCO, plus volume risk/operational variability risk as recovery depends on achieved savings.
Counterparty Credit Risk | Risk of customer late/non-payment. | Risk of the customer not transferring the agreed share of savings.
M&V (Measurement & Verification) | Simpler/less disputed due to the guaranteed threshold; baseline adjustments are moderate. | More stringent, highly dependent on the baseline and operational adjustments → higher potential for disputes.
Contract Complexity | Medium; includes clauses for shortfall compensation, standard M&V. | High; requires a sharing formula, baseline adjustments, etc.
Bank Acceptance | Generally easier access to loans (savings are guaranteed). | Access to financing depends heavily on customer creditworthiness and M&V quality; often requires additional guarantees/collateral.
Ownership & O&M | Flexible; O&M can be performed by either the ESCO or the customer. | O&M is usually handled by the ESCO to control performance.

## Slide 31
Thank you!
Page 27