## Slide 1
VIETNAM SCALING UP ENERGY EFFICIENCY PROJECT
(VSUEE)

## Slide 2
CONSIDERATIONS IN FINANCING ESCO PROJECTS

## Slide 3
OBJECTIVES
1. Identify risks of the energy efficiency/ESCO project 2. Consider risk mitigation options when financing an energy efficiency/ESCO project

## Slide 4
SCOPE OF EE INVESTMENT AND RETURN ON INVESTMENT (ROI) PERIOD
Developing the scope of energy efficiency investments and payback period
O&M + Lighting & HVAC (medium-term investment)
O&M & Lighting + HVAC/process (long-term investment)
HVAC & Lighting & O&M + RE & Building insulation
O&M & Lighting & HVAC & RE + Repair of building envelope (windows, facades)
Operational optimization
2 years
5 years
15 years
25 years
50 years
Savings
No Cost / Low Cost
Payback
ESCO*
High investment
* Shared savings, guaranteed savings

## Slide 5
SCOPE OF EE INVESTMENT AND RETURN ON INVESTMENT (ROI) PERIOD
Developing the scope of energy efficiency investments and payback period
Energy Efficiency Solution | Average Payback Period
Insulation | 
Hot water insulation | 0.75 – 1 year
Draft-proofing equipment | 6 – 6.5 years
Insulation on loose-filled layers | 1.5 years
Double-wall insulation | 2 – 4 years
Roof insulation | 11 – 15 years
High-efficiency thermal doors | 65 – 70 years
Double-glazed windows | 10-15 years
Internal wall insulation | 37 – 62 years
External wall insulation | 50 – 85 years
High-efficiency glazing (SHGC) | 5 – 7 years
Shading devices | 5 – 7 years
Energy Efficiency Solutions | Average Payback Period
Lighting, Heating, and Appliances | 
Daylighting controls | 5 – 7 years
Occupancy sensors | 3 – 5 years
Lighting | 2 – 3 years
Programmable thermostats | 1.5 – 2 years
Heating system controls (TRVs) | 6.5 – 7.5 years
Mechanical heat recovery & ventilation | 3 – 5 years
Condensing gas boilers | 4.5 – 6.5 years
Condensing oil boilers | 6 – 9 years
High-efficiency elevators (using VV/F inverter drives) | 8 – 10 years
Meters / Building Management Systems (BMS) | 5 – 8 years

## Slide 6
CAPITAL SUPPLY VS. DEMAND FOR ENERGY EFFICIENCY FUNDING
The Energy Efficiency market presents substantial growth opportunities for financial institutions.
While some financial institutions have ample capital to lend for energy efficiency investments,
others lack dedicated funding for such projects.
This has resulted in a significant gap between the supply and demand of capital for energy-saving initiatives.

## Slide 7
FINANCIAL BARRIERS TO ENERGY EFFICIENCY PROJECTS
Financial Barriers
Stringent lending requirements and conditions
- Limited internal investment capacity
- Limited borrowing capacity
- Traditional lending methods are based on assets
- The "small scale" of EE projects makes them unattractive to banks because the appraisal costs are significantly higher compared to larger projects.
Awareness and traditions
- Lack of information dissemination
- Lack of information about the benefits of energy efficiency projects, about M&V, and about incentive mechanisms
Project development
Risk assessment and mitigation
- Lack of project development capacity (ESCOs, financial institutions, equipment suppliers, consultants, etc.)
- Lack of capacity to develop project packages, sell EPC contracts, and develop energy efficiency projects
- Financial institutions lack the capacity to assess risks of energy efficiency projects
- Financial institutions lack support tools for decision-making
- Lack of M&V plans and assurance mechanisms.

## Slide 8
FINANCIAL MECHANISMS FOR ENERGY EFFICIENCY PROJECTS
The two primary financial approaches
Traditional Financing
The borrower pledges to transfer assets (collateral in case of default).
Project Financing
The lender accepts the project itself as collateral.

## Slide 9
Traditional financing or corporate financing
The company implementing the project must demonstrate to the lender that it has:
Sufficient revenue from business activities,
Assets to provide as collateral
In case of default: The lender has the right to seize and sell the company's assets.
FINANCIAL MECHANISMS FOR ENERGY EFFICIENCY PROJECTS

## Slide 10
Project-Based Financing
FINANCIAL MECHANISMS FOR ENERGY EFFICIENCY PROJECTS
Project finance: a preferred financial mechanism for large infrastructure projects
- A few energy efficiency projects: large cogeneration projects
Most projects are funded through a combination of both traditional methods and secured lending approaches.

## Slide 11
Funding for energy efficiency projects
FINANCIAL MECHANISMS FOR ENERGY EFFICIENCY PROJECTS
For energy efficiency projects:
The 'value' of the project lies in the cash flow it generates.
Debt repayment: comes from the avoided energy costs.
The amount of energy cost savings generated is used to repay the investment debt.

## Slide 12
Project-Based Funding
FINANCIAL MECHANISMS FOR ENERGY EFFICIENCY PROJECTS
Higher risk factors: Project finance
Debt repayment cash flow relies solely on the project (unverified savings/revenue), with no "cushion" from the company's overall operations.
Limited recourse and collateral primarily consisting of project assets.
High project completion risk & performance risk.
Dependence on contracts & partners (e.g., power purchase agreements, operation & maintenance contracts, supply agreements, off-takers); complex legal structure.
Numerous relatively high-risk factors are associated with the expected business investment returns, which are not entirely comparable to the relatively low risk of investing in energy efficiency.

## Slide 13
EE PROJECT FINANCING MECHANISMS
Financial instruments
Cash
Financial Institutions Lending to Businesses
Vendor Financing (Equipment Supplier Provides Funding)
Soft Loans and Concessional Financing
Leasing
Dedicated Energy Efficiency Fund
Equity Capital

## Slide 14
RISK MANAGEMENT IN EPC CONTRACTS
  Credit risk
  Financial risk
  Audit and design risk
  Construction risk
  Performance risk
  Customer-related risk

## Slide 15
Question
Which risks should be concerned about first?
Which risk has the greatest impact on EE project success?

## Slide 16
RISK MANAGEMENT IN EPC CONTRACTS
Financial and Market Risk Control
  Rish sources:
  Interest rate hikes; FX volatility (especially for imported equipment); energy price fluctuations – directly impacting cash flow and debt service capacity
  Mitigation:
  Conduct sensitivity analysis for interest/FX/energy prices; use indexation or pass-through clauses in contracts; negotiate risk-sharing among parties.
  Safeguards:
  Use contractual collars/hedging for price risks; establish DSRA to absorb short-term shocks; consider hedging instruments for FX/interest rate where feasible.

## Slide 17
Credit Risk Control – Customer Creditworthiness
RISK MANAGEMENT IN EPC CONTRACTS
  Risk sources:
  Delayed or non-payment by client; weak creditworthiness of the IE; disputes over actual savings – disrupting debt service cash flow
  Mitigation:
  Escrow/lockbox accounts; assignment of receivables; ongoing monitoring of financials and receivables; “take-or-pay” clauses ensuring minimum payment obligations
  Safeguards:
  DSRA covering 3–6 months of debt service; termination fee ladder; step-in rights for lenders/ESCO in case of client default.)

## Slide 18
Control of Design and Construction Risks
RISK MANAGEMENT IN EPC CONTRACTS
  Risk sources:
  Design errors; cost overruns; delays in construction; poor workmanship.
  Mitigation:
  Independent design review; fixed-price/time EPC contracts; strict construction supervision; milestone-based acceptance.
  Safeguards:
  Performance bonds from contractors; CAR/EAR insurance; LDs for delays and defects.

## Slide 19
Performance and M&V Risk Control
RISK MANAGEMENT IN EPC CONTRACTS
  Risk sources:
  Baseline shorter than 12 months, missing seasonal data; changes in operating hours/load; inaccurate measuring devices; disagreement on M&V approach.
  Mitigation:
  Use a baseline of at least 12 months excluding abnormal data; include baseline adjustment clauses when hours/load change; prepare a clear M&V plan (scope, devices, acceptable error margin, dispute-resolution process).
  Safeguards:
  Require OEM performance guarantees; apply LDs (liquidated damages) linked to performance levels; define operational SLAs (response time, reliability, MTBF/MTTR).

## Slide 20
Operational & O&M Risks Control
RISK MANAGEMENT IN EPC CONTRACTS
  Risk sources:
  Lack of preventive maintenance; failures of critical equipment; performance degradation; spare parts shortage; improper operations.
  Mitigation:
  Preventive maintenance plan; CMMS; long-term spare parts agreements; operator training; real-time data monitoring.
  Mitigation:
  Preventive maintenance plan; CMMS; long-term spare parts agreements; operator training; real-time data monitoring.

## Slide 21
Legal & Contractual Risks Control
RISK MANAGEMENT IN EPC CONTRACTS
  Risk sources:
  Incomplete protections in contracts; weak enforceability; change in law; divergent interpretations; incomplete permits/licenses.
  Mitigation:
  Standardized contract templates; independent legal review; include baseline adjustment clauses; clear dispute-resolution procedures.
  Safeguards:
  Step-in rights; termination fee ladder; LDs; mandatory insurance obligations; transparent risk allocation.

## Slide 22
Environmental, Social & Safety (E&S) Risks Control
RISK MANAGEMENT IN EPC CONTRACTS
  Risk sources:
  Non-compliance with environmental laws; community impacts; poor OHS practices; environmental incidents; excessive noise/dust/waste
  Mitigation:
  E&S assessments; environmental & safety management plans; staff training; periodic monitoring and reporting; stakeholder engagement.
  Safeguards:
  Compliance with lender/international E&S standards; third-party liability insurance; right to suspend operations upon material breaches; emergency response plans.

## Slide 23
Customer Behavior Risk Control
RISK MANAGEMENT IN EPC CONTRACTS
  Risk sources:
  Changes in process/hours/load; non-compliance with operating guidance; lack of cooperation in metering/verification; payment deprioritization.
  Mitigation:
  Contractual obligations; change-control procedures; operator training; continuous data monitoring and early-warning triggers.
  Safeguards:
  Take-or-pay clauses; right to suspend services upon breach; KPI-based bonus-malus; escrow/lockbox for savings cash flows.

## Slide 24
GO/NO-GO” CHECKLIST
  Baseline ≥ 12 months with seasonal/abnormal data treated?
  M&V plan is clear (scope, meters, acceptable error, dispute-resolution)?
  Financial model includes sensitivity (interest, FX, energy prices) and minimum DSCR holds under sensitivities?
  Cash-flow controls in place: escrow/lockbox, assignment of receivables, DSRA (3–6 months of debt service)?
  Price mechanics: indexation / pass-through / collar/hedging defined?
  Performance protections: OEM performance guarantees; LDs linked to shortfalls?
  Operations & maintenance: PM schedule, operational SLAs, critical spares and contingency plan?
  Contract terms: step-in rights, termination fee ladder, transparent risk allocation?
  Insurance: CAR/EAR, Business Interruption, third-party liability?
  Legal & E&S: permits in place; environmental-social compliance and reporting/monitoring defined?
Notes: “Go/No-Go” Checklist (English)
Baseline ≥ 12 months with seasonal/abnormal data treated?
M&V plan is clear (scope, meters, acceptable error, dispute-resolution)?
Financial model includes sensitivity (interest, FX, energy prices) and minimum DSCR holds under sensitivities?
Cash-flow controls in place: escrow/lockbox, assignment of receivables, DSRA (3–6 months of debt service)?
Price mechanics: indexation / pass-through / collar/hedging defined?
Performance protections: OEM performance guarantees; LDs linked to shortfalls?
Operations & maintenance: PM schedule, operational SLAs, critical spares and contingency plan?
Contract terms: step-in rights, termination fee ladder, transparent risk allocation?
Insurance: CAR/EAR, Business Interruption, third-party liability?
Legal & E&S: permits in place; environmental-social compliance and reporting/monitoring defined?
Decision guide: ≥ 8/10 “Yes” → proceed to detailed due diligence. < 8/10 → request revisions before moving forward.

## Slide 25
DISCUSSION
(CASE STUDY)
Notes: Divide students into groups for discussion (5 groups/class);
Provide each group with a typical case study description (attached with slides). The instructor will give suggestions and discussion requirements.
Groups discuss for about 5 minutes and present their discussion results within ~3 minutes/group.
(Focus on presenting differences or elaborating on content compared to previous groups.)
The instructor synthesizes the discussion results from all groups.

## Slide 26
Thank you!