## Slide 1
VIETNAM SCALING UP ENERGY EFFICIENCY PROJECT (VSUEE)

## Slide 2
Key features of energy efficiency projects

## Slide 3
TYPES OF ENERGY-EFFICIENT PROJECTS
Types of EE
System optimization
Equipment upgrades
Building an energy management system (EnMS)
Waste heat recovery
Process improvement & system optimization (for compressors, pumps, fans, boilers, etc.);
Eliminating energy losses;
Installing high-efficiency motors (IE3, IE4, IE5);
Installing variable frequency drives (VFDs) with control sensors;
LED lighting, solar-powered lights, etc.;
Establishing an energy management system (following ISO 50001 or internal standards);
Deploying monitoring, tracking, and analysis equipment.
Utilizing waste heat from existing sources (for heating, power generation, etc.).
Page 2
Equipment upgrades
Waste heat recovery
Utilizing waste heat from existing sources (for heating, power generation, etc.).

## Slide 4
TYPES OF ENERGY-EFFICIENT PROJECTS
Waste heat recovery
Equipment retrofitting and upgrading
System optimization
Energy management system

## Slide 5
PROJECT EFFECTIVENESS EVALUATION
Evaluating the effectiveness of an energy-saving project
Economic
Technical
Social and Environmental

## Slide 6
PROJECT PERFORMANCE EVALUATION
Evaluation criteria for energy efficiency projects

## Slide 7
SOME FUNDAMENTAL ISSUES IN PROJECT FINANCE
GENERAL INTRODUCTION
Finance is an important factor determining the success of energy efficiency project implementation.
Cost savings or additional profits must meet or exceed a certain threshold.
Energy efficiency projects must be competitive compared to other projects.
To determine suitable investment options by comparing alternatives to achieve organizational goals.
Project financing is needed to avoid having to invest internal resources for investments in EE projects.

## Slide 8
SOME INDICATORS FOR PROJECT FINANCIAL EFFICIENCY
Interest rate
  When an amount of money is loaned for a specified period (typically one year), a certain percentage must be repaid.
  FV = PV(1 + i)n
Discount rate
  Converts future cash flows into their present equivalent value, adjusting for the time value of money.
  Also referred to as the hurdle rate or cost of capital.
Depreciation
  Allocates the cost of an investment over the predicted lifespan of equipment or processes.
  Depreciation values are used to reduce the recorded value of the investment.
  Accounting value and lifespan may differ from actual/useful life.
Inflation
  Measures the decline in purchasing power of money.
  Typically expressed as an annual percentage increase in costs over time
Residual Value
  The estimated amount recoverable from an asset at replacement time or at the end of its useful life.

## Slide 9
SOME INDICATORS FOR PROJECT FINANCIAL EFFICIENCY
Benefits
  The benefits from an energy efficiency project may include:
  Energy savings;
  Revenue from energy sales;
  Reduced maintenance costs;
  Income from improved quality;
  Income from increased productivity.
Net cash flow
  Equipment procurement costs;
  Installation and construction costs;
  Design & consulting costs;
  Training and technology transfer costs;
  Contingency costs.

## Slide 10
SOME INDICATORS FOR PROJECT FINANCIAL EFFICIENCY
Simple Payback Period (SPP)
Return on Investment (ROI)
Net present value (NPV)
Internal Rate of Return (IRR)
Operating Costs and Equipment Costs

## Slide 11
SOME INDICATORS FOR PROJECT FINANCIAL EFFICIENCY
  The time required to recover the initial investment from cash flows.
  A widely used quantitative method to evaluate the cost-effectiveness of energy efficiency investments.
  Does not consider savings beyond the payback year or the time value of money.
  Formula: Simple Payback Period = Capital Cost / Annual Cash Flow
Simple Payback Period (SPP)
  Expresses the "annual benefits" of a project as a percentage of capital cost.
  Does not require projects to have equal lifespans or cost comparisons.
  Formula: ROI = Net Annual Savings / Project Capital Cost
Return on Investment (ROI)
  Discounts all net benefits at the minimum attractive rate of return (MARR) to determine equivalent present values.
  Net benefits are for the life of the project equipment
Net Present Value (NPV)

## Slide 12
SOME INDICATORS FOR PROJECT FINANCIAL EFFICIENCY
  The discount rate at which the net present value of cumulative benefits from an investment equals the investment cost.
  The higher the IRR value, the more effective the project is.
Internal Rate of Return (IRR)
  Life cycle costs in aggregate will typically exceed the initial equipment investment costs..
Operating costs and equipment costs

## Slide 13
Financial and economic analyses are used by the World Bank to determine a project’s viability. Governments often require similar analyses to assess the impacts of proposed policies, regulations and government programs on public expenditures and societal benefits.
Financial analysis. Used determine an operation’s financial viability from the perspective of the implementing entity. It focuses on cash inflows and outflows associated with the project and uses market prices.
Economic analysis. Determines the operation’s net impact (cost or benefit) on the overall economy and society (at the country and global levels). It uses economic prices which consider opportunity costs to society, presence of government interventions that create market distortions (e.g., taxes, tariffs, subsidies), and externalities.
Financial and Economic Analysis (World Bank)

## Slide 14
FINANCIAL ANALYSIS TECHNIQUES
Technical Assessment
Financial Evaluation
Amount of energy saved
Impact on equipment lifespan and durability
Equipment compatibility with the entire system
Impact on maintenance and upkeep costs
Impact on business operations
Required operational skills and worker attitudes
Equipment installation space
Aesthetic considerations
Simple payback period (Payback)
Net present value (NPV)
Internal rate of return (IRR)

## Slide 15
FINANCIAL ANALYSIS TECHNIQUES
Option | Criterion (1) | Criterion (2) | Criterion (n) | Total score
 | Weight | Weight | Weight | 
Option A |  |  |  | 
Option B |  |  |  | 
Option C |  |  |  | 
Technical Assessment Table

## Slide 16
FINANCIAL ANALYSIS TECHNIQUES
What investors want to know?
When will the investment pay back?
Total value generated?
Profitability per unit of capital?
Simple Payback Period (Payback)
Net Present Value (NPV)
Internal Rate of Return (IRR)

## Slide 17
FINANCIAL CRITERIA ASSESSMENT
When will the investment pay back?
Simple Payback Period (Payback)
The payback period is the length of time required for the project's income to cover or recover the project's investment cost.
The simple payback period does not account for the time value of money.
It is typically only applied to projects with a short payback period (less than 3 years).
Payback period
Years before full recovery
Unrecovered cost at the start of the year
-----------------------------------
Cash flow during the year
=
+

## Slide 18
FINANCIAL ASSESSMENT
When will the investment pay back?
Simple Payback Period (Payback)
 | Cashflow of the project | 
Year | Project A | Project B
0 | ($1,000) | ($1,000)
1 | 500 | 100
2 | 400 | 300
3 | 300 | 400
4 | 100 | 600
Project A |  |  |  |  |  | 
 | Year | 0 | 1 | 2 | 3 | 4
Cash flow |  | -1000 | 500 | 400 | 300 | 100
Cumulative Cash Flow |  | -1000 | -500 | -100 | 200 | 300
Project B |  |  |  |  |  | 
 | Year | 0 | 1 | 2 | 3 | 4
Cash flow |  | -1000 | 100 | 300 | 400 | 600
Cumulative Cash Flow |  | -1000 | -900 | -600 | -200 | 400
For two projects A and B with cash flows given in the table below:
Payback period A = 2.0 + 100/300 = 2.33 years
Payback period B = 3.0 + 200/600 = 3.33 years

## Slide 19
FINANCIAL CRITERIA ASSESSMENT
The total value?
Net Present Value (NPV)
Bt: Annual Benefits
Ct: Annual Costs
i : Discount Rate
Ct
Bt
1
2
n
NPV
IRR
NPV= 0 🡺 IRR
IRR (Internal Rate of Return): This is the appropriate discount rate at which NPV = 0.
NPV > 0: The higher the NPV, the greater the financial efficiency of the project.
NPV ≤ 0: The project is not financially viable.
The selected option is the one with the highest NPV and NPV > 0.

## Slide 20
FINANCIAL CRITERIA ASSESSMENT
Profitability per unit of capital?
Internal Rate of Return (IRR)
NPV1
NPV2
IRR
i
Internal Rate of Return (IRR): The discount rate at which the Net Present Value (NPV) of a project equals zero.
NPV

## Slide 21
FINANCIAL CRITERIA ASSESSMENT
Profitability per unit of capital?
Internal Rate of Return (IRR)

## Slide 22
COMPREHENSIVE ASSESSMENT OF ENERGY EFFICIENCY PROJECTS
(1) Basis for Impact Assessment
(2) Basis for Risk Assessment
(3) Project management and risk management for energy efficiency projects

## Slide 23
COMPREHENSIVE APPRAISAL OF ENERGY EFFICIENCY PROJECTS
Key elements of impact assessment and introduction to approaches used for energy saving decisions:
Establish evaluation objectives
Establish the approach, define baseline aspects, and prepare a plan
Compare energy use and demand before project implementation
Report evaluation results and work with Project operators to implement opportunities
The Project evaluation process begins

## Slide 24
RISK ASSESSMENT
Identify the sources of risk
Determine the pathways and critical points where these risks may arise
Measure the potential consequences of these risks under different scenarios
Provide means to mitigate and address these consequences

## Slide 25
COMPREHENSIVE EVALUATION OF ENERGY EFFICIENCY PROJECTS
  Secure approval from senior leadership and business owners/investors for the energy efficiency project and establish the organizational structure for it.
  Identify the company's energy flows and costs, and develop targets.
Establish strategic goals and conduct a baseline assessment
  Begin with a comprehensive diagram of the proposed project & its financial and energy-related consequences.
Identify the sources of risks
  Determine critical points and pathways associated with various risk-driving factors.
Risk assessment
  Consider risk factors that could threaten the company's mission.
Risk mitigation and prevention
  Determine the conditions under which the project's benefits (or project portfolio's benefits) clearly outweigh the project risks.
  Establish a contract management system to keep risks within acceptable limits.
Project initiation and continuous control

## Slide 26
CAPITAL FUNDING MODELS FOR PROJECT IMPLEMENTATION
Asset-based financing
Retained earnings financing
Debt financing
(Bank loans)
Leasing (Equipment or Financial)
Performance Contract

## Slide 27
CAPITAL FUNDING MODELS FOR PROJECT IMPLEMENTATION
Equipment Supplier
Businesses
Purchase cost
Equipment
Disadvantages
Requires supervision, inspection, and independent verification;
Requires reliable relationships and equipment suppliers;
Limited scope.
Advantages
Easy to implement;
Low cost;
A good way to start commercial energy-saving activities;
Project sustainability can be ensured through independent verification requirements.
Financing through company assets or retained earnings

## Slide 28
CAPITAL FUNDING MODELS FOR PROJECT IMPLEMENTATION
The bank can provide credit for up to 60%-70% of the total project cost;
The funds used to repay the debt are typically generated from the energy savings;
The loan repayment period usually corresponds to the payback period of the energy efficiency project.
Bank Loan (Debt Financing)
Equipment Supplier
Businesses
Purchase cost
Equipment
Bank

## Slide 29
CAPITAL FUNDING MODELS FOR PROJECT IMPLEMENTATION
Reasons for leasing:
Financial Reasons
  With some lease agreements, the entire lease payment may be tax-deductible.
  Some leases allow for "off-balance-sheet" financing, preserving financial creditworthiness.
Risk sharing
  Leasing is suitable for short-term asset use and reduces the risk of owning obsolete equipment.
  Lease agreements involve less risk and liability.
Lease Payments
Leasing Organization
Lessee (Enterprise)
Leased Equipment
Leasing

## Slide 30
CAPITAL FUNDING MODELS FOR PROJECT IMPLEMENTATION
A performance contract
A performance contract is a unique agreement that allows for the implementation of necessary improvements with minimal upfront investment.
The contractor is typically responsible for purchasing and installing the equipment, as well as maintaining it throughout the contract period.
The contractor is compensated based on the performance efficiency of the installed equipment and only after the installed equipment has actually reduced costs.
Energy Service Companies (ESCOs) often serve as contractors in this line of business.

## Slide 31
PREPARING AN INVESTMENT REPORT
 | Energy Audit Report | Investment Grade Audit (IGA) / Feasibility Study Report
Purpose | Assess current energy usage and propose energy saving opportunities | Analyze the financial & economic feasibility of selected solutions following an energy audit
Main content | Collect energy consumption data; Analyze the performance of equipment, production lines, and systems; Identify areas of energy waste; Propose energy conservation measures/solutions. | Calculate investment costs, operational costs, and economic benefits; Conduct financial analysis (NPV, IRR, Benefit-Cost Ratio, Payback Period); Perform socio-economic analysis (social and environmental benefits); Propose financing options.
Result | A list of potential energy-saving opportunities, but without detailed financial viability assurance | A basis for making investment decisions or for seeking funding/loans

## Slide 32
An Investment Report can be prepared by consulting firms or a company's internal personnel and presented to the corporate leadership or financial support institutions. Key contents of the investment report typically include:
(1) The rationale for implementing energy efficiency projects within the organization.
(2) Findings from the energy audit report and proposed energy-saving solutions.
(3) Financial efficiency calculations for the proposed energy-saving measures.
(4) Assessment of other impacts on the business and the environment.
(5) Preliminary financial analysis such as payback and sometimes NPV as well as IRR
PREPARING AN INVESTMENT REPORT

## Slide 33
PREPARING AN INVESTMENT REPORT
(1) Bases for implementing energy efficiency projects at the unit.
Policy on investing in energy efficiency:
As required by law (Construction Law, Public Investment Law, Investment Law)
Awareness of the effectiveness of improving energy efficiency within the unit
Investment resources allocated for energy efficiency projects:
Capital policy for energy efficiency projects
Amount of capital available for use in energy efficiency projects
(2) Results of the energy audit report and proposed energy-saving solutions.
To serve as a basis for investment project activities, enterprises must undergo an energy audit to form the foundation for preparing the investment report.
The results and proposed energy-saving solutions in the audit report are the foundations for preparing the investment report.

## Slide 34
PREPARING AN INVESTMENT REPORT
(3) Calculation of financial efficiency for proposed energy-saving solutions
In the investment report, detailed financial calculations must be performed (Enterprises need to investment grade audit (not just an energy audit) to help prepare the investment report)
Detailed calculation of investment costs and disbursement methods;
Source of capital and cost of capital;
Capital borrowing and debt repayment methods;
Project lifespan;
Depreciation calculation method;
Comprehensive calculation of construction, installation, and commissioning costs for the invested system;
Calculation of annual savings;
Calculation of annual operation and maintenance costs;
Calculation of other project benefits (if any);
Calculation of financial inflows at the project's end;
Calculation of the project's post-tax cash flow according to the cash flow table in the “Financial Analysis Techniques” section;
Calculation of project risks.

## Slide 35
PREPARING AN INVESTMENT REPORT
Solution No. | Solution | Annual Savings |  | Estimated Savings Million VND | Estimated Investment Cost (Million VND)
 |  | GJ/year | MWh/year |  | 
ECM 1 | Improve combustion efficiency by reducing excess gas in the preheater and reducing clinker outlet temperature | 75,424 |  | 2,420 | 3,890
ECM 2 | Improve cooling efficiency by more even distribution of clinker | 95,742 |  | 3,070 | 2,380
ECM 3 | Install an additional cyclone stage for the stage 1 preheater and recover additional heat from exhaust gas | 326,554 |  | 10,480 | 27,000
ECM 4 | Use cooling air to supply the kiln burner | 21,343 |  | 685 | 740
ECM 5 | Generate electricity from waste heat from the kiln cooling section | - | 29,490 | 32,180 | 187,200
ECM 6 | Install inverter for raw material fan (R2S20) - Line 2 | - | 2,080 | 2,040 | 7,200
ECM 7 | Replace inefficient equipment - preheater fan, Line 1 | - | 1,920 | 1,885 | 3,000
ECM 8 | Replace inefficient equipment - raw material fan, Line 1 | - | 1,490 | 1,460 | 3,000
ECM 9 | Install conveyor system for kiln input, Line 1 to reduce energy consumption of the pneumatic conveying system | - | 2,290 | 2,250 | 6,000
ECM 10 | Install inverter for fan at coal mill (P22) - Line 2 | - | 490 | 480 | 600
 | Total | 519,063 | 37,760 | 56,950 | 241,010

## Slide 36
EXAMPLE ANALYSIS
Current status of the system
high oxygen concentration in flue gas
Solution | Oxygen reduction level | Investment cost | Operation cost | Implementation Complexity | Note
Excess Air Reduction | **** | Low | Medium | Low | Requires precise air flow control to avoid incomplete combustion. ¦
Air Distribution Control | *** | Medium | Medium | Medium | Requires modification of the air supply structure and distribution equipment.
Flue Gas Recirculation (FGR) | *** | Medium | Medium | Medium | Requires additional gas recirculation equipment and fans, and control of the recirculation flow
Automatic Combustion Control Optimization | **** | Medium | Medium | Medium | Requires an O₂ sensor system, PLC/DCS, and automatic control

## Slide 37
EXAMPLE ANALYSIS
Calculating energy savings using software
Calculation of the economic and technical efficiency of the project
STT | Parameter | Unit | Formula | Value
I. Baseline data |  |  |  | 
I.1 | Current heat loss | % | A | 21,1%
I.2 | Projected heat loss after implementing the solution | % | B | 15,2%
I.3 | Total fuel consumption in 2024 | Tons/year | C | 23.614
I.4 | Estimated efficiency factor | % | D | 80%
II. Energy Saving Potential |  |  |  | 
II.1 | Amount of fuel saved | Tons/year | E = (A-B)*C*D | 1.115
II.2 | Average fuel price | VND | F | 
II.3 | Cost saving | VND/ year | G=E*F | 
II.4 | Investment cost | VND | H | 
II.5 | Simple Payback Period | Year | J=H/G | 
II.6 | Internal Rate of Return | % | IRR | 
II.7 | Net Present Value (NPV) (over 5 years, discounted at 12% year) | VND | NPV | 
III. Environment |  |  |  | 
III.1 | Conversion to TOE (Tons of Oil Equivalent) | TOE | E=D*0,373 | 415.89

## Slide 39
If an energy efficiency project only meets the technical requirements but has a long payback period and other economic indicators are not feasible, would you decide to invest? And what criteria should be evaluated to make the investment decision for the project?

## Slide 40
1. Re-analyze the project's costs and benefits (materials, labor, machinery, operation, etc.)
2. Analyze and evaluate all benefits brought by the project (environmental, branding, greenhouse gas emission reduction, production efficiency, etc.)
3. Compare and analyze the benefits of the solution compared to lower-technology alternatives
4. Explore funding sources and support from investment funds or joint venture partners to share risks
5. Adjust the project scale, focus on the core part of the project, and eliminate less important components
6. Accept lower economic efficiency to gain benefits in other aspects
7. Postpone and wait for a more appropriate time

## Slide 41
Thank you!