## Slide 1
VIETNAM SCALING UP ENERGY EFFICIENCY PROJECT (VSUEE)

## Slide 2
Business models for EE project implementation, including performance contracting and ESCO implementation

## Slide 3
DEFINITION OF ESCO
  Energy Service Company
An ESCO is an organization that provides services, technical and financial solutions, and implements investment projects on energy efficiency and conservation based on energy performance contracts.
Energy Efficiency Project + EPC = ESCO
ESCO
Notes: Energy service organizations include enterprises as defined by enterprise law and other organizations as defined by relevant laws.
The investment and business activities of energy service organizations are carried out in accordance with the law on enterprises, the law on investment, the law on public-private partnership investment, and other relevant laws.
An energy efficiency contract is formed between the customer and the energy service organization, serving as the basis for the customer to pay the energy service organization when implementing energy saving and efficiency projects.

## Slide 4
CHARACTERISTICS OF ESCO
Contractor
Equipment manufacturer
Government
Financial institution
Energy supplier
Professional technical consulting engineer
ESCO
Contractor
Governments
Equipment manufacturer
Organizations
Financial
Professional technical consulting engineers
Energy suppliers
BUSINESS OWNER

## Slide 5
Contractor
Equipment manufacturer
Government
Financial institution
Energy supplier
Professional technical consulting engineer
ESCO
BUSINESS OWNER
Integrated energy services
  Development
  Identification of Energy Conservation Measures (ECM)
  Engineering Design
  Finance*
  Procurement
  Construction and on-site supervision
  Acceptance
  Capacity building
  Performance guarantee
  Operation and maintenance *
  Monitoring &amp; Evaluation of Savings
* Some ESCO offers
ESCO BUSINESS MODEL – INTEGRATED SERVICES

## Slide 6
TYPES OF ENERGY EFFICIENCY CONTRACTS
Guaranteed Savings Contracts.
Energy savings sharing contracts.
Electricity purchase agreement (Heating).

## Slide 7
SAVINGS GUARANTEE CONTRACT
Guaranteed Savings – How Working Capital Works
Chart: €
| Currently | In the EPC program | After the EPC program
Series 1 | 1 | 0.6 | 0.6
Series 2 | 0 | 0.3 | 0.4
Series 3 | 0 | 0.15 | 0
Current annual costs for business owners
Energy costs and O&M costs
Business owner's bank debt repayments
Financial fees
Investment capital
Business owner's income (optional)
Energy costs and O&M costs
Business owner
benefits
Annual business costs decrease slightly or remain the same

## Slide 8
Payment during construction* (similar to a turnkey arrangement)
Loan to customers (if applicable)
Customer commitment
Financial institution
Customer
ESCO
ESCO implements the solution
Solution implementation time
ENERGY SAVINGS GUARANTEE CONTRACT
Notes: Emphasis:
The timing of payment to the ESCO depends on the contract. Two payment options are typically considered:
Payment during construction (similar to a turnkey arrangement),
Payment after M&V implementation and achievement of the committed savings.

## Slide 9
Energy savings achieved
Customers repay loans directly to financial institutions
Financial institution
Financial
Customer
ESCO
Payback period
ESCO guarantees savings
Savings are used to repay debt and pay ESCO*
M&amp;V
ENERGY SAVINGS GUARANTEE CONTRACT
Notes: Emphasis:
The timing of payment to the ESCO depends on the contract. Two payment options are typically considered:
Payment during construction (similar to a turnkey arrangement),
Payment after M&V implementation and achievement of the committed savings.

## Slide 10
ESCO guarantees:
Savings = or &gt; debt
ESCO pays any shortfall
BANK
Lender
CUSTOMER repays debt
Energy savings:
As per the baseline comparison
CUSTOMER
ESCO
Debt
Energy savings
ENERGY SAVINGS GUARANTEE CONTRACT
Notes: Note: This example applies to payments to ESCO during implementation and during the reimbursement period. If M&V shows that the savings are not guaranteed as committed, ESCO must pay the shortfall.
  Cost: fixed price or additional costs. Savings may exceed the guaranteed amount.
  Guarantee: If the savings achieved fall below the guaranteed amount, the ESCO will compensate the customer for the shortfall.
  Term: The contract has a fixed term.
  Cash flow: The customer's cash flow immediately improves.
  Equipment ownership: Typically, the customer owns the equipment.

## Slide 11
Capital
Business owners invest their own capital or borrow capital to implement projects, or a combination of both.
ESCO has no credit risk.
ESCO can assist in finding sources of capital.
Contract duration
Typically fixed and arranged with debt services (in the case of borrowing).
ENERGY SAVINGS GUARANTEE CONTRACT

## Slide 12
How does the savings rate – working capital work?
Chart: €
| Currently | In the EPC program | After the EPC program
Series 1 | 1 | 0.6 | 0.6
Series 2 | 0 | 0.3 | 0.4
Series 3 | 0 | 0.15 | 0
Current annual costs for business owners
Energy costs and O&M costs
DN pays to ESCO,
ESCO
pays to the bank
Financial fees
Investment capital
Business owner receives (optional)
Energy costs and O&M costs
Business owner
benefits
Annual business costs are reduced or remain the same
SHARED SAVINGS AGREEMENT

## Slide 13
Loan capital
Technical design, construction, acceptance, measurement, and verification
Organization
Financial
Business
Enterprise
ESCO
Construction period
ENERGY SAVINGS SHARING AGREEMENT

## Slide 14
Pay off debt
Measurement and verification, corrective actions
Share savings based on effectiveness
Organization
Financial
Business
business
ESCO
ENERGY SAVINGS SHARING AGREEMENT
Payback Period

## Slide 15
ESCO reimburses by using the costs from the energy savings.
This may be the entire amount or a certain percentage.
Usually compared annually.
Option: accumulated savings ("savings bank").
SHARED SAVINGS AGREEMENT
Notes: Saving accumulation: Some ESCOs stipulate in their contracts that any excess savings in one year go into a virtual "savings bank." The extra savings can be used in future years to offset a lack of savings.
Savings accumulation: Some ESCOs stipulate in their contracts that any excess savings in a given year will be placed into a virtual "savings bank." This extra savings can be used in subsequent years to offset a lack of savings.

## Slide 16
Chauffage (French term) is a type of energy performance contract (EPC) in which the business owner pays the Energy Service Company (ESCO) or contractor a fixed fee for each unit of useful energy (heat, cooling, electricity) supplied to the building.
ESCOs charge for energy processing in different units:
GJ/BTU of heat
GJ/ton of cooling water
kWh of electricity
The ESCO controls the plant's operation and maintenance processes; drafts agreement contracts.
HEATING CONTRACT

## Slide 17
ESCO is responsible for:
Providing energy services (e.g., heating, cooling, hot water),
Operating and maintaining equipment, and
Ensuring efficiency and cost savings (often sharing the savings with customers).
Simply put: instead of paying separately for fuel or electricity, customers pay for the "comfort provided" (e.g., cooling or heating), while the ESCO bears the risk for efficiency and performance.
Contracts can last from 10 to 15 years. Or throughout the lifetime of the energy-efficient equipment.
HEATING CONTRACT
Notes: Key differences:
Heating Contracts: Pay for output energy services (guaranteed supply levels and reliability).
Guaranteed Savings Contracts: Pay based on guaranteed savings (guaranteed energy consumption reduction efficiency).
Shared savings contracts: Pay based on actual TKNL savings shared between the business owner and ESCO

## Slide 18
Power purchase agreement – how does it work?
Chart: €
| Currently
Series 1 | 1 | 0.6 | 0.6 | 60
Series 2 | 0 | 0.3 | 0.3 | 40
Series 3 | 0 | 0.1 | 0.1
Energy costs and O&M costs
Payments to ESCO
Capital
Customer Benefits
Energy costs and O&M costs
ESCO profit
Interest
Customer savings
Business benefits
Energy costs and O&M costs
EPC contract term
During the investment payback period
After the investment capital repayment period
HEATING CONTRACT
Notes: The first column shows the current energy and O&M costs before implementing the energy efficiency solution.
The second column shows the first phase of the heating contract: ESCO implements the solution, and the customer pays ESCO periodically based on the amount of energy supplied (ensuring lower costs than currently, ESCO uses the money paid to repay the principal and interest on the investment).
The third column is the ESCO's profit-making phase, where the customer continues to pay the ESCO after the ESCO has recouped its investment (this phase may be long or short or overlapped with the phase in column 2 depending on the agreement between the two parties).
The final column is after the EPC contract expires, the equipment or system is handed over to the customer for operation and management, and the customer enjoys the savings. This phase may or may not exist depending on the agreement (if the Chauffage contract phase extends throughout the solution's lifecycle, this phase does not exist).

## Slide 19
ESCO implements energy saving/alternative energy solutions
ESCO has the right to operate energy saving systems/equipment
Financial organization
Financial
Business
Enterprise
ESCO
During construction
Cooling/heating center (e.g.)
HEATING CONTRACT

## Slide 20
Customers pay for energy services
ESCO provides energy services
ESCO operates
Organization
Financial
Business
Enterprise
ESCO
ESCO Repayment of loan
Cooling/heating center (e.g.)
HEATING CONTRACT
After construction period

## Slide 21
CHOOSE CONTRACT TYPE – Share savings
For IE:
Advantages
  No/low initial CAPEX; pay from actual savings at an agreed percentage.
  Transfers most performance risk to the ESCO; often includes O&M/operational support.
  Minimal increase in debt on the balance sheet; rapid technology upgrades.
  Transparent if the contract clearly states the sharing ratio, baseline, and M&V plan.
  Must share a portion of savings → net benefits are lower than self-investment.
  Requires close M&V coordination: providing data, allowing measurement, accepting baseline adjustments.
  Changes to functionality/output/processes must follow adjustment terms to avoid disputes (lack of flexibility).
  Long-term commitment; risk of technology/supplier lock-in if flexibility clauses are inadequate.
Challenges
Notes: "Technology lock-in" is the risk that a business becomes "stuck" with a particular technology/solution/vendor for many years, making it difficult or costly to upgrade or switch to a better option later on.

## Slide 22
Advantages
  Revenue is directly linked to savings; revenue can increase when savings exceed the plan.
  Proactive in design–procurement–operation (as agreed), optimizing technology to maximize savings.
  Long-term cooperative relationship; standardize the model to expand the project portfolio.
Challenges
  Requires significant capital/working capital; cash flow is delayed as it only materializes after savings are realized.
  Exposure to performance risk and M&V/baseline adjustment risk; higher M&V and transaction costs.
  Customer credit risk (delayed/non-payment); operational change risk leading to savings shortfalls.
  More complex legal-financial structure than guaranteed contracts; may require insurance/guarantees/risk support mechanisms.
For ESCO:
CHOOSE CONTRACT TYPE – Share savings
Notes: This type of contract often involves more complex legal and financial paperwork than a guarantee contract. To provide peace of mind for both parties, it is sometimes necessary to add a 'safety cushion' such as insurance, guarantees, or risk-sharing funds/mechanisms.

## Slide 23
Advantages
  The ESCO owns the assets and controls operations. Capital costs are typically lower (IE borrows/arranges capital itself); savings are guaranteed – if there is a shortfall, ESCO compensates according to the contract. IE retains all upside if actual savings exceed the guaranteed amount.
Challenges
  IE must arrange financing and record debt; requires a full bidding/procurement process. Requires contract management & M&V capabilities to monitor, verify savings, and enforce the compensation mechanism. Must agree early on: baseline, guaranteed level, adjustment rules when output/capacity changes; may take time if historical data is limited. Commit to operating under the operating conditions to preserve the guarantee.
CHOOSE CONTRACT TYPE – Ensure savings levels
For IE:

## Slide 24
Advantages
  Little or no capital required (IE responsible); ESCO cash flow is typically received according to contract milestones, with little dependence on measured savings (only relevant when considering offsets).
  Lower credit risk than the shared model because the primary payer is the IE based on the fixed contract value.
  Clear scope of guarantees → technical initiative to meet/exceed guarantees.
Challenges
  Guarantee responsibility: if savings fall short, compensation/penalties (liquidated damages) apply.
  Requires clear M&V/baseline adjustments; requires insurance/performance guarantees, sometimes requiring lender "step-in."
  Limited profit (upside mainly belongs to IE), order profit margin may be lower than shared savings.
  High-quality input data is required to establish safety levels.
For ESCO:
CHOOSE CONTRACT TYPE – Ensure savings level
Notes: With a guaranteed contract, if the actual savings exceed the plan, the customer (IE) receives the additional amount. ESCOs typically only receive the agreed-upon fee, so the profit per contract is often lower than in the savings-sharing model.
Step-in (the right to "intervene") is a clause that allows a third party – usually the lender of the ESCO or the customer (IE) – to temporarily "step in" to replace the ESCO to operate/remedy when the ESCO violates important obligations.

## Slide 25
Advantages
  No/low capital investment: shift from investing in equipment to leasing "utilities" (steam, hot/cold water, compressed air, electricity, etc.).
  Predictable cash flow: pay a standby fee + fees based on metered utility usage; suitable for budgeting operating costs.
  Fewer disputes over savings: Pay based on useful output, no need for complex M&V savings.
  Service quality per service agreement: Commitment to temperature/pressure/flow rate; ESCO is penalized if standards are not met.
  Focus on core business operations as ESCO is responsible for the design, operation, maintenance, and safety of the solution.
  Flexible expansion: Additional operation-maintenance services can be purchased for existing systems, including metering and energy management integration.
For IE:
CHOOSE CONTRACT TYPE – Heating

## Slide 26
Challenges
  Long-term commitments: multi-year contracts; carefully review price adjustment and early termination clauses.
  Minimum production commitments (take-or-pay): risk when demand decreases or functionality changes.
  Supplier dependency: risk of service interruptions affecting production; contingency/step-in plans are needed.
  Fuel cost risk: if there is no transparent pass-through/hedging mechanism, the IE may bear the volatility.
  Total cost over the term: total service fees may be higher than self-investment if demand is stable and the IE can borrow cheap capital.
  On-site safety & legal governance: permits, fire safety, environment, area access rights; clearly define responsibility allocation.
  Technology/supplier lock-in: Avoid lock-in through open standards, data rights, and mid-term upgrade/renewal clauses.
  Measurement & acceptance: require a standardized measurement system, periodic inspections, and rules for handling errors/data loss.
CHOOSING THE CONTRACT TYPE – Heating
For IE:
Notes: Price adjustment clause: Include the indices used as benchmarks for price adjustments in the price adjustment clause, such as
  CPI (Consumer Price Index) to compensate for inflation in labor costs, O&M.
  Fuel price index (coal/oil/gas prices announced by the agency/supplier) to pass through fuel fluctuations.
  Exchange rate (if there is a portion of import/computing costs in foreign currency).
  Reference interest rate (SOFR/VNIBOR) for financial fees, if agreed.
  Typical wording:
Take-or-pay is a clause in a service/goods contract stipulating that the customer must pay for a committed minimum volume, regardless of whether they take (consume) the entire volume or not (pay).
  Purpose: to ensure the supplier recovers fixed costs (investment, operational readiness).
  In Chauffage/ESCO: IE usually commits to a minimum monthly/quarterly utility consumption (steam, cold water, compressed air, etc.). If consumption is lower than the commitment, IE still pays for the shortfall.
Pass-through: "Directly pass on" cost fluctuations (usually fuel) to the selling price/service according to a pre-agreed formula. The supplier does not bear the price risk.
  Example: Steam price in month t = Base price + 0.8 × (Coal price_t – Base coal price).
  Advantages: simple, transparent. Disadvantages: the customer (IE) bears the volatility.
Hedging: "price risk mitigation" using financial instruments/commercial terms to fix or limit input prices (oil/gas/electricity, exchange rates, etc.). Risk is partially locked in, in exchange for insurance costs.

## Slide 27
Advantages
  Stable cash flow from long-term contracts, ready capacity fee structure, and energy consumption fees.
  Payment based on measured useful energy, no disputes over baseline or savings levels ⇒ reduced measurement and verification costs.
  Operational autonomy, technical optimization to save fuel and maintenance costs ⇒ increased profit margins.
  ESCOs often collaborate with equipment/technology manufacturers/suppliers.
  Easy to raise capital as the assets formed can be recognized and used as collateral; suitable when investment capital is lacking.
  Ability to expand into multiple "utilities" (steam, hot/cold water, compressed air, electricity, etc.) and sell bundled operation and maintenance services.
  The residual value of assets/at the end of the transfer period can generate additional benefits.
For ESCO:
CHOOSING THE CONTRACT TYPE – Heating
Notes: Advantages for ESCO
Stable cash flow from long-term contracts, ready capacity fee structure, and energy consumption fees.
Payment based on measured useful energy, no disputes over baseline or savings levels ⇒ reduced measurement and verification costs.
Operational autonomy, technical optimization to save fuel and maintenance costs ⇒ increased profit margins.
Easier capital raising as the formed assets can be recognized and used as collateral; suitable when customers lack investment capital.
Capability to expand into multiple "utilities" (steam, hot/cold water, compressed air, electricity, etc.) and bundle operation and maintenance services.
The residual value of the asset/at the end of the transfer period can generate additional benefits.
Risks and challenges for ESCO
High capital requirements, long payback period ⇒ cash flow pressure and financial leverage.
Risk of fuel and material price fluctuations if there is no price transfer mechanism or indexation in the contract.
Production risks when customer demand changes ⇒ requires a minimum purchase commitment mechanism.
Risk of failing to meet service quality commitments (availability rate, temperature/pressure/flow rate); penalties may apply if targets are not met.
Legal, environmental, and safety risks during operation; compliance costs may be high.
Partner-related risks (credit, early termination); asset recovery/relocation upon contract termination is often difficult and costly.
Recommendations for contract design (summary)
Clearly separate capacity fees and energy fees; index fuel prices.
Specify minimum purchase commitments, metering boundaries, and supply quality standards.
Include clauses on legal changes, early termination, and compensation, along with payment guarantee mechanisms.

## Slide 28
Challenges
  High capital requirements, long payback period ⇒ cash flow pressure and financial leverage. Risk of fuel and material price fluctuations if there is no transfer pricing mechanism or indexation in the contract. Production risk when customer demand changes ⇒ requires a minimum purchase commitment mechanism. Risk of failing to meet service quality commitments (availability rate, temperature/pressure/flow rate); penalties may apply if targets are not met. Legal, environmental, and safety risks during operation; compliance costs may be high. Partner-related risks (credit, early termination); asset recovery/relocation at contract end is often difficult and costly.
CHOOSING THE CONTRACT TYPE – Heating
For ESCO:
Notes: Advantages for ESCO
Stable cash flow from long-term contracts, ready capacity fee structure, and energy consumption fees.
Payment based on measured useful energy, no disputes over baseline or savings levels ⇒ reduced measurement and verification costs.
Operational autonomy, technical optimization to save fuel and maintenance costs ⇒ increased profit margins.
Easier capital raising as the formed assets can be recognized and used as collateral; suitable when customers lack investment capital.
Capability to expand into multiple "utilities" (steam, hot/cold water, compressed air, electricity, etc.) and bundle operation and maintenance services.
The residual value of the asset/at the end of the transfer period can generate additional benefits.
Risks and challenges for ESCO
High capital requirements, long payback period ⇒ cash flow pressure and financial leverage.
Risk of fuel and material price fluctuations if there is no price transfer mechanism or indexation in the contract.
Production risks when customer demand changes ⇒ requires a minimum purchase commitment mechanism.
Risk of failing to meet service quality commitments (availability rate, temperature/pressure/flow rate); penalties may apply if targets are not met.
Legal, environmental, and safety risks during operation; compliance costs may be high.
Partner-related risks (credit, early termination); asset recovery/relocation upon contract termination is often difficult and costly.
Recommendations for contract design (summary)
Clearly separate capacity fees and energy fees; index fuel prices.
Specify minimum purchase commitments, metering boundaries, and supply quality standards.
Include clauses on legal changes, early termination, and compensation, along with payment guarantee mechanisms.

## Slide 29
Which type of contract should you choose?
A guaranteed savings contract or a shared savings contract?
DISCUSSION

## Slide 30
COMPARISON OF CONTRACT TYPES
Criteria | Guaranteed Savings | Shared Savings
Funding | Customers prepare their own capital/or borrow from banks. | ESCO arranges capital (usually still borrows from banks/project finance).
Cash Flow/Repayment | Customers pay ESCO based on service fees/performance; customers repay the bank loan (if any). | ESCO recovers capital through a share of actual savings until the end of the repayment period/profit.
Core Commitment | ESCO guarantees a minimum savings level; ESCO compensates for any shortfall. | No minimum guarantee; shares based on measured savings.
Performance Risk | Primarily on ESCO. | Primarily on ESCO, plus production/operational volatility risk due to recovery through savings.
Partner credit risk | Customer delays/fails to pay. | Customers not transferring their share.
M&V (Measurement & Verification) | Simpler/less contentious due to guaranteed thresholds; baseline adjusted moderately. | More stringent, dependent on baseline and operational adjustments → higher risk of disputes.
Contract complexity | Average; deficiency clauses, standard M&V. | High; requires sharing formulas, baseline adjustments, etc.
Bank acceptance | Typically easier access to loan capital (secured savings). | Access to loan capital depends heavily on customer creditworthiness and M&V quality; often requires additional guarantees/collateral.
Ownership & O&M | Flexible; O&M by ESCO or customer. | ESCO typically handles O&M to control performance.

## Slide 31
Thank you!