## Slide 1
Module 16:
Investment Grade Audit (IGA)

## Slide 2: INVESTMENT GRADE AUDIT – IGA
An Investment-Grade Energy Audit (IGA) is a comprehensive, detailed analysis of a facility's energy use, designed to identify cost-effective energy efficiency measures (EEMs) and provide financial-grade projections for energy savings, return on investment (ROI), and risk assessment.
IGAs are typically conducted before major energy efficiency investments, especially for performance contracting, financing, or large-scale retrofits.

## Slide 3: OBJECTIVES OF IGA
Provide Accurate and Reliable Data: Enable businesses, investors, and financial institutions to make well-informed investment decisions.
Evaluate Technical Feasibility: Assess whether the energy technology, equipment, and systems are appropriate and efficient, including specifying details of equipment characteristics and costs.
Verify Financial Feasibility and Prepare Detailed Financing Plan: Ensure the project yields expected profitability, a suitable return on investment (ROI), and develop a comprehensive financing plan.
Minimize Investment Risks: Identify potential risks and propose measures to mitigate them.
Develop an Implementation Roadmap: Create a detailed plan outlining the project timeline and financial requirements.
Notes: Slide 3 should include “specify details of equipment characteristics and costs” also in addition to verify Financial Feasibility, it should include Prepare Detailed Financing Plan

## Slide 4: WHEN TO CONDUCT IGA (Investment-Grade Audit)
Before Project Implementation: Conducted prior to making investment decisions for a project.
Applicable to Large Investment Projects: Typically performed for projects requiring significant capital and utilizing funds from financial institutions.
Reasons to Conduct IGS Before the Project:
1. Provide Necessary Information for Investment Decisions: Helps stakeholders make informed choices.
2. Identify the Most Effective Energy-Saving Measures: Ensures the optimal use of resources.
3. Accurate Forecast of Costs and Payback Period: Gives investors a comprehensive view of the project before proceeding.
4. For Projects Seeking External Financing: Often required when a project depends on funding from external sources.
5. Meets Financial Institution Requirements: Includes detailed information necessary for bank loans and financing approvals.

## Slide 5: The different of type of Energy Audits
Preliminary Energy Audit: Provides an overview without in-depth financial and technical details. It is the initial step before conducting an IGA.
Detailed Energy Audit: Focuses on identifying energy efficiency measures but lacks in-depth financial analysis as in IGA.
Investment Grade Audit (IGA): The highest level, offering a comprehensive, detailed analysis, including technical, financial, and risk assessment of proposed energy-saving measures.
As an extension of the detailed audit
Notes: • Slide 5 is great! This should be used to replace the Slide in Module 15 which shows 4 audit levels.

## Slide 6: Detailed Energy Audit and Investment-Grade Audit (IGA)
Information obtained from a detailed energy audit (DEA):
Analysis of current energy usage and operational costs of the baseline scenario.
Examination of equipment, systems, and operations to identify energy-saving opportunities.
Evaluation of the type and potential savings, including guaranteed savings.
Additional components included in an IGA:
Financial requirement estimates for implementing IGS, including project cash flow projections.
Development of methods to verify and validate savings levels and any additional costs for implementing measures.
Detailed equipment specification
Possible bidding documents for procuring equipment
Detailed project implementation plans.
Maintenance requirements.
Notes: • On Slide 6, IGA does NOT include and energy service agreement - that follows AFTER the IGA is completed. But it should include detailed equipment specification (and possible bidding documents for procuring equipment)

## Slide 7: Key Components of an IGA
Pre-Audit Phase (Planning & Data Collection)
On-Site Assessment (Fieldwork & Data Collection)
Energy Savings Opportunities & Cost-Benefit Analysis
Implementation Roadmap & Action Plan
Final Report & Presentation
Notes: • Change maintenance to operation and maintenance - same in Slide 7 and 9

## Slide 8: 1. Pre-Audit Phase (Planning & Data Collection)
A. Initial Assessment & Project Scope
  Define audit objectives (e.g., cost savings, carbon reduction, operational efficiency)
  Identify key stakeholders (e.g., facility managers, finance teams, ESCOs, utility providers)
  Determine the level of detail required for financing or investment purposes.
B. Utility Bill & Historical Energy Data Analysis
  Collect 12–36 months of utility bills (electricity, gas, water, steam)
  Analyze energy consumption trends (peak demand, seasonal variations).
  Identify benchmarking comparisons (e.g., ENERGY STAR Portfolio Manager, ASHRAE 90.1).
C. Site Information & Equipment Inventory
  Gather building schematics, construction records, and equipment manuals.
  Identify existing HVAC, lighting, motors, pumps, compressed air, boilers, process systems.
  Evaluate control systems & automation technology.
Notes: • Change maintenance to operation and maintenance - same in Slide 7 and 9

## Slide 9: 2. On-Site Assessment (Fieldwork & Data Collection)
A. Walk-Through & Energy Systems Inspection
  Conduct a physical inspection of the facility's major energy-consuming systems.
  Interview operations and maintenance (O&M) staff to understand system issues and anomalies.
  Identify operational inefficiencies (e.g., overheating, underutilized equipment, outdated controls).
B. Metering & Measurement (Real-Time Data Collection)
  Install temporary data loggers and submeters (if required)
  Conduct power quality analysis and harmonic distortion tests for electrical loads.
  Use thermal imaging cameras for heat loss in building envelopes.
  Monitor airflow, temperature, and humidity for HVAC optimization.
Notes: • Change maintenance to operation and maintenance - same in Slide 7 and 9

## Slide 10: 2. On-Site Assessment (Fieldwork & Data Collection)
C. Lighting & Controls Audit
  Identify inefficient lighting systems and control settings.
  Measure light levels (lux/lumens) against industry standards.
  Evaluate opportunities for LED upgrades and daylight harvesting.
D. HVAC & Mechanical Systems Analysis
  Measure airflow rates, temperature setpoints, and efficiency levels.
  Assess boiler, chiller, and furnace performance.
  Identify opportunities for variable frequency drives (VFDs), economizers, or heat recovery.
E. Process & Industrial Equipment Efficiency
  Evaluate compressed air systems, refrigeration, steam systems, motors, and drives.
  Look for leaks, pressure losses, and inefficiencies in energy-intensive processes.
  Identify waste heat recovery potential.

## Slide 11: 3. Energy Savings Opportunities & Cost-Benefit Analysis
A. Identify Energy Efficiency Measures (EEMs)
  Shortlist low-cost, medium-cost, and capital-intensive efficiency upgrades.
  Categorize measures by payback period and savings potential.
B. Financial & Economic Analysis
  Annual Energy Savings (kWh, MMBtu, water savings).
  Project Costs (materials, labor, engineering, permitting).
  Simple Payback Period (initial cost ÷ annual savings).
  Net Present Value (NPV) and Internal Rate of Return (IRR).
  Lifecycle Cost Analysis (LCCA);
  Cash Flow Analysis (including tax benefits, incentives, and rebates).
C. Risk Assessment & Sensitivity Analysis
  Evaluate potential risks and uncertainties affecting projected savings.
  Perform sensitivity analysis on energy price fluctuations and equipment performance.
  Assess impact of operational changes and occupant behavior on savings.
Notes: A. Identify Energy Efficiency Measures (EEMs)
• Shortlist low-cost, medium-cost, and capital-intensive efficiency upgrades.
• Categorize measures by payback period and savings potential.
• Examples of EEMs:
o Lighting retrofits (e.g., LED conversion).
o HVAC upgrades (e.g., replacing old chillers, demand-controlled ventilation).
o Building envelope improvements (e.g., insulation, window glazing).
o Smart automation (e.g., advanced energy management systems, IoT-based monitoring). o Renewable energy integration (e.g., solar PV, battery storage).
B. Financial & Economic Analysis
• Calculate:
o Annual Energy Savings (kWh, MMBtu, water savings).
o Project Costs (materials, labor, engineering, permitting).
o Simple Payback Period (initial cost ÷ annual savings).
o Net Present Value (NPV) and Internal Rate of Return (IRR).
o Lifecycle Cost Analysis (LCCA) (incorporating maintenance and replacement costs).
o Cash Flow Analysis (including tax benefits, incentives, and rebates).
C. Risk Assessment & Sensitivity Analysis
• Evaluate potential risks and uncertainties affecting projected savings.
• Perform sensitivity analysis on energy price fluctuations and equipment performance.
• Assess impact of operational changes and occupant behavior on savings.

## Slide 12: 4. Implementation Roadmap & Action Plan
A. Prioritization of Energy Efficiency Measures
  Rank measures by:
    Cost-effectiveness (ROI, NPV, IRR).
    Feasibility (technical complexity, installation time)
    Strategic alignment (sustainability goals, compliance with regulations)
B. Phased Implementation Strategy
  Define short-term, mid-term, and long-term action plans.
  Develop a retrofit timeline with project milestones.
  Identify funding mechanisms (ESCO financing, performance contracts, utility rebates, green bonds).
C. Measurement & Verification (M&V) Plan
  Establish baseline energy performance for tracking savings.
  Define M&V protocols using IPMVP (International Performance Measurement & Verification Protocol).
  Outline post-project monitoring and reporting requirements.
Notes: A. Prioritization of Energy Efficiency Measures
• Rank measures by:
o Cost-effectiveness (ROI, NPV, IRR).
o Feasibility (technical complexity, installation time).
o Strategic alignment (sustainability goals, compliance with regulations).
B. Phased Implementation Strategy
• Define short-term, mid-term, and long-term action plans.
• Develop a retrofit timeline with project milestones.
• Identify funding mechanisms (ESCO financing, performance contracts, utility rebates, green bonds).
C. Measurement & Verification (M&V) Plan
• Establish baseline energy performance for tracking savings.
• Define M&V protocols using IPMVP (International Performance Measurement & Verification Protocol).
• Outline post-project monitoring and reporting requirements.

## Slide 13: 5. Final Report & Presentation
A. Comprehensive Energy Audit Report
  Executive Summary (key findings, savings potential, recommended measures).
  Energy Baseline Analysis (current consumption trends, benchmarks).
  Technical Findings & EEMs (energy modeling results, ROI analysis).
  Financial Feasibility & Risk Analysis (payback periods, sensitivity analysis).
  Implementation Roadmap (step-by-step execution plan).
  M&V Strategy (methods for validating energy savings).
  Appendices (technical documentation, metering data, equipment specs).
B. Stakeholder Presentation
  Present findings to decision-makers (e.g., facility managers, investors, CFOs).
  Address questions on financial viability and implementation logistics.
  Secure approval for moving forward with selected energy efficiency projects.
Notes: A. Comprehensive Energy Audit Report
The IGA report includes:
• Executive Summary (key findings, savings potential, recommended measures).
• Energy Baseline Analysis (current consumption trends, benchmarks).
• Technical Findings & EEMs (energy modeling results, ROI analysis).
• Financial Feasibility & Risk Analysis (payback periods, sensitivity analysis).
• Implementation Roadmap (step-by-step execution plan).
• M&V Strategy (methods for validating energy savings).
• Appendices (technical documentation, metering data, equipment specs).
B. Stakeholder Presentation
• Present findings to decision-makers (e.g., facility managers, investors, CFOs).
• Address questions on financial viability and implementation logistics.
• Secure approval for moving forward with selected energy efficiency projects.

## Slide 14: STEPS TO PERFORM IGA
Collect energy consumption data of the facility: Detailed description of energy data (consumption, operating costs, equipment used).
Technical and financial analysis of the solutions.
Risk assessment and implementation planning.
Site Survey: Perform on-site inspections of the project to evaluate system performance and identify opportunities for improvement.ext
Identify potential energy saving opportunities.
Reports and recommendations: Summarize the results and make recommendations for improvement solutions.

## Slide 15: IGA REPORT FORM
General Information:Services, consumption, habits
Proposed EE measures: Calculate savings
Financial options and cash flow of the project:
Calculation of feasible financial expenditures of the project Analysis of sensitivity options
Inspection and Monitoring Plan Detailed plan for project implementation Operation and Maintenance Requirements

## Slide 16: ESSENTIAL INFORMATION
Financial options
  Project financing sources Requirements of financial institutions Loan Guarantee/Mortgage Project cash flow
Performance Contract
  Contract type (guaranteed or savings sharing) Details of the service provider
Measurement and Validation Plan
  Baseline plan Methods used to calculate savings
Cost of equipment
  Quotation of the main equipment (spending budget) Details of the equipment supplier Device Warranty
Maintenance
  Maintenance contract information

## Slide 17: Conclusion
Purpose of IGA: An Investment-Grade Energy Audit (IGA) is a highly detailed and financially rigorous evaluation that provides actionable recommendations for energy efficiency upgrades with verified savings and return on investment.
Methodology of IGA: Conducts on-site assessments, collects real-time data, and performs in-depth financial analysis.
Benefits of IGA: IGA helps businesses and institutions make informed investment decisions that enhance sustainability, reduce operational costs, and improve energy resilience

## Slide 18
EXAMPLES OF CASH FLOWS AND FINANCING SOURCES OF SOME EE PROJECTS

## Slide 19
Thank you!