## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISES
Technical staffs
Module 15:
Renewable Energy for Industrial Enterprises (IEs)
Module 16:
Solar energy for IEs

## Slide 2: CONTENT
1. Concept and forms of Renewable Energy
Concept and definition of renewable energy according to legal documents, types of renewable energy...
2. Legal basis, orientation and policies for RE development in Vietnam
Documents on policies, development goals, electricity purchase and sale prices
3. The Role of RE in Green Transition, Sustainable Development, …
The role, potential, and trend of applying renewable energy in business production of enterprises for the goal of green development, reducing greenhouse gas emissions, and sustainable development.
4. Challenges of using RE in the Industrial Sector
Advantages and disadvantages of renewable energy forms, challenges, advantages and difficulties
5. Some examples of Solar Energy applications
Focus on Paper and Pulp, Textile, Other

## Slide 3
1. Concept and forms of Renewable Energy

## Slide 4: CONCEPT OF RENEWABLE ENERGY
1. International Energy Agency (IEA)
Renewables, including solar, wind, hydropower, biofuels and others, are at the centre of the transition to less carbon-intensive and more sustainable energy systems.
2. The International Renewable Energy Agency (IRENA)
IRENA promotes the widespread adoption and sustainable use of all forms of renewable energy, including Bioenergy, Geothermal, Hydropower, Ocean, Solar and Wind energy, in the pursuit of sustainable development, energy access, energy security and low-carbon economic growth and prosperity.
3. According to Law No. 50/2010/QH12 on Using Energy Economically and Efficiently
Renewable energy resources include hydropower, windpower, sunlight, geothermal, biofuels, and other renewable energy resources.

## Slide 5: FORMS / SOURCES OF RENEWABLE ENERGY
1. Solar Energy
Photovoltaic - PV, Solar Thermal Power - CSP & Thermal – Solar thermal
2. Wind Energy
Offshore / Onshore Wind Power – Offshore / Onshore
3. Hydro Power
4. Geothermal Energy
5. Ocean Energy
Water Tidal – Tidal, Wave – Wave
6. Hydrogen Energy (H2)
Green hydrogen – electricity stool water from renewable energy
7. Bio Energy
Biogas / Biomass / Biodiesel

## Slide 6: THE ROLE OF RENEWABLE ENERGY IN GREEN TRANSFORMATION
Green Transformation is a term that refers to efforts to achieve a sustainable and environmentally friendly future. This concept includes a set of policies, strategies and practices with the aim of ensuring economic, social and environmental sustainability.
The main goals of green transformation include increasing energy efficiency, reducing carbon emissions, promoting sustainable use of natural resources, minimizing environmental pollution and enhancing social participation.

## Slide 7: BENEFITS OF GREEN TRANSFORMATION FOR BUSINESS
Enhance brand awareness
Employee morale satisfaction
Increase investment opportunities
Improve productivity
Reduce waste and reduce costs
Notes: Vietnamese enterprises are increasingly recognizing the strategic benefits of green transformation. With growing awareness of environmental regulations like CBAM, many businesses are committing to energy efficiency, waste reduction, and sustainability as core strategies—not only to remain competitive globally but also to attract investment, enhance brand value, and improve employee engagement.

## Slide 8
2. Legal basis, orientation and policies for RE development in Vietnam

## Slide 9: LEGAL BASIS – Orientation for RE development in Vietnam
Electricity Law No. 28/2004-QH11: Promotes the exploitation and utilization of new and renewable energy sources for power generation.
Law on Efficient and Economical Use of Energy No. 50/2010/QH12: Encourages the development of renewable energy.
Decision No. 432/QĐ-TTg: Vietnam’s Sustainable Development Strategy for the 2011–2020 period.
Decision No. 2068/2015/QĐ-TTg: Vietnam’s Renewable Energy Development Strategy to 2030, with a vision to 2050.
Decision No. 896/QĐ-TTg: National Climate Change Strategy to 2050.
Decision No. 1393/QĐ-TTg: National Green Growth Strategy.

## Slide 10: LEGAL BASIS – Orientation for RE development in Vietnam
Resolution No. 55-NQ/TW The Politburo's Resolution on Strategic Orientation for Energy Development to 2030, with a vision to 2045
Decision No. 500 /QD-TTg : National power development plan for the period 2021 - 2030, vision to 2050 (PDP VIII).
Decision No. 280/QD-TTg : promulgating the National Program on economical and efficient use of energy for the period 2019 - 2030 .
VNEEP 3 program : An important factor contributing to ensuring Vietnam's energy security in the new development stage . This goal is divided into 02 stages:
Phase 2019 -2025 : save 5 -7% of total energy
Phase 2026 – 2030 : save 8 – 10% of total energy

## Slide 11: POWER PLAN VIII – REDUCTION ENERGY DEVELOPMENT GOALS

## Slide 12: CURRENT STATUS OF VIETNAM'S ELECTRICITY SOURCE
Over the past 10 years, Vietnam's electricity industry has developed and grown rapidly thanks to the country's economic development and the increase in electricity demand. During this period, the electricity system mainly relied on coal, gas and hydroelectric power plants .
Vietnam's installed power capacity (Source: Institute of Energy)
Coal

## Slide 13
3. The Role of RE in Green Transition, Sustainable Development

## Slide 14: RENEWABLE ENERGY POTENTIAL OF VIETNAM
1
221GW
Onshore wind power
4
77.4GW
Solar water power
2
600GW
Offshore Wind Power
5
48.2GW
Rooftop solar
3
837.4GW
Ground mounted solar power
6
7GW
Biomass electricity (Electricity produced from waste, solid waste 1.8GW)
Orientation to strongly develop offshore wind power combined with other types of renewable energy ( solar energy , onshore wind energy ...) to produce new energy (hydrogen -H2 , green ammonia -NH3 ...) to serve domestic demand and export.

## Slide 15: ELECTRICITY PRICE POLICY IN RENEWABLE ENERGY SECTOR
Grid- connected solar power 2,083 VND/kWh (9.35 cents )
Solar power according to net energy compensation mechanism
SOLAR POWER (Decision 11)
Floating solar power 1,783 VND /kWh (7.69 cents)
Ground solar power1,644 VND /kWh (7.09 cents)
Rooftop solar panels 1,943 VND /kWh (8.38 cents
SOLAR POWER (Decision 13)
On-shore: 1,928 VND /kWh (8.5 cents)
Off-shore: 2,223 VND /kWh (9.8 cents)
WIND POWER (Decision 39)
The electricity selling price for the cogeneration (heat-electricity) project is 5.8 cents/kWh.
BIOMASS ELECTRICITY (Decision 24)
Price buy : 1,614 VND /kWh (7.8 cents)
State support price: 207 VND/kWh
WIND POWER (Decision 37)
Cogeneration (heat-electricity) project: 1,634 VND/kWh (7.03 cents/kWh)
Other project: 1,968 VND/kWh (8.47 cents/kWh)
BIOMASS ELECTRICITY (Decision 08)

## Slide 16: POTENTIAL OF RE APPLICATION IN INDUSTRIAL
1
Solar Energy
Solar voltage (PV)
4
Biomass Energy
Combustion and disposal of by-products in industry
2
3
Solar Energy
Hot water
Solar Energy
Heat Drying

## Slide 17
1
Solar Energy
Solar voltage (PV)

## Slide 18: SOLAR ENERGY
Solar Power
Photovoltaic Technology (Solar Photovoltaic, PV)
Concentrating Solar Power (CSP)
Solar Heat
Solar themal – Solar heat
Heat recovery serves the following purposes: drying, heat supply support, etc.
Regarding technology:
Solar energy uses technologies that convert sunlight into electricity or thermal energy for different purposes.
1

## Slide 19
SOLAR RADIATION INTENSITY AND SUNSHINE HOURS BY REGION
TT | Territory | NLM density T kWh/m 2 .day | Number of sunshine hours hours/year
1 | Northeast | 3.3 – 4.1 | 1600 – 1750
2 | Northwest | 4.1 – 4.9 | 1750 – 1800
3 | North Central Coast | 4.6 – 5.2 | 1700 – 2000
4 | Central Highlands and South Central Coast | 4.9 – 5.7 | 2000 – 2600
5 | Southern Vietnam | 4.3 – 4.9 | 2200 – 2500
 | National average | 4.6 | 1700 – 2500

## Slide 20
TYPES OF SOLAR POWER TECHNOLOGY

## Slide 21
SOLAR POWER (PV) PRINCIPLE
The photoelectric effect occurs when photons in light have enough energy to free electrons from atoms or molecules in a material, creating an electric current .

## Slide 22
CHARACTERISTIC
Regional Differences in Solar Radiation:
Southern Vietnam: Solar radiation levels remain stable throughout the year.
Northern Vietnam:
High solar radiation during summer and autumn, comparable to the southern region.
Lower solar radiation during winter and spring, with moderate levels.
Renewable Potential: Solar energy is an inexhaustible renewable resource, generated from sunlight (solar radiation)
Variety in Scale, Capacity, and Application: Solar power projects can be implemented on both large/industrial scales (solar power plants) and small scales (rooftop solar systems).
Weather Dependence: The performance of solar panels depends on weather conditions, which affects the daily electricity output of a solar power system.

## Slide 23
01
No noise and no emissions during operation
02
Solar panel lifespan is more than 25 years and recyclable
03
The system is carried out in modules, which can be integrated to raise the capacity easily​​
04
Solar power (PV) can be installed on rooftops, on the ground – land with no economic value, on water
05
The implementation schedule of solar power projects is short, reducing project management costs compared to some other forms of renewable energy
ADVANTAGE OF SOLAR POWER

## Slide 24
01
Dependent on weather conditions, the transmitting power is unstable and fluctuating
02
At night (no sunlight), solar power is equal to "zero"
03
Depending on the purpose of use, the system may require a storage system, increase investment costs, reduce payback time.
04
Some thin-film solar panel technologies contain semiconductors that are harmful to the environment (the proportion of this technology in the market is very small)
05
Appropriation of land fund compared to some other forms of renewable energy (wind power)
DISADVANTAGES OF SOLAR POWER

## Slide 25
01
Solar Rooftop
02
Ground mounted Solar Power
03
Floating Solar power Plant
Decision 13: Rooftop solar power system is a solar power system with photovoltaic panels installed on the roof of a construction work and has a capacity of no more than 01 MW, directly or indirectly connected to the power grid with a voltage level of 35 kV or lower of the Electricity Buyer.
Decision 13: Ground-mounted solar power projects are grid-connected solar power projects except for projects specified in Clause 7 of this Article.
Decision 13: Floating solar power project is a grid-connected solar power project with photovoltaic panels installed on a structure floating on the water surface.
TYPES OF SOLAR POWER (PV)

## Slide 26
PHOTOVOLTAIC EFFICIENCY (SOLAR CELL)

## Slide 27
https://www.cleanenergyreviews.info/blog/most-powerful-solar-panels
PHOTOVOLTAIC EFFICIENCY (SOLAR PANEL/ MODULE)

## Slide 28
PMT Panel 500Wp = Block Weight 28Kg
QHD98: In 2030, DMT = 12,836 MW = 12,836,000 KW x (2x28Kg) = 718,816,000 Kg ~ 719 thousand ton
By 2050, solar power will be 189.3 GW => total block quantity PMT panels are install set , wish Calculated : 10.6 million tons​
( Source : IRENA: End-of-life management Solar Photovoltaic Panels)
SOLAR PANEL (PV) RECYCLING PROCESS

## Slide 29
Using these technologies for crystalline silicon (Si) solar panels, several studies have reported that it is possible to recover over 80% of the main materials from an expired solar panel.
For thin-film solar panels, First Solar (USA) has announced a recovery rate of 95% – 97% of the Cd (cadmium) and Te (tellurium) elements from thin-film solar panels.
SOLAR PANEL (PV) RECYCLING PROCESS

## Slide 30: TYPES OF SOLAR POWER TECHNOLOGIES & SYSTEM CONFIGURATIONS
Three Main Types of Solar Power Technologies & Configurations
1. Standalone Solar Power System (Stand-Alone)
• Application: Remote areas, islands, locations without electricity grids
• No connection to the power grid, uses battery storage system
• High investment cost, long payback period
• Maintenance costs required (battery replacement when lifespan ends)
2. Grid-Tied Solar Power System (On-Grid)
• Application: Electricity consumers (especially industrial sectors)
• Connected and synchronized with the power grid, no battery storage system
• Not dependent on load demand
• Reasonable investment cost, acceptable payback period
• Scalable, allows capacity expansion, interaction with the grid, and surplus power sales to EVN (Vietnam Electricity)
3. Hybrid Solar Power System
• Integrates multiple energy sources (wind, diesel generators, etc.)
• Flexible and diverse design, tailored to usage needs
• High investment cost, long payback period
• Requires maintenance costs (if battery storage is included)

## Slide 31
STAND ALONE / OFF GRID SOLAR SYSTEM

## Slide 32
GRID-CONNECTED SOLAR POWER SYSTEM
(WITH OR WITHOUT EXPORT DEVICE)

## Slide 33
HYBRID SOLAR POWER SYSTEM
(INVERTER HYBRID INTEGRATED WITH GRID CONNECTION)

## Slide 34
SOLAR POWER PLANT

## Slide 35: INTRODUCTION TO DECREE 58/2025/NĐ-CP
DETAILED REGULATIONS ON SEVERAL ARTICLES OF THE LAW ON ELECTRICITY REGARDING THE DEVELOPMENT OF RENEWABLE ENERGY AND NEW ENERGY ELECTRICITY
(issued March 3, 2025)
Chapter III – Development of Self-Produced, Self-Consumed Electricity from Renewable and New Energy Sources
Section 2 – Development of Rooftop Solar Power for Self-Production and Self-Consumption
Article 13 – Policies to Encourage Development
Construction works that comply with laws on investment, construction, land, environmental protection, safety, and fire prevention and fighting may install rooftop solar power systems for self-production and self-consumption.

## Slide 36: INTRODUCTION TO DECREE 58/2025/NĐ-CP (cont)
Article 14 – Mechanism for Purchasing and Selling Surplus Electricity
The purchase price for surplus electricity is the average market electricity price of the preceding year as announced by the electricity market transaction operating unit, but must not exceed the maximum price level in the ground-mounted solar price bracket.
Rooftop solar power systems installed on public property for self-production and self-consumption are not permitted to sell surplus electricity.
Quote: “Entities specified in Clause 1 of this Article may sell surplus electricity to the Surplus Power Buyer, but the volume must not exceed 20% of the electricity output at the rooftop solar system’s output point based on solar radiation intensity.”
If the surplus electricity fed into the Surplus Power Buyer’s grid exceeds 20%, only 20% of that output will be paid for.
Article 15 – Notification of Power Source Development
Organizations or individuals developing rooftop solar power for self-production and self-consumption with an installed capacity of less than 1,000 kW, connected to the national electricity system, and not registering to sell surplus electricity must send a Notification (Form No. 02) in the Annex of this Decree to: The provincial Department of Industry and Trade; The electricity unit, Local authorities managing construction and fire prevention and fighting. This is for management, monitoring, and guidance in compliance with legal regulations.

## Slide 37: INTRODUCTION TO DECREE 58/2025/NĐ-CP (cont)
Article 16 – Entities Required to Register Development and Authority to Issue Development Registration Certificates
Registration is required for:
Organizations or individuals developing power sources with an installed capacity of 1,000 kW or more.
Organizations or individuals developing power sources with an installed capacity of less than 1,000 kW but registering to sell surplus electricity to the Surplus Power Buyer (excluding households).
The total installed capacity registered under Point a and Point c, Clause 1 of this Article must not exceed the capacity allocated to the locality in accordance with power development planning laws.
The Department of Industry and Trade is the competent authority to issue the Certificate of Registration for Power Source Development to entities specified in Clause 1 of this Article.

## Slide 39
CALCULATE SOLAR POWER OUTPUT PER DAY
E = A x r x H x PR
Parameters:
• E: Daily generated electricity (kWh/day)
• A: Solar panel area (m²) ~ 2.4m² per panel
• r: Solar panel efficiency (%) ~ 20%
• H: Average daily solar irradiation (kWh/m².day) ~ 4.6 kWh/m².day
• PR: System performance ratio (%) ~ 90%
Example Calculation (1 kWp Solar System)
A 1kWp solar array consists of two 500Wp panels. Each panel has dimensions: 2.2m × 1.1m = 2.4m². Total array area: 4.8m².
E = 4.8m2 x 20.4% x 4.6kWh/m2.day x 90% = 4 kWh/ day
Energy Loss Factors:
1. Inverter losses: 1% - 2%
2. Temperature losses: 3% - 5%
3. DC cable losses: 1% - 3%
4. AC cable losses: 1% - 3%
5. Shading losses: 0% - 20%
6. Low irradiance losses: 3% - 5%
7. Dirt, dust, and maintenance losses: ~1%
Notes: không dùng số giờ nắng để tính 1kwp tạo ra 4kwh/ngày hay 1700 đến 2000 giờ nắng để tính ra số kwh trong năm. Cách tiếp cận này không phù hợp vì cần phải tính theo mật độ năng lượng kwh/m2 x day và các yếu tố suy giảm hiệu suất hệ thống. cột trong slide 19 là cột số giờ nắng , không phải cột sản lượng điện

## Slide 40
GUIDE TO READING PV PANEL CATALOGUE INFORMATION

## Slide 41
GUIDE TO READING CATALOGUE INVERTER INFORMATION

## Slide 42: CASE STUDY
PROJECT OVERVIEW INFORMATION:
Investor: Vietnam Meiwa Co., Ltd. (Dong Nai)
EPC Contractor: DAT Group
Project capacity: 1.7 MWp
Annual output: 2,448 MWh
Annual savings for the enterprise: nearly VND 5 billion
CO₂ emission reduction: over 1,767 tons
PROJECT OVERVIEW INFORMATION:
Investor: Duy Tan Plastic Joint Stock Company (Binh Duong)
EPC Contractor: Vu Phong Group
Project capacity: 2.17 MWp
Annual output: 3,000,000 kWh
Annual savings for the enterprise: over VND 7 billion
CO₂ emission reduction: over 2,550 tons

## Slide 43
Look at the picture and tell what happens to the solar panels? What is this phenomenon called? Cause? Proposed solutions to overcome this situation.
DISCUSSION QUESTIONS

## Slide 44
2
Solar Energy
Hot water

## Slide 45
SOLAR THERMAL APPLICATIONS – SOLAR HOT WATER
Solar water heaters have the following main technologies: vacuum tubes, oil tubes, and flat plates. Each type has its own advantages and disadvantages, suitable for different conditions.
Solar Water Heater | Vacuum Glass Tube | Oil Glass Tubing | Flat Plate
Composition | Glass Tubes | Oil glass tube is coated with 3 layers of copper, silver, titanium | Kính cường lực và lớp thấu kính
Heating | 4h | Faster than a vacuum tube 1 - 2h | 2h
Heat transfer capability | Slow | Fast | Fast
Heat retention time | approximately 72h | approximately 72h - 96h | approximately 100h
Electricity Usage | No | No | No
Pricing | Cheap | High | Prety high

## Slide 46
Solar Water Heater | Vacuum Glass Tube | Oil Glass Tubing | Flat Plate
Advantage | The price is cheap, less damaged, and easy to replace. | - Continue to transfer heat as soon as the sun goes out. - No residue in the heat collector tube, ensuring water quality. | Because of the detachable design, the heat collector flat plate can be installed in any position, no need to be near the insulator.
Disadvantage | - Low heat retention time. - Slow heat transfer. - Easy to build residue, moss, and viscosity in the tube after a long time of use. | The price of oil hoses is higher than vacuum hoses | The price is very high, 3-6 times higher than other others.
SOLAR THERMAL APPLICATIONS – SOLAR HOT WATER

## Slide 47
SOLAR HOT WATER – VACUUM TUBE

## Slide 48
SOLAR HOT WATER – OIL TUBING

## Slide 49
SOLAR HOT WATER – FLAT PLATE

## Slide 50
SOLAR WATER HEATER COMBINED HEAT PUMP
The solar solution combined with a heat pump for the plant is an effective option to provide hot water, take advantage of renewable energy and reduce operating costs.

## Slide 51
SOME APPLICATIONS OF SOLAR WATER HEATING IN INDUSTRY
Food Processing Industry: Solar water heating systems are applied in food, pharmaceutical, paper, and rubber processing factories to supply hot water for washing, drying, distillation, sterilization, mixing, etc.
Textile Industry: Used in textile, footwear, and garment factories to supply hot water for washing, drying, softening, lubricating, dyeing, etc.

## Slide 52
3
Solar Energy
Heat Drying

## Slide 53
Solar Drying Technology Application (1)
A device that uses solar energy to dry products such as agricultural produce, food, seafood, medicinal herbs, etc.
Working Principle: Based on the greenhouse effect, utilizing solar heat to evaporate water, enabling quick drying while maintaining quality.
Advantages:
Energy Saving: Uses free solar energy, reducing electricity costs vs. conventional dryers.
Environmentally Friendly: Renewable energy, zero emissions.
Product Quality: Preserves natural color, flavor, and nutrients.
Stable Operation: Can integrate with electric heating or heat pumps for cloudy days.
Scalable: Applicable for industrial production.

## Slide 54
Structure, Operation
Drying chamber – insulated, heat-absorbing space for products.
Solar collector panels – convert sunlight into heat (polycarbonate sheets with >95% light transmission).
Ventilation system – circulates air and removes moisture.
Control system – adjusts temperature, humidity, and drying time.
Auxiliary heating sources – electric heating elements, heat pumps for heating and dehumidification.
Solar Drying Technology Application (1)

## Slide 55
Case Study
PROJECT OVERVIEW INFORMATION:
Investor: BESEAFOOD – Seafood Processing Import-Export Joint Stock Company (Vung Tau)
EPC Contractor: Vietnam Sustainable Energy Technology Joint Stock Company (SETECH)
Dryer Capacity: 2,400 kg fresh per batch
Dried Product: Seafood (fish)
Drying Time: 12–24 hours per batch (depending on product type and material thickness)
Maintained Drying Temperature: 35–65°C (depending on product)
Energy Source: Combination of solar energy and auxiliary heating (electric heating elements)
Performance:
Reduces drying time by 1.5–2 times compared to traditional sun-drying
Saves 60% electricity
Reduces raw material loss and increases product value

## Slide 56: Discussion
Potential Integrated Solutions for Industrial Use:
Solar water heating combined with a heat pump to supply hot water for production.
Solar water heating for secondary heating in boilers to improve efficiency.
Key Question: What is the feasibility and effectiveness of these two solutions?

## Slide 57
4
Biomass Energy
Combustion and disposal of by-products in industry

## Slide 58: BIO ENERGY
Biomass
Biomass and by-products from industrial facilities (wood waste, sawdust, coconut shells, bagasse, etc.), rice husks, straw, etc.
Biogas
Biogas produced during anaerobic digestion is a mixture of several gases.
Biodiesel
Fuels are formed from compounds of animal and plant origin (biological) such as fuels extracted from animal and plant fats (animal fat, coconut oil, etc.), cereals (wheat, corn, soybeans, etc.)
1. About technology:
Bio energy can be used to produce electricity or as fuel for transport, heating and cooking (biomass, biogas and biofuels)

## Slide 59: PRINCIPLE
Waste incineration is a mature technology, while waste gas combustion is commercialized but still being refined. However, there are a number of other emerging technologies that can produce energy from waste and other fuels without direct combustion.

## Slide 60: 3. CHARACTERISTIC
Recreate
Bioenergy is produced from renewable resources such as crops, organic waste and other living organisms.
Rich and diverse
Bioenergy is derived from a variety of organic resources, including agricultural crops, organic waste from industry, by-products…
Less pollution
Minimize negative impact on the environment.
Most biomass energy in Vietnam is used in traditional ways, such as cooking with low efficiency (10%-20%), while the use of biomass for electricity and heat generation mainly includes high efficiency direct biomass combustion, co-firing of biomass with coal and biomass gasification. These new uses, especially direct combustion, are currently increasing.

## Slide 61: 4. ADVANTAGES
01
Reduced landfill volume and reduced waste transported to landfills
02
Reduce carbon emissions.
03
Avoid waste disposal costs and landfill taxes.
04
Use by-products as fertilizer. Use waste gas or avoid methane emissions from landfills.
05
Ash can be used in the construction industry. Incineration also eliminates the problem of leachate generated in landfills.

## Slide 62: 5. DISADVANTAGES
01
The cost of operating and maintaining waste-to-energy plants is quite expensive.
02
Smoke and ash emitted from the chimneys of incinerators affect the environment around the plant.
03
Unsorted municipal waste (including organic and inorganic waste) affects incineration efficiency.
04
Municipal waste-to-energy plants are usually built for environmental benefits rather than for electricity generation or heat recovery.
05
Construction investment costs are very high. Most imported technologies are not suitable, domestic equipment and technology are inadequate and lack uniformity. There is a lack of management activities and activities to classify solid waste at source.

## Slide 63
BIOMASS ENERGY APPLICATION
Fluidized Bed Biomass Boiler Solution
The fluidized bed biomass boiler is an efficient and environmentally friendly technology that uses biomass fuel to produce steam for various industries.
Biomass includes agricultural and forestry by-products such as rice husks, sawdust, wood shavings, and bagasse, which are burned in a fluidized bed furnace to generate heat.
This heat boils water in pipes, producing high-pressure steam for production processes.
Applications of Fluidized Bed Biomass Boilers:
Food Industry – food processing, beverages, beer and alcohol production
Textile Industry – fabric drying, dyeing
Paper Industry – paper and pulp production
Other Industries – wood drying, agricultural product drying, etc.

## Slide 64
A fluidized bed boiler consists of 7 main components, each playing a critical role in operation:
Fluidized bed combustion chamber
Air supply system
Fuel Supply System
Circulating system (CFB)
Heat exchange system
Flue gas cleaning system
Automatic control system
BIOMASS ENERGY APPLICATION

## Slide 65
BIOMASS ENERGY APPLICATION
Criteria | Fluidized Bed Boiler | Traditional Boiler
Combustion efficiency | 97–99% | 85–90%
NOx emissions | 90% reduction | Standard
Fuel | Diverse (coal dust, waste, biomass) | Mainly lump coal
Operating temperature | 800–900°C | >1000°C
Operating costs | 30–40% savings | Standard
Advantages:
Can produce steam quickly, suitable for production lines with frequent load changes.
Easy to operate without complex processes or skills.
Biomass fuel reduces greenhouse gas emissions compared to fossil fuels.
Automated control with PLC-SCADA systems allows easy monitoring and efficient operation.
Disadvantages:
Requires large storage space for fuel and post-combustion ash.
Ash inside the boiler must be cleaned every 4 weeks, increasing maintenance costs.
Biomass fuel has variable moisture content and size, requiring good mixing skills for optimal efficiency.
Fluidized Bed Biomass Boiler Solution

## Slide 66
Case Study: Biomass Energy Application
Project Overview:
Location: Thanh Hoa
Investor: Miza Co., Ltd.
Construction time: 3 months (2021)
Product Information:
Product name: Fluidized bed furnace
Installed capacity: 40 tons/h
Design pressure: 16 bar, 200°C
Working pressure: 10 bar, 180°C
Fuel: wood chips, cinnamon chips, paper industry plastic waste
The high-efficiency fluidized bed boiler, designed and manufactured by Kim Truong Phuc, has been operating at Miza Paper Factory since May 2021. It has helped the company significantly save on input material costs, meet production plans, and optimize profits.

## Slide 67
General Information:
Client: Kumho Tire Vietnam Co., Ltd.
Location: Binh Duong Province
Scope: Fluidized bed boiler system – 38 tons steam/hour
Completion date: July 2020
Technical Specifications:
Capacity: Two boilers – 20 tons/h and 18 tons/h
Design standard: TCVN 12728:2019
Fuel: wood pellets, wood chips
20 tons/h boiler uses 100% biomass fuel
Flue Smoke Treatment System
SCADA Control System
Case Study: Biomass Energy Application

## Slide 68
THANK YOU