## Slide 1
Module 17:
Greenhouse gas overview and related requirements
Technical staffs
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISES

## Slide 2
Sources of greenhouse gas emissions
Electricity and heat: Burning coal, natural gas, and other fossil fuels is the largest source of GHG emissions worldwide.
Industry: Producing the products that power the world today creates a lot of GHG.
Transportation: Greenhouse gas emissions from transportation come primarily from burning fossil fuels...
CONCEPTS

## Slide 3
Agriculture and land: About one-fifth of all global GHG emissions come from land use, mainly from deforestation and emissions from livestock. This also includes fuels used for agriculture, forestry and fishing, direct emissions from land use and wildfires.
Other energy sources.
Food waste.
Operate from buildings.
Sources of greenhouse gas (GHG) emissions
CONCEPTS

## Slide 4
GREENHOUSE EFFECT – GREENHOUSE GASES
Greenhouse effect: Refers to the effect that occurs when radiant energy from sunlight passes through glass windows or roofs, is absorbed and dispersed back into the interior space as heat, resulting in heating the entire interior space, not just the illuminated areas.
Greenhouse gas: A gaseous component that can absorb long-wavelength radiation reflected from the earth's surface when illuminated by sunlight, then disperse the heat back to the earth, causing the greenhouse effect. The greenhouse effect is believed to be the cause of global warming.
The temperature will increase gradually

## Slide 5
In addition to CO2, CH4, N20, gas combinations… and water vapor also have similar effects but to different degrees.
As greenhouse gas concentrations increase, the greenhouse effect becomes more widespread and widespread, increasing global temperatures (global warming) and thus changing the climate in the coming decades and decades.
 The climate will change
Climate change is considered one of the greatest challenges facing the world.
Eleven percent of the world's population is now vulnerable to the impacts of climate change such as droughts, floods, extreme weather events and rising sea levels.
GREENHOUSE EFFECT – GREENHOUSE GASES

## Slide 6
UNFCCC COPs
Global average annual temperature relative to pre-industrial times (degrees Celsius)
https://www.unep.org/emission-gap-report-2023
Our climate has warmed 0.80C since 1880 – two-thirds of that increase has occurred since 1994.
Without action, warming is predicted to increase by another 30C by 2100.
Notes: Liên Hợp Quốc về Biến đổi Khí hậu (United Nations Framework Convention on Climate Change, UNFCCC hoặc FCCC)

## Slide 7
INTERNATIONAL ACTIONS ON CLIMATE CHANGE
The United Nations Framework Convention on Climate Change (UNFCCC) was negotiated at the 1992 Earth Summit:
  Goal: “Stabilize atmospheric concentrations of greenhouse gases at a level that would prevent dangerous anthropogenic interference with the climate system”
  The Kyoto Protocol of December 1997 introduced three flexible mechanisms:
Emissions market mechanism
Co-implementation mechanism
Clean Development Mechanism
Paris Agreement 2015: Keep global temperature rise below 2 degrees Celsius and strive to limit the increase to 1.5 degrees Celsius.
2021 United Nations Climate Change Conference in Scotland (COP26).

## Slide 8
VIETNAM'S COMMITMENT TO CLIMATE CHANGE RESPONSE
Updated report September 2022: By 2030, the unconditional contribution is 15.8% (reducing 146.3 million tons of CO2); The conditional contribution with international support is 43.5% (reducing 403.7 million tons of CO2).

## Slide 9
UNITED NATIONS SUSTAINABLE DEVELOPMENT GOALS
 The world is very interested
United Nations climate change response actions
7. Clean and sustainable energy
Good working conditions and economic growth
Innovative industry and infrastructure
11. Sustainable cities and communities
12. Responsible consumption and production
13. Climate action

## Slide 10
GLOBAL SUSTAINABLE DEVELOPMENT PROGRAM

## Slide 11
Greenhouse gases (GHG): According to the Kyoto Protocol and the Environmental Protection Law
GHGs are converted to tonnes of CO2 equivalent according to their global warming potential (GWP). The GWP is determined by the United Nations Framework Convention on Climate Change (UNFCCC).
CONCEPTS
Notes: GWP: Tiềm năng nóng lên toàn cầu (The Global Warming Potential) là tỷ số giữa bức xạ cưỡng bức của một kg KNK phát ra so với 1kg CO2 trong cùng 1 khoảng thời gian (ví dụ như 100 năm)
Liên Hợp Quốc về Biến đổi Khí hậu (United Nations Framework Convention on Climate Change, UNFCCC hoặc FCCC)
Uy ban Liên chính phủ về Biến đổi Khí hậu (IPCC)

## Slide 12
CONCEPTS
Notes: GWP: Tiềm năng nóng lên toàn cầu (The Global Warming Potential) là tỷ số giữa bức xạ cưỡng bức của một kg KNK phát ra so với 1kg CO2 trong cùng 1 khoảng thời gian (ví dụ như 100 năm)
Liên Hợp Quốc về Biến đổi Khí hậu (United Nations Framework Convention on Climate Change, UNFCCC hoặc FCCC)
Uy ban Liên chính phủ về Biến đổi Khí hậu (IPCC)

## Slide 13
Net zero
Carbon Neutral
Emissions
Residual emissions
Offsetting emissions and compensating the remaining emissions
No additional greenhouse gases are released into the atmosphere.
Carbon Neutral
Net zero
Carbon Neutral and Net Zero
CONCEPTS

## Slide 14
ROADMAP FOR IMPLEMENTATION CONTENT
Decree 06/NĐ-CP
Provide activity metrics
2022
Greenhouse Gas Inventory Report
Emissions Quota
Implementation
GHG Mitigation
Vietnam Emission Commitment
NET- ZERO
2023
2025
2026
2030
2050
2027
Carbon Credit
2024
Review of greenhouse gas inventory and mitigation reports
Moving towards carbon neutrality -Net zero
3/2025: report to the Provincial Committee
12/2025: report to MONRE

## Slide 15: LAWS – REGULATIONS ON GREENHOUSE GAS EMISSIONS
Decree 06/2022/ND-CP on greenhouse gas emission reduction and ozone layer protection.
Decision 13/2024/QD-TTg on the list of sectors and facilities emitting greenhouse gases that must conduct greenhouse gas inventories (updated) on August 13, 2024.
Decision 896/QD-TTg dated 2022 approving the National Strategy on Climate Change for the period up to 2050 issued by the Prime Minister.
Decision 2626/QD-BTNMT of 2022 promulgating the list of emission factors for greenhouse gas inventory.
Decision 942/QD-TTg of 2022 on action plan to reduce methane emissions by 2030.

## Slide 16: LAWS – REGULATIONS ON GREENHOUSE GAS EMISSIONS
Decision 569/QD-BTNMT 2023 on action plan to reduce methane emissions by 2030.
Circular 17/2022/TT-BTNMT Technical regulations on measurement, reporting, appraisal, and mitigation of greenhouse gas emissions in the field of waste management.
Circular 23/2023/TT-BNNPTNT Technical regulations on measurement, reporting, appraisal, and mitigation of greenhouse gas emissions in the forestry sector.
Circular 38/2023/TT-BCT Technical regulations on measurement, reporting, appraisal, and mitigation of greenhouse gas emissions in the Industry and Trade sector
Circular 13/2024/TT-BXD Procedures and technical regulations on GHG inventory and measurement, reporting, appraisal and mitigation of greenhouse gas emissions in the Construction sector
Circular 63/2024/TT-BGTVT Technical regulations on measurement, reporting, appraisal of greenhouse gas emission reduction and greenhouse gas inventory in the Transport sector

## Slide 17
ACTIONS TO BE TAKEN AT THE COMPANY LEVEL
Step 1: Determine the scope of greenhouse gas (GHG) audit.
Step 2: Collect data on GHG audit.
Step 3: Select the GHG emission factor.
Step 4: Determine the GHG audit method.
Step 5: Perform quality control of GHG audit.
Step 6: Assess the uncertainty of GHG audit.
Step 7: Recalculate the GHG audit results.
Step 8: Develop a report on GHG audit results.

## Slide 18
The structure of a greenhouse gas report includes the following chapters:
Chapter 1: General description of the organization's goals and inventory objectives:
This chapter includes a description of the reporting organization, those responsible, the purpose of the report, the intended users, the dissemination policy, the reporting period and frequency, the data and information contained in the report (a list of GHGs reviewed and explained), and the organization's statement of verification.
Chapter 2: Organizational Boundaries:
This chapter includes a description and explanation of the boundaries and methods of consolidation.
Chapter 3: Reporting Boundaries:
This chapter includes a description and explanation of the types of emissions considered.
GREENHOUSE GAS REPORTING - REQUIREMENTS
Notes: Điều khoản 8

## Slide 19
The structure of a greenhouse gas report includes the following chapters:
Chapter 4: Quantified GHG Emissions and Removals Inventory:
This chapter includes quantified data results by type of emission or removal, a description of the methodology and activity data used, references and documentation of emission and removal factors, uncertainties and precision affecting the results, and a description of planned actions to reduce uncertainty for future inventories.
Chapter 5: GHG reduction initiatives and internal performance monitoring:
The organization can report on its GHG reduction initiatives and the results of its internal performance monitoring.
GREENHOUSE GAS REPORTING - REQUIREMENTS
Notes: Điều khoản 8

## Slide 20: GREENHOUSE GAS INVENTORY REPORT
Greenhouse gas inventory report according to Decree 06/2022/ND-CP, Form 06, Appendix II
I. Information of facilities required to conduct greenhouse gas inventories 1. Name of the establishment, address, business license… 2. Information about the legal representative of the establishment. 3. Information about the field of business and production activities. | II. Information on production and business activities and operating data of the facility 1. Boundaries and scope of operations of the facility. 2. Infrastructure, technology and operations of the facility must conduct greenhouse gas inventories. 3. Emission sources and sinks of greenhouse gases within the scope of operations of the facility. 4. Information system, data on greenhouse gas emissions of the facility, identifying the causes of limitations in the greenhouse gas inventory of the facility. | III. Results of greenhouse gas emissions inventory 1. Description of the greenhouse gas emission inventory method (data collection method, emission factor). 2. Activity data related to greenhouse gas emissions of the facility. 3. Results of the greenhouse gas inventory of the facility. 4. Reliability, completeness, uncertainty of information, data on greenhouse gas emissions and results of the greenhouse gas inventory of the facility.

## Slide 21
The organization may decide to conduct verification
In order to view the GHG emissions and removals information in a fair and objective manner, the organization shall conduct verification in accordance with the needs of the intended users. The principles and requirements are described in ISO 14064-3.
Requirements for the verification body are described in ISO 14065.
Requirements for the competence of the validation team and verification team are described in ISO 14066.
VERIFICATION ACTIVITIES - REQUIREMENTS
Notes: Điều khoản 8

## Slide 22
DISCUSS
Introduce a GHG inventory report as required by Form No. 06, Appendix II, Decree 06/2022

## Slide 23
Introduce a GHG inventory report as required by ISO 14064-1:2018 and related documents.
DISCUSS

## Slide 24
THANK YOU