## Slide 1
MODULE 18: CALCULATION AND MANAGEMENT OF GREENHOUSE GAS EMISSIONS IN ENTERPRISES
Technical staff
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Notes: MD 18 có bổ sung các Slide nói về MRV, TT 38, NĐ 06 và các thông tin về CBAM

## Slide 2: SỰ CẦN THIẾT CỦA HỢP PHẦN
Compliance with international laws and requirements
1
Meeting the trend of sustainable development and social responsibility
2
Reduce costs and increase operational efficiency
3
Improving competitiveness and access to international markets
4
Ready for carbon markets and green finance opportunities
5
Improve intrinsic capacity and risk management
6
Notes: Tại sao phải học phần này
Học phần này có thể áp dụng gì cho công việc

## Slide 3: MỤC TIÊU CỦA HỢP PHẦN
Determining the scope and identification of sources of greenhouse gas emissions
Understand methods of quantifying and reporting greenhouse gas emissions
Notes: Học phần này cung cấp kiến thức, kỹ năng gì
Kết quả đạt được sau khi học

## Slide 4: Terminology and definitions
Source of greenhouse gases (GHG): The process of releasing GHG into the atmosphere
GHG sink: The process of removing GHG from the atmosphere
GHG removal: The removal of GHG from the atmosphere through GHG sinks.
GHG emission factor: A coefficient that relates greenhouse gas activity data to GHG emissions. Global warming potential (GWP): The ratio of the radiative forcing of one kilogram of a GHG emitted compared to one kilogram of CO₂ over the same time period (e.g., 100 years).
GHG inventory: A list of GHG sources and GHG sinks, along with their quantified GHG emissions and removals.
GHG report: An independent document intended to communicate GHG-related information of an organization or a GHG project to its intended users.
GHG project: An activity or set of activities that alter baseline GHG conditions and result in reduced GHG emissions or enhanced GHG removals.

## Slide 5: Source of GHG emissions
CO2 EMISSIONS
Burning fossil fuels, solid waste, trees, and other biomass materials, as well as the result of certain chemical reactions in production
CO₂ is removed from the atmosphere or sequestered when absorbed by plants as part of the biological carbon cycle
CH4 EMISSIONS
Emitted during the production and transportation of coal, natural gas, and petroleum
Emitted from livestock and other agricultural activities, land use, and the decomposition of organic waste in solid waste landfills.
N20 EMISSIONS
Emitted from agricultural activities and land use
Burning fossil fuels and solid waste; as well as during wastewater treatment

## Slide 6: Source of GHG emissions
PFCS EMISSION
Used in the electronics industry for semiconductor manufacturing
SF6 EMISSION
Used in electrical transmission and distribution equipment
Electronics manufacturing.
Healthcare sector.
HFCS EMISSION
Emissions in refrigeration and air conditioning
Most HFCs are contained in equipment, so emissions result from wear and tear, improper maintenance, or leaks at the end of the product's life cycle

## Slide 7
GWP coefficient: Global warming potential
The Global Warming Potential (GWP) was developed to compare the global warming impacts of different greenhouse gases
It is a measure of the amount of energy that 1 ton of greenhouse gas will absorb over a specific period (usually 100 years) compared to 1 ton of CO2
According to the IPCC AR6
The GWP of CO2 = 1
The GWP of CH4 = 27.9: meaning 1 ton of CH4 emissions is equivalent to 27.9 tons of CO2
The GWP of N20 = 273: meaning 1 ton N20 emissions is equivalent to 273 tons of CO2
CO2e (CO2 Equivalents) is a unit of measurement used to compare emissions from different greenhouse gases according to their GWP by converting the amount of gas into an equivalent amount of CO2.

## Slide 8
Picture 1
Picture 2
Could you please list the emission sources and sinks shown in the below pictures?
DISCUSS

## Slide 9
Principle
4.1 Summary
4.2 Relevance
4.3 Completeness
4.4 Accuracy
4.5 Consistency
4.6 Transperency
Principles of GHG inventory
The application of principles to ensure that the information related to greenhouse gases is a truthful and fair report.
Relevance: Selecting greenhouse gas sources, data, and methods that are suitable for the needs of the users.
Completeness: Including all relevant greenhouse gas emissions and removals.
Accuracy: Minimizing deviations and uncertainties to the extent feasible.
Consistency: Enables meaningful comparisons in information related to greenhouse gases.
Transparency: Disclosing complete and relevant information related to greenhouse gases, allowing intended users to make decisions with reasonable confidence.
Notes: Điều khoản số 4
Sự liên quan: Lựa chọn nguồn KNK, hấp thu KNK, loại bỏ KNK, dữ liệu và phương pháp luận phù hợp với nhu cầu của người sử dụng
Sự đầy đủ : Bao gồm tất cả các phát thải và loại bỏ KNK có liên quan
Sự nhất quán: Cho phép so sánh có ý nghĩa trong thông tin liên quan đến KNK
Sự chính xác: Giảm thiểu sự sai lệch và sự không chắc chắn trong phạm vi thực tế
Sự minh bạch: Cung cấp đầy đủ và thích hợp thông tin liên quan đến KNK để cho phép những người sử dụng có mục đích đưa ra quyết định với độ tin cậy hợp lý

## Slide 10
Boundary
Organizational boundaries: A group of activities or facilities where an organization exercises operational/financial control or ownership.
Reporting boundaries: A group of greenhouse gas emissions or removals reported from within the organizational boundaries, as well as significant indirect emissions.
Farm
Supplier
Warehousing
Project
After sale service
Notes: Điều khoản 5
+ Ranh giới của tổ chức: Kiểm soát vận hành, kiểm soát tài chính
+ Ranh giới báo cáo: Trực tiếp, gián tiếp

## Slide 11
Organizational boundary
There are two approaches..
Approach 1: Control: Operational control or financial control..
The organization is responsible for all greenhouse gas emissions and/or removals from facilities over which it has financial or operational control
Kiểm soát
Vận hành
Tài chính
Your organization has the authority to establish and implement its operational policies at the activity level.
Your organization has the ability to direct the financial and operational policies of the operation.
Operation
Control
Finance
Notes: Đặt câu hỏi: Báo cáo cho tổ chức nào?

## Slide 12
Organizational boundary
There are two approaches.
Approach 2: Equity share: Organizations using the equity share approach calculate the proportion of emissions corresponding to their ownership share in the operation.
The consolidation approach must be suitable for the intended purpose of the GHG inventory.
The organization must document and report the consolidation approach applied.
For example: If an organization owns 100%, it is responsible for 100% of the emissions and removals GHG of that organization. If it owns 20%, then 20% of the emissions/removals are reported.
Notes: Đặt câu hỏi: Báo cáo cho tổ chức nào?

## Slide 13
Organizational boundary
Parent company
80% equity ownership. Full financial control.
Full operational control
Consolidation method
Equity sharing
Financial control
Operational control
30% equity ownership.
Full financial control.
No operational control
Emissions volume
Notes: Đặt câu hỏi: Báo cáo cho tổ chức nào?

## Slide 14
Company R owns and operates a winery (Plant N) and a vineyard (Farm A). Company R also owns 50% of the equity in Vineyard B, which is fully operated and financially controlled by another company.
Approach | The amount of GHG that Company R supervises/reports
Equity share approach | ?
Operational control approach | ?
Financial control approach | ?
Each type of GHG emission must be converted into CO2 equivalent (CO2e) units.
DISCUSS
N Plant
B Farm
A Farm
10,000 tons CO2 e/year
5,000 tons CO2 e/year
1,000 tons CO2 e/year

## Slide 15
Classification of emission types according to ISO 14064-1:2018
Reporting boundary
Category 1: Direct GHG emissions from sources within the organization's boundary
Category 2: Indirect GHG emissions from imported energy
Category 3: Transportation services.
Category 4: Use of external products
Category 5: Use of the organization's products
Category 6: Other sources (leased assets, franchising, employee commuting, etc.).
Notes: Đặt câu hỏi: Nguồn thải của ai?

## Slide 16
Reporting boundary
Direct emission
Direct emission
Classification
Fuel type
Note
Classification
Fuel type
Note
Stationary combustion
Mobile combustion
Generator (if any)
Canteen gas stove (if any)
Incinerator (if any)
Boiler (if any)
Dryer (if any)
Gas welding machine (if any)
Fire pump
Others (If any)
Forklift (if any)
Internal patrol motorcycle (if any)
Employee shuttle bus (if any)
Cargo truck (if any)
Others (If any)

## Slide 17
Reporting boundary
Direct emission
Direct emission
Classification
Fuel type
Note
Classification
Fuel type
Note
Leak
Office air conditioner
Cooling system
Wastewater treatment system
Septic tank (if any)
"High-voltage electrical equipment (if any)
Fire extinguisher
Other (if any)
Refrigerant gas
Refrigerant gas
Industrial process
Chemical reaction (if any)
Physical activity (if any)
Biological reaction (if any)
Direct emission
Direct emission
Classification
Fuel type
Note
Leak
Office air conditioner
Cooling system

## Slide 18
Reporting boundary
Indirect emissions
Indirect emissions
Classification
Fuel type
Note
Classification
Fuel type
Note
Classification
Fuel type
Note
Electricity consumption
Office electricity
Lighting electricity
Production electricity
Refrigerated container (if any)
Other (If any)
Other purchased energy (if any)
Indirect emissions
Transportation services
Use of external products/services
Ship/ barge container
container
container
Personal motorcycle
Personal car
Outsourced car service
Business airplane
Business bus
Other source
Leased assets
Use of raw materials
Wastewater treatment services
Use of goods/ equipment/ assets
Accommodation for employees
Use of the company's products/services
Use of the company's products/services
Products/ services treatment after using
Investment activities

## Slide 19
Please identify the scope and sources of greenhouse gas emissions at your enterprise
DISCUSS

## Slide 20: Steps to implement greenhouse gas inventory
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Determining the scope and boundaries of GHG inventory
Identifying GHG sources and sinks
GHG inventory
Quality check of measurement
Emission reduction plans and initiatives
GHG statement

## Slide 21: Decree 06/2022 ND-CP

## Slide 22: Circular 38/2023/TT-BCT – Requirements

## Slide 23: Circular 38/2023/TT-BCT – Requirements

## Slide 24: Greenhouse gas inventory reference documents
National
International
International
Notes: https://www.ipcc-nggip.iges.or.jp/
ghg conversion factors epa
Emission factor UK

## Slide 25
Quantification of emissions and removal of GHG
Calculation of GHG emissions
Method of calculation/measurement.
Continuous monitoring of emission sources
Intermittent monitoring
Using Emission Factors
Formula:
GHG Emissions = Activity Data × Emission Factor × GWP (Global Warming Potential)

## Slide 26: Quyết định 2626/QĐ-BTNMT: Hẹ số phát thải

## Slide 27: Guidelines for greenhouse gas inventory
Step 1: Collect data
Scope | Emission Sources | Data | Responsible | Months | Greenhouse Gas Type
Scope 1 | Boiler - Generator - Equipment using natural gas | Invoice Statistical report Meter reading | Technical | 1 - 12 | CO₂, CH₄, N₂O
 | Diesel forklift - 4-seater car - 7-seater car - Delivery vehicle | Invoice Distance | Administration Procurement | 1 - 12 | CO₂, CH₄, N₂O
 | Production process (stages that generate emissions) | Meter reading Quantity of raw materials input | Production | 1 - 12 | CO₂, CH₄, N₂O, HFCs, PFCs, SF₆
 | Office air conditioning system - Refrigeration system - Refrigerator, freezer - Industrial wastewater treatment - Septic tank | Invoice Statistical report Meter reading Number of workers | Administration Technical | 1 - 12 | HFC, CH₄, N₂O
Scope 2 | -Electricity consumption in the company | Invoice Meter reading | Technical | 1 - 12 | CO₂
Scope 3 | - Use of raw materials for production - Employee transportation - Business travel - Transportation of raw materials - Waste treatment | Invoice Meter reading Distance | Procurement Administration | 1 - 12 | CO₂, CH₄, N₂O

## Slide 28: Guidelines for greenhouse gas inventory
Level 3:
- Emission factor at the enterprise
- Direct measurement monitoring
- High reliability
Level 2:
- Intermediate approach
- National emission factor
- Acceptable reliability
Level 1:
- Estimative approach
- International emission factor
- Low realiability
Step 2: Quantitative approach and data collection
Must choose a method to reduce uncertainty.
Create consistent results, repeatable annually
Can be reportable
Note: Each type of greenhouse gas may require a different approach.

## Slide 29: Guidelines for greenhouse gas inventory
Step 3: CO2e Calculation
Operational data
  Emission factor
2. X
2. =
2. X
2. =
tons of emissions(tons)
Emissions (Tons)
Global Warming Potential (GWP)
Tons CO2e
Example: Calculate CO2e from electricity consumption data of a company.
Step 1: Collect the total electricity consumption data and convert the units to MWh.
Step 2: Choose the emission factor for Vietnam's power grid.
Year 2022: 0.7221
Year 2023: 0.6766
Tons CO2e = MWh x 0.6766 x GWP

## Slide 30: Guidelines for greenhouse gas inventory
Step 4: Calculate the uncertainty/uncertainty range (IPCC).
Assessment of the uncertainty of the KNK inventory at the grassroots level shall comply with the guidance in Article 11 of 38/2023/TT-BCT Quantification of uncertainty of KNK inventory shall comply with the guidance in Chapter 3, Book 1, Guidelines of IPCC 2006, Guidelines of IPCC 2019

## Slide 31: Practice exercises
Identify, inventory, and quantify GHG emissions from input data sources

## Slide 32: Practice exercises
1. Direct GHG emissions from fuel combustion activities.

## Slide 33: Practice exercises
2. GHG emissions leakage from equipment and production processes involving refrigerants (HFC and HCFC gases).

## Slide 34: Practice exercises
2. GHG emissions leakage from equipment and production processes involving refrigerants (HFC and HCFC gases).

## Slide 35: Practice exercises
2. GHG emissions leakage from equipment and production processes involving refrigerants (HFC and HCFC gases).

## Slide 36: Practice exercises
2. GHG emissions leakage from equipment and production processes involving refrigerants (HFC and HCFC gases).

## Slide 37
3. Indirect GHG emissions from the use of purchased electricity.
Practice exercises

## Slide 38: Practice exercises
4. Indirect GHG emissions from the use of purchased steam

## Slide 39: Practice exercises
5. GHG emissions from anaerobic decomposition.
5.1.1. Direct emissions of CH4 and CO2 from organic waste
5.1. GHG emissions during the anaerobic treatment process.

## Slide 40: Practice exercises
5. GHG emissions from anaerobic decomposition.
5.1.1. Direct emissions of CH4 and CO2 from organic waste
5.1. GHG emissions during the anaerobic treatment process

## Slide 41: Practice exercises
5. GHG emissions from anaerobic decomposition.
5.1.1. Direct emissions of CH4 and CO2 from organic waste
5.1. GHG emissions during the anaerobic treatment process

## Slide 42: Practice exercises
5. GHG emissions from anaerobic decomposition
5.1.1. Direct emissions of CH4 and CO2 from organic waste
5.1. GHG emissions during the anaerobic treatment process

## Slide 43: Practice exercises
5. GHG emissions from anaerobic decomposition
5.1.1. Direct emissions of CH4 and CO2 from organic waste
5.1. GHG emissions during the anaerobic treatment process

## Slide 44: Practice exercises
5. GHG emissions from anaerobic decomposition
5.1.2. Direct N2O emissions
5.1. GHG emissions during the anaerobic treatment process

## Slide 45
Calculate the CO2e emissions (in tonnes) for the company’s stationary combustion activities
Step 1: Look up calorific value coefficient
Calorific value …=…TJ/Gg
Step 2: Converting energy units to TJ
Look up density: g/liter (if necessary)
Converting energy units to TJ
Step 3: Choosing the appropriate Emission Factor (EF)
Step 4: Calculating emissions for different types of fuels
Emissions (tons CO2e) = Consumption (converted to TJ) × (CO2 emission factor × GWP + CH4 emission factor × GWP + N2O emission factor × GWP) / 1000
DISCUSS

## Slide 46
Calculate the CO2e emissions (in tonnes) for the company’s mobile combustion activities
Step 1: Lookup the calorific value
Calorific value = ...TJ/Gg
Step 2: Convert energy units to TJ
Lookup the density: g/liter (if necessary)
Convert from other energy units to TJ
Step 3: Select the appropriate EF (emission factor)
Step 4: Calculate the emissions for each fuel type
Emissions (tonnes CO2e) = Consumption (converted to TJ) * (CO2 emission factor * GWP + CH4 emission factor * GWP + N2O emission factor * GWP) / 1000
DISCUSS

## Slide 47
Calculate the CO2e emissions (in tonnes) from the company's domestic and industrial wastewater treatment system using the provided information.
Calculate CH₄ emissions from domestic wastewater
TOW = P x BOD x 0,001 x I x 365
Emission CH4 = TOW x EF
TOW: Total organic matter degraded in domestic wastewater (kg BOD/year)
P: Total national population in the inventory year (persons).
BOD: National per capita factor in the inventory year (g/person/day).
0,001: Convert from g BOD to kg BOD
I: Adjustment factor for BOD from industrial wastewater discharged into the domestic wastewater system (default is 1.25 for unrestricted discharge; otherwise, the default is 1.00).
DISCUSS

## Slide 48: Greenhouse gas inventory report
Greenhouse Gas Inventory Report according to Decree 06/2022/ND-CP, Form 06, Appendix II
Information required for a facility to conduct a greenhouse gas (GHG) inventory:
Facility name, address, business license
Information about the legal representative of the facility
Information about the area of operation, business, and production
II. Information about the facility's business operations and activity data
Boundaries and scope of the facility's operations
Infrastructure, technology, and operations of the facility required to conduct a greenhouse gas inventory
GHG emission sources and sinks within the facility's operational scope
Information system and data on the facility's GHG emissions, identification of limitations in the GHG inventory process
III. Result of the greenhouse gas emissions inventory
Description of the greenhouse gas emissions inventory method (data collection method, emission factors)
Activity data related to the facility's greenhouse gas emissions
Results of facility’s greenhouse gas inventory
Reliability, completeness, and uncertainty of information, data on greenhouse gas emissions, and the facility's greenhouse gas inventory results

## Slide 49
An organization can decide to conduct verification
To review the information on emissions and greenhouse gas removal in a fair and objective manner, the organization must conduct verification in accordance with the needs of the intended users. The principles and requirements are described in ISO 14064-3.
The requirements for the verification body are described in ISO 14065.
The requirements for the competence of the verification and audit team are described in ISO 14066
Verification activities - Requirements
Notes: Điều khoản 8

## Slide 50: Measurement, Reporting, and Verification (MRV) of GHG reduction activities
1. General Requirements:
Measurement, reporting, and verification must follow procedures issued by competent authorities, ensuring transparency, accuracy, and consistency, in alignment with international regulations and Vietnam’s national context.
2. Measurement:
Facilities shall carry out measurement of emission reduction outcomes based on issued guidelines.
Ministries and relevant agencies conduct sector-level measurements based on related policies, programs, and plans.
3. Reporting:
Facilities must submit annual reports starting from 2027 (before March 31).
Ministries must submit sectoral reports annually from 2024 (before January 15).
The Ministry of Natural Resources and Environment (MONRE) is responsible for consolidating and preparing the national GHG emission reduction report.
4. Verification:
Facility-level verification is conducted annually starting from 2026.
Sector-level verification is conducted by ministries starting from 2023.
MONRE leads the verification of the consolidated report to support national reporting in accordance with international climate commitments.

## Slide 51: Requirements and Purpose of CBAM
CBAM stands for Carbon Border Adjustment Mechanism.
It is an environmental policy tool designed by the EU to impose a carbon tax on goods imported into the EU, equivalent to the carbon price that EU domestic products are incurring.
Purpose of CBAM
Prevent "carbon leakage" Promoting global emissions reduction Supporting the EU's climate goals
CBAM Requirements Greenhouse Gas Emissions Report Buy CBAM Certificate from EU Data transparency and production traceability

## Slide 52: Roadmap for applying CBAM
In the first phase (from 2023–2026), CBAM applies to high-emission products such as: Iron and steel; Aluminium; Cement; Fertilizer; Electricity; Hydrogen and some arising products (steel screws, aluminum bars...
What do Vietnamese businesses need to do to adapt to CBAM?
Measurement and inventory of greenhouse gas emissions (according to international standards such as GHG Protocol, ISO 14064)
Building a transparent reporting system
Increasing the use of renewable energy and clean technology
Work with EU partners to meet technical and legal requirements.

## Slide 53
EXERCISE 1
Calculate the CO2e emissions of the Company with the information provided
+ Total coal used for the boiler in the year: 200,000 tons
+ Total LPG used for the canteen: 24,000 kg
+ Total DO used for the generator: 45,000 liters. Knowing that 1 liter of DO = 0.84 Kg

## Slide 54
Calculate the company's CO2e emissions with the information provided
+ Total DO oil used for internal staff transportation: 65,000 liters. Knowing that 1 liter of DO = 0.84 Kg
EXERCISE 2

## Slide 55
EXERCISE 1 + 2

## Slide 56
THANK YOU