## Slide 1
Module 20:
Concepts and indicators of financial and economic analysis of EE projects
Technical staffs
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISES

## Slide 2: Module 20 – Concepts and indicators of financial and economic analysis of EE projects
Evaluating/selecting EE projects
1
Evaluating the effectiveness of energy-saving solutions
2
Estimation of costs and benefits of EE project
3

## Slide 3: 1. EVALUATING/SELECTING EE PROJECTS
Objectives
Identify criteria and carry out the selection of energy efficiency solutions.
Select and propose methods for evaluating the effectiveness of energy-saving solutions.
Contents
Steps for evaluating and selecting solutions
Technical criteria
Financial criteria
Evaluation of the effectiveness of energy-saving solutions
Consideration of basic issues such as cash flow, depreciation, and financing
Financial performance evaluation based on fundamental criteria
Case study analysis

## Slide 4: Parameters to be described and identified from the EE projects
Describe the technical aspects of the EE project
Identify the expenses (outflows) of the EE project
Identify the benefits (inflows) of the EE project
Identify other economic and social benefits

## Slide 5: DESCRIBE THE TECHNICAL ASPECTS OF THE EE PROJECT
Current energy consumption and management status of the company
Energy efficiency opportunities for the company
Describe replacement investments, upgrades, new investments, ... for energy-consuming equipment
Describe changes in parameters and energy consumption indicators, equipment maintenance before and after the project
Estimate investment, upgrade, and maintenance costs required for the project
Estimate energy consumption levels after the project implementation

## Slide 6: Economic Analysis and Financial Analysis in (EE) Projects
Criteria | Financial Analysis | Economic Analysis
Objective | Evaluates direct monetary costs and benefits to the project owner/investor | Evaluates costs and benefits from a national or societal perspective
Target audience | Investors, enterprises, banks, financiers | Governments, development agencies, policy makers
Considered benefits | - Revenue- O&M costs- Capital costs- Taxes | - Greenhouse gas (GHG) reduction- Public health- Job creation- Foreign currency savings
Common metrics | - NPV (Net Present Value)- Financial IRR (FIRR)- Payback Period | - Economic IRR (EIRR)- Benefit/Cost ratio (B/C)- Total Resource Cost (TRC)
Environmental & social impacts | Not included or only limited consideration | Quantified or monetized (e.g., avoided CO₂ emissions)
Investment decision basis | Based on profitability for the investor | Based on overall benefit to the economy or society
Notes: Example:
A project improves an air compressor system and saves USD 100,000 annually in electricity costs:
  Financial analysis: Focuses on how much money the business saves → whether it’s financially attractive to invest.
  Economic analysis: In addition to cost savings, also considers CO₂ emissions reduction, improved air quality, public health benefits, etc.

## Slide 7: Financial indicators
When is the payback?
Total value delivered?
Profitability per unit of capital?
Simple Payback Period
Net Present Value (NPV)
Internal Rate of Return (IRR)
Payback period – the length of time it takes for the project’s income to recover the project’s investment costs. Simple payback period (SPP): does not take into account the time value of money. Usually only applicable to projects with short payback periods (less than 3 years).
What financial performance evaluation criteria do you often use to make investment decisions?
Notes: Sử dụng 1, hoặc kết hợp nhiều tiêu chí
Tiêu chí thời gian hoàn vốn: phương án được chọn là phương án có thời gian hoàn vốn nhanh nhất. Đây là phương pháp đơn giản nhất

## Slide 8: IDENTIFY THE EXPENSES (OUTFLOWS) OF THE EE PROJECT
Energy efficiency projects involve a variety of costs:
Investment costs (cost of capital)
Operating and maintenance costs
Energy and related costs
Other expenses
Replacement cost: the cost of removing equipment at the end of the project life cycle.
Installation costs (construction, installation)
Equipment costs
Taxes, customs fees
Employee training costs
Other costs (Insurance, Engineering and Transport)
Labor costs (salaries for operating and management staff, ...)
Repair and maintenance costs
Other costs (supplementary materials, administrative costs)
Lost production due to production stoppages during project installation and commissioning.
….
Notes: Qui mô của khoản đầu tư là yếu tố rất quan trọng trong đánh giá tài chính của các dự án hiệu quả năng lượng. Chi phí này thường thể hiện bằng một lượng tiền lớn chi vào năm dự án được triển khai. Chi phí đầu tư bao gồm các loại chi phí sau đây:
Các chi phí vận hành và bảo dưỡng gắn với các hoạt động đang thực hiện hoặc với các thiết bị được phân tích. Các loại chi phí khác nhau hình thành chi phí vận hành và bảo dưỡng bao gồm

## Slide 9: IDENTIFY THE BENEFITS (INFLOWS) OF THE EE PROJECT
Energy and material savings
Savings through repairs and maintenance
Increased revenue due to improved product grade and quality
Tax credits and incentives from the government/power companies
Value of recovered equipment when decommissioned
Improved worker safety (thanks to reducing uncounted tasks and insurance costs)
Enhanced reliability
Reduced environmental protection costs
Improved product quality
Improved capacity utilization

## Slide 10: EVALUATING THE EFFECTIVENESS OF ENERGY-SAVING SOLUTIONS
Main components of the energy-saving project investment
Initial investment
Annual revenue (energy savings)
Annual costs (operating costs, fuel, etc.)
Project depreciation
Debt repayment (principal and interest in case of borrowing)
Income tax
...
Project cash flow
Cash Flow Before Tax – CFBT: Cash flow does not include corporate income tax;
CFBT is the basis for calculating CFAT (Cash Flow After Tax) for projects subject to corporate income tax

## Slide 11: TYPES OF CASH FLOWS
One-time
Annually
Others
Cash inflows
Residual value of the equipment
Operating revenue & savings
Working capital
Cash outflows
Initial investment cost
Operating costs & taxes
Working capital

## Slide 12: COSTS AND SAVINGS
Initial investment costs
Investment in new lighting systems, motor speed controllers
Investment in pipeline modifications and steam system insulation
Annual operating costs (and savings)
Operating inputs — materials, energy, and labor
Consumption — fuel, fuel additives, labor, ash disposal
Wastewater treatment — chemicals, electricity, labor, sludge
Working capital
Inventory
Accounts receivable/payable, cash

## Slide 13: VALUE OVER TIME OF CASH FLOWS - EQUIVALENT VALUE
Single interest matching
K0 => K0 + K0 * i * n in which: K0 : Initial capital (capital at the time of 0) i : Interest Rate (%) n : Number of interest compounding periods
Compound interest
K0 => K0 (1+i )n in which: K0 : Initial capital (capital at the time of 0) i : Interest Rate (%) n : the number of interest compounding periods

## Slide 14: DISCOUNT RATE AND COST OF CAPITAL
The discount rate is usually denoted as "r or i". Cost of capital = source of capital x interest rate. The company's general capital cost is calculated based on the company's borrowing capital cost and the company's own capital cost (the profit rate obtained if the company invests outside). When the capital source is only derived from bank loans, the total cost of capital will be equal to the bank loan interest. Depending on the structure of the fund, the combination formula can have more than two components:

## Slide 15: EFFECTS OF INFLATION
The concept of inflation: the degree of decline in the value of the currency We can prove it (1+R) = (1+r)* (1+ilf) r: nominal interest rate/discount rate; ILF: inflation rate; R: real discount rate or R = r +ilf +r*ilf approximate we have R = r + ilf
Coin
Increase Value due to investment
Decrease in value due to inflation

## Slide 16: CURRENT VALUE OF CASH FLOW
Current Value = Other Reciprocal Value x (PV Coefficient)
Annual cash flow value n
Cash flow value at "Time 0," is at the start of the project
The current value factor (PV) depends on the discount rate i With different values of i (discount rate): 10%, 15%, 20% With n years (number of years) Available Tables Formula (PV = ) Excel (function PV(rate,nper,pmt,fv,type))

## Slide 17: SOME VALUE CONVERSION FORMULAS
Know
Find
Factor
Formula

## Slide 18: FINANCIAL INDICATORS USED TO EVALUATE EE PROJECTS
1
SPP
Time required to recover investment capital from cash flow Quantitative method is widely used to evaluate the cost effectiveness of energy-saving investments Do not consider savings after the payback year and do not take into account the time-based value of the simple payback = Annual Net Savings/ capital cost of the project
4
IRR
The discount rate at which the net present value of the cumulative benefits of an investment equals the cost of the investment. The higher the IRR, the more efficient the project.
2
ROI
Describe the “annual benefit” from the project as a percentage of the cost of capital
Does not require projects to have the same life or compare costs
ROI = cost of capital/annual cash flow
5
0&M
The operating energy cost (i.e. the electricity cost for the equipment, e.g. a pump or a 10kW fan)/year will be higher than the initial investment cost of the equipment.
3
NPV
All Net benefits are amortized at the lowest attractive rate of return to determine equivalent present values.
6
LCC
For example, consider comparing traditional fluorescent lamps, spotlights, to replace with CFL or LED.
CFLs last 5 times longer than halogen lamps and LEDs last at least 20 times longer than halogen lamps => the calculation will take into account the life cycle to compare the original equipment and the replacement

## Slide 19: RATED BY NPV AND IRR
NPV
B t : Profit benefit annually​​​
C t : Cost annually​​​
i : Ratio rate extract discount
C t
B t
1
2
n
IRR
NPV= 0  IRR value
IRR (Internal Rate of Return): is the appropriate discount rate at which NPV = 0

## Slide 20: EVALUATION OF EE PROJECTS BASED ON NPV
NPV > 0: the larger the NPV of the project, the higher the financial efficiency of the project.
NPV ≤ 0: the project is not financially efficient
The selected option is the option with the largest NPV and NPV >0
Projects have equal lifespans
Direct comparison of NPV values ​​of projects
Projects have different lifespans.
  - Find the least common multiple of the project lives
  - Iterate through the projects to the life equal to the least common multiple
  - Compare the projects with the new lives
  - Note: can compare pairs of projects

## Slide 21: EVALUATION OF EE PROJECTS BASED ON IRR
IRR : Rate collect profit internal in
With i1 we have NPV1; NPV1 >0
With i2 we have NPV; NPV2 <0
We have :
Project with IRR > i* is feasible
The project with the largest IRR is the optimal project
IRR
NPV
i
NPV1
NPV2

## Slide 22: EVALUATION OF EE PROJECTS BASED ON IRR
IRR ≥ MARR - the larger the IRR of the project, the higher the financial efficiency of the project.
IRR < MARR - the project is not financially efficient.
The selected option is the option with the largest IRR ≥ MARR
MARR: Minimum Acceptable Rate of Return
Projects with equal lifespans
Directly compare the IRR values ​​of the projects
Projects with different lifespans
Compare each pair of projects
Subtract the project with small investment from the project with large investment
If the new project has an IRR larger than MARR, the project with large investment is better, otherwise the project with small investment is better

## Slide 23: FINANCIAL INDICATORS USED TO EVALUATE EE PROJECTS
Target | Definitio | Advantages | Disvantages | Suggested Application
NPV (Net Present Value | NPV is the net present value, which measures the difference between the total present value of cash inflows and cash outflows over the life of a project, after discounting at an appropriate rate. | Full consideration of cash flows throughout the project life. - Reflects the time value of money. - Easy comparison between different projects | It is necessary to choose an appropriate discount rate, otherwise it may lead to incorrect results. - Cannot be applied to projects with too long or uncertain time and cash flows. | - Used in long-term projects, when cash flows can be forecasted and an appropriate discount rate can be determined.
IRR (Internal Rate of Return) | IRR is the internal rate of return, which is the discount rate that makes the net present value (NPV) of a project equal to 0. It reflects the profitability of the project. | Easy to understand, easy to use. - Shows the project's profit rate, helping to evaluate the project's attractiveness. - Suitable for investors requiring high profit rates. | Cannot be applied if there are many inconsistent cash inflows and outflows. - IRR can have multiple values ​​in some special situations (uneven cash flows). | Used to compare investment projects of different sizes and durations. - Suitable for investors interested in profitability.
(Payback Period) | Payback period is the amount of time required to recover the initial investment from the cash flows generated during the project. | Easy to understand and calculate. - Reflects the ability to recover capital quickly. - Simple and cost-effective analysis. | Does not take into account the time value of money. - Does not fully reflect long-term financial feasibility - Does not measure profits after the payback period. | Suitable for short-term projects or when quick decisions are needed. - Used when wanting to evaluate the liquidity of a project.
(LCC - Life Cycle Costing) | LCC is a method of calculating the total cost of a project throughout its life cycle, from design, construction, operation to maintenance and disposal. | Calculates total costs over the life of the project. Useful in making long-term cost decisions - Can identify hidden costs that are not visible at the outset. | - Complex and requires a lot of long-term forecasting data. - Can be difficult to determine exact future costs. | Used in projects requiring long-term sustainability, such as infrastructure, manufacturing plants. - Suitable for long-term maintenance and operation decisions.

## Slide 24: FINANCIAL INDICATORS USED TO EVALUATE EE PROJECTS
NPV is the most powerful financial analysis indicator because it fully considers the project's cash flows and reflects the time value of money, helping to make a more accurate decision on the feasibility of the project. However, it requires choosing the appropriate discount rate.
IRR is useful in measuring the profitability of a project, especially when comparing projects with different rates of return. However, it can be problematic when cash flows are unstable or inconsistent.
Payback period is simple and easy to use, especially in short-term projects or when quick decisions are needed. However, it does not take into account the time value of money and does not fully reflect long-term profitability.
Life cycle analysis (LCC) is a good method to evaluate the overall cost over the life of a project, which is useful in projects that require long-term sustainability, but requires a lot of forecast data and can be complicated in determining future costs.
Depending on the goals and characteristics of each project, these indicators can be used independently or in combination to make optimal financial decisions.

## Slide 25: ADVANTAGES OF NPV AND IRR OVER OTHER METHODS
Takes into account the time value of money
Takes into account all cash flows over the life of the project
IRR is more popular with development financers and those who are more familiar with the rate of return
A project is acceptable if the IRR is higher than the cost of money used to finance the project, so the investor's desired rate cannot be arbitrary

## Slide 26: WHICH METHOD TO USE?
An investor who wants his money to pay back in a short period of time will use the discounted payback period. When there is no loan, NPV and IRR are preferred. A bank that lends and has several investment options will want to use the NPV and IRR methods to compare returns with other investment options For small projects, the calculation of the payback time may be sufficient, but for large projects that require external loans, then it is necessary to calculate NPV and IRR When you don't have enough information at hand, a simple payback period will often be used Some investors want a high intrinsic return on investment instead of immediate return on investment IRR cannot be used if the project has more than 1 year of negative net cash flow or a project with a lot of negative cash flow. In this case, use NPV

## Slide 27: SENSITIVITY ANALYSIS
 | Thv | NPV | IRR
Base case scenario |  |  | 
Project cost increases (+10%) |  |  | 
Bank interest rate increases (+20%) |  |  | 
Exchange rate changes (-20%) |  |  | 
Energy savings decrease (-20%) |  |  | 

## Slide 28: LIFE CYCLE COSTS
Currently, in the analysis and evaluation of energy saving projects, people use the Life Cycle Cost Analysis (LCC) method for evaluation.
Life cycle cost of a product
LCC = Purchase cost + Operation and maintenance cost + Spare parts cost + Electricity cost
In case of taking into account the time value of money flow:
LCC = Initial investment cost + Present value of future costs.
In which: C0: Initial investment cost
Ct: Cost incurred during the use of equipment in year t
n: Equipment life
i: Discount factor

## Slide 29: EXAMPLE LCC CALCULATION
Calculate the life cycle cost and compare the alternative of replacing a 15W LED lamp with a 100W incandescent lamp. The parameters of the alternative are given in the table below.
LED lamps have a lifespan of 20,000 hours, each year they are lit for 4,000 hours, so the lamp can be used for 5 years. Incandescent lamps only have a lifespan of 1,000 hours, so in 1 year the bulb must be replaced 4 times. During the lifetime of the LED lamp, 20 incandescent bulbs must be used.

## Slide 30: EXAMPLE LCC CALCULATION
Electricity power and cost​ money electricity belong to each type lamp row year :
Initial cost and annual electricity cost of 2 types of lamps:
With discount factor i = 10%, the life cycle cost for the first year when comparing 2 types of lamps is:
 | Incandescent bulb | Led bulb
Electricity power consumption (kWh) | 0.1*4000 = 400 | 0.015*4000 = 60
Electricity bill ( VND ) | 800000 | 120000
Year | 0 | 1 | 2 | 3 | 4 | 5
Incandescent bulb | 9000 | 836000 | 836000 | 836000 | 836000 | 836000
LED bulb | 9000 | 120000 | 120000 | 120000 | 120000 | 120000
Year | 0 | 1 | 2 | 3 | 4 | 5 | LLC
Discount Rate | 1.0000 | 0.9091 | 0.8264 | 0.7513 | 0.6830 | 0.6209 | 
Incandescent bulb | 9000.0 | 760000.0 | 690909.1 | 628099.2 | 570999.2 | 519090.2 | 3,178,098.0
LED bulb | 90000.0 | 109090.9 | 99173.6 | 90157.8 | 81961.6 | 74510.6 | 544,894.4

## Slide 31: ESTIMATION OF COSTS AND BENEFITS OF EE PROJECT
Depreciation:
  Is the systematic valuation and allocation of the value of assets that are depreciated over a period of use. Used to calculate corporate income tax deductions in the early years of a project.
Straight-line depreciation or straight-line depreciation is the most commonly used today.
  Annual depreciation: Dt = D = (P0 -Prm )/ Tdp
    In there :
    P0 : Initial value (original price) of fixed assets;
    Prm : Remaining value of fixed assets at the end of the depreciation period
    T dp : Depreciation period ​
  Simple, but slow to recover investment

## Slide 32: EXAMPLE OF STRAIGHT LINE DEPRECIATION
P0 = 100; Prm = 10; Tdp : 5 years
Years
P0
Prm
Tdp

## Slide 33: METHOD OF REPAYMENT OF PRINCIPAL AND INTEREST
Loan and payment method
Where to get capital to implement the project
Loan or equity?
Loan?
  How much?
  For how long?
  Guaranteed?
  Term?
  Interest rate?
  Payment method?
Payment method?
Annual payment includes: Principal and interest payment
Annual principal repayment, annual interest payment calculated on loan capital
Repay principal at the end of the loan term, pay interest annually
Repay principal and interest annually
Repay principal and interest at the end of the loan term
Investment project capital
Equity
Loan capital
principal repayment
interest payment
interest period

## Slide 34: PRINCIPAL AND INTEREST REPAYMENT METHODS
Annual principal repayment
Principal repayment = Loan/number of years
Interest repayment = interest rate × outstanding principal at the beginning of the year
Years
Interest
Annual
Origin
Debt
Years
Interest
Annual
Origin

## Slide 35: PRINCIPAL AND INTEREST REPAYMENT METHODS
Annual installment
Annual payment A = Loan  ( A/P,i,n)
Interest payment = interest rate  outstanding principal at the beginning of the year
Principal payment = annual payment - interest payment
Principal and interest paid in final year
Debt
Years
Interest
Annual
Origin
Years
Interest
Annual
Origin
Debt

## Slide 36: CORPORATE INCOME TAX
Annual corporate income tax
TN = L  T n
in there:
L : Income bear tax
Tn : Tax rate
Depreciation and interest are deductible and not included in corporate income tax.

## Slide 37: FINANCIAL CASH FLOW OF EE INVESTMENT PROJECT IN CASE OF NON-LOAN
Determine project cash flow
Calculate efficiency indicators
  NPV
  IRR
    Cash flow after tax:
    CFAT = CFBT - IT
    CFAT = CFBT- (CFBT- Dt ) x tr = CFBT (1-tr ) + D x tr
    Profit after tax (NI – Net Income):
    NI = TI -IT= TI x (1-tr )
    = (CFBT - D ) x (1-tr ) =CFBT (1-tr ) + D x tr - D
    = CFAT - D
Compare projects based on NPV and IRR indicators
    Cash flow before tax (CFBT): CFBTt = Bt – Ct
    Bt: project profit stream
    Ct: project cost stream
    Taxable income (TI – Taxable Income): TI = CFBT – D
    D: Depreciation
    Income tax (IT – Income Tax): IT = tr x TI
    tr: tax rate

## Slide 38: FINANCIAL FLOW OF EE INVESTMENT PROJECT IN CASE OF LOAN
Capital head fixed assets : 500
Current money before tax
Tax rate Tr : 20 %
Deduction loss even in 5 years

## Slide 39: Financial cash flow of investment project of renewable energy in case of borrowing capital
  Borrowing affects project CFAT cash flow
  NPV CSH increases
  IRR CSH increases
  In case of borrowing, two actors have income from the project: creditors and owners
Parameters as in the example above
Borrow 200. Pay principal evenly over 5 years, interest rate 10%
Project CFBT = Shareholder CFBT = Bt - Ct
Debt CFBT in year 0: Loan Capital
Debt CFBT = - (Principal Payment + Interest Payment)
TI = CFBT - Depreciation - Interest Payment
IT = TI × Tax Rate
Shareholder CFAT = Shareholder CFBT –
Principal Payment - Interest Payment - IT

## Slide 40: Some issues when evaluating EE projects
One number problem subject about school fit get a loan capital
When​ get a loan good than Are not get a loan ?
Have right get a loan more much more good or not​
Where to be interest rate threshold to decide determine Have should borrow or not ?
Fight price risk round real presently attend sentence effect fruit power quantity
The costs​ head private increase
Expense​ power wage increase / decrease
Image enjoy belong to abuse release next attend sentence
Image enjoy belong to attend sentence next product export and next the set part link mandarin other...

## Slide 41: QUIZZ
The purpose of depreciation of project fixed assets (TS) is to…
A) reflects the depreciation of the asset B) knows the residual value of the asset
C) shows the useful life of the asset D) supports non-taxation of the amount invested in the asset
2. How many times can a project's cumulative cash flows change sign during the project's life?
A) no time B) one time C) many times D) No
3. If a project has an IRR less than the loan interest rate then:
A) should not borrow capital B) should not invest
C) IRR csh = IRR project D) none of the answers are correct
4. Choose the correct formula in the following sentences:
A) CFAT =CFBT*(1-Tr) + NI B) CFAT =CFBT*(1-Tr) + D*Tr
C) CFAT =CFBT+ NI D) CFAT =CFBT*(1-Tr) + D

## Slide 42
THANK YOU